## Slide 1: Thoughts on the E(U)RICA DAQ
Hidetada Baba
RIKEN

## Slide 2: Outline
Time-stamp based Event Building
Introduction to time-stamping hardware
Proposing = On-demand TSEB system
Tasks

## Slide 3: Beta decay experiment (2009)
Beam line detector
  Beam line DAQ
  Beam trigger
Si detector
  Si DAQ
  Si trigger
  = Beam OR Beta
Ge detector
  Ge DAQ
  Si and Ge trigger
  = (Beam OR Beta) AND Gamma
Implanted Beam
Delayed beta
Prompt gamma
Isomer gamma
Delayed gamma
Strip Si
Beam line
Beam event
time
Prompt
Isomer
Beta event
Beta

## Slide 4: Time Stamp, individual trigger, individual DAQ
Beam Trigger DAQ
Gamma Trigger DAQ
48bits, 100MHz
Beta Trigger DAQ
2008～

## Slide 5: Dead time with Time stamp
DAQ A
DAQ B
DAQ C
Event if the common trigger,
the dead time of the system is not straight forward.
Dead time

## Slide 6: Live time @ Beta decay experiment
Title | Trigger | Rate(cps) | Live Time(%)
Beam DAQ | Beam | 101 | 97.9
Si DAQ | Si | 456 | 95.3
Ge DAQ | Si x Gamma | 434 | 81.3
Beta Decay | Si x not-Beam | 368 | 95.3
Prompt Gamma | Beam x Si x Gamma | 54 | 89.0
Isomer Gamma | Beam x Si x Gamma | 21 | 89.4
Beta-delayed Gamma | not-Beam x Si x Gamma | 172 | 88.9
Live time =
N of built events based on DT monitor
N of built events by acquired data
Trigger for DAQ A
Trigger for DAQ B
Trigger for DAQ C
Trigger for DAQ D
Dead time free
Time stamper

## Slide 7: GANIL Time Stamp v.s. RIKEN Time Stamp
Master module counts the clock (= time-stamp)
Slave modules ask the time stamp for the Master
Very safe system
Not easy to combine with other system
  Should accept external clock
GANIL case
100 MHz
48 bits

## Slide 8: GANIL Time Stamp v.s. RIKEN Time Stamp
Distribute bare clock and the reset pulse
Each module counts the clock (= time-stamp)
A little bit dangerous system (Should have a monitor)
Easy to combine with other system
RIKEN case
100 MHz
48 bits
Clock
Source
Clock
Clear
Clock
Clear
Reset
Pulse

## Slide 9: On-demand Time-Stamp based Event Building System Over the Internet
Any DAQ systems are welcome
Can reduce the effort for user-support
Client
Beam
DAQ
Raw+TS data
Si
DAQ
Raw+TS
data
E(U)RICA
DAQ
Raw+TS
data
On-demand
server
On-demand
server
On-demand
EB server
TS DB
Put request
Request = “Beam AND E(U)RICA”,
2012 May 3. 19:00-21:00,
window = +- 100ns”
PID+TS
data
Beam
+
E(U)RICA
Beam
E(U)RICA
Req
Return
combined data
68Ni

## Slide 10: Analysis scheme
Raw+TS data
Raw+TS
data
Raw+TS
data
Beam
  TS
  Z, A
EURICA
  TS
  E, T
  Pos
Si
  TS
  E, T
  Pos
Pre Analysis
Analysis Server
Analysis Server
On-demand
EB Server
ASCII
RIKEN Inside
On your laptop
ROOT
Put requests
via Web-Browser
Down load
combined data

## Slide 11: Maximize physics outputs
Gamma DAQ
Neutron DAQ
Si DAQ
TPC DAQ
SHARAQ DAQ
Mass Ring DAQ
Separate DAQ +Non-biased Trigger
Extract Physics Events after measurements
Beam DAQ
Maximize physics outputs
Beta decay DAQ

## Slide 12: Tasks
a.s.a.p
  Check of the TS connectivity
  Hardware development is required or not?
Very few DAQ software development
  RUN start/stop, handling TS values
New TSEB system
  Will be available (by Mar. 2012)
  Only for the event compilation
Please discuss about analysis frame work
  may be next year?