## Slide 1
Applying γ-imaging techniques to nuclear physics experiments
Hans-Jürgen Wollersheim
Why position sensitive γ-ray detectors for radioactive ion beams?
3D position sensitive HPGe detectors
Characterization of position sensitive HPGe detectors

## Slide 2
Challenges of γ-ray spectroscopy
efficiency vs resolution
Composite HPGe detectors
in ADD BACK mode
Emission at rest
ΔE=2keV
g ray
Channel No.
Counts(arb. units)

## Slide 3
Challenges of γ-ray spectroscopy
efficiency vs resolution
High Mγ
Doppler broadening
Emission in flight
v
Solution
Δө
- Segmentation
- Gamma-ray tracking
- Pulse shape analysis
- Doppler correction
Channel No.
Counts(arb. units)
ө

## Slide 4
γ-ray spectroscopy with 3D position sensitive HPGe detectors
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation
HISPEC
DESPEC
Efficiency: 43% (M =1) 28% (M =30)
P/T: 58% (M=1) 49% (M=30)
Angular resolution: ~1º
FWHM (1 MeV, v/c=50%) ~ 6 keV
Advanced GAmma Tracking Array

## Slide 5
γ-ray spectroscopy with 3D position sensitive HPGe detectors
Δ
β = 0.5

Via tracking it becomes possible to determine the incident angle and preserve the good energy resolution.
Energy
Counts
PSA = 5 keV
Segment = 12 keV
Detector = 35 keV
Eγ = 1.3 MeV
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation

## Slide 6
γ-ray spectroscopy with 3D position sensitive HPGe detectors
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation

Background suppression and P/T can be improved by applying imaging techniques.
S. Tashenov, et al. NIMA 586 (2008) 224-228

## Slide 7
HPGe detector
9 cm
7 cm

## Slide 8
Gamma Arrays based on Compton Suppressed Spectrometers
Tracking Arrays based on
Position Sensitive Ge Detectors
ε ~ 50 - 25 %
( Mγ = 1 - Mγ = 30)
ε ~ 10 - 7 %
( Mγ = 1 – Mγ = 30)
GAMMASPHERE
EUROBALL
GRETA
AGATA

## Slide 9
HPGe detector: working principle

## Slide 10
HPGe detector: working principle

## Slide 11
HPGe detector: working principle

## Slide 12
HPGe detector: working principle

## Slide 13
HPGe detector: working principle

## Slide 14
HPGe detector: position sensitivity

## Slide 15
HPGe detector: position sensitivity

## Slide 16
Highly segmented
HPGe detectors
AGATA:
Advanced Gamma Tracking Array
Digital electronics
to record and process segment signals
Pulse Shape Analysis to identify the interaction position coordinates
(x,y,z,E)i
Reconstruction of tracks
e.g. by evaluation of permutations
of interaction points
reconstructed γ-rays
Ingredients of γ-ray tracking

## Slide 17
Comparison provides the position
Pulse Shape Analysis to identify the interaction position coordinates
(x,y,z,E)i
Traces from a data base for known positions (x,y,z)
Ingredients of γ-ray tracking

## Slide 18
Method to characterize the pulse shape of HPGe detectors
Determine a data-base of pulse shapes S(x,y,z) which allows one to correlate an arbitrarily measured pulse, with an interaction position inside the detector.
How to do this?
Using PET principle in combination with g-ray imaging techniques !
?

## Slide 19
Large FoV of about 20 cm diam.
Low Spatial Resolution 5mm-1cm
Small FoV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FoV = 8x9 cm2
www.siemens.de
Gem-imaging.com
Which γ-camera to use?

## Slide 20
Method to characterize the pulse shape of HPGe detectors
22Na
HPGe-Detector
2D γ-camera
511 keV
511 keV
PET approach using a high performance γ-camera
Data group “A)” Data group “B)”
Features:
Estimated time 20h
Precision: 1-2 mm
Imaging
Requirements:
Excellent resolution Dx/x
Large field of view FoV
c2(Ai,Bi)

## Slide 21
Method to characterize the pulse shape of HPGe detectors
22Na
HPGe-Detector
2D γ-camara
511 keV
511 keV
PET approach using a high performance γ-camera
Data group “A)” Data group “B)”
Features:
Estimated time 20h
Precision: 1-2 mm
Imaging
Requirements:
Excellent resolution Dx/x
Large field of view FoV
c2(Ai,Bi)

## Slide 22
Large FoV of about 20 cm diam.
Low Spatial Resolution 5mm-1cm
Small FoV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FoV = 8x9 cm2
www.siemens.de
Gem-imaging.com
Which γ-camera to use?

## Slide 23
Small FOV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Gem-imaging.com
Which γ-camera to use?
Scintillator
Position Sensitive
PMT

## Slide 24
Small FOV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Gem-imaging.com
Which γ-camera to use?
Scintillator
Position Sensitive
PMT
g-ray

## Slide 25
Small FOV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Gem-imaging.com
Which γ-camera to use?
Scintillator
Position Sensitive
PMT
g-ray

## Slide 26
Small FOV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Gem-imaging.com
Which γ-camera to use?
Scintillator
Position Sensitive
PMT
g-ray

## Slide 27
Small FOV of about 3-4 cm diam.
Higher Spatial Resolution 2-3mm
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Gem-imaging.com
Which γ-camera to use?
Scintillator
Position Sensitive
PMT
g-ray
g-ray 2

## Slide 28
16 wires in X axis and 16 wires in Y axis
Hamamatsu R2486 PSPMT
Photocathode = 56.25 mm
d = 76 mm
t = 3 mm
ρ = 7.4 g/cm3
LYSO scintillator
Cerium-doped Lutetium Yttrium Orthosilicate
C.Domingo Pardo, N. Goel, et.al., IEEE, Vol.28, Dec. 2009
Gamma camera: Individual multi-anode readout

## Slide 29
Position reconstruction
Collimated Na-22 source placed at different positions

## Slide 30
Position calibration
Determine: Xr(xm,ym), Yr(xm,ym)
Gamma-ray scattering technique
Grid raw image when it is parallel to PSD surface (0 deg)
00 position

## Slide 31
Position reconstruction
LYSO =76 mm
Photocathode=56.26 mm
Central Interaction
Peripheral Interaction
C. Domingo Pardo, N.Goel, et.al., IEEE, Dec. 2009 Volume: 28 Issue 12
average charge profile at the center
Reference peak fitting
Charge (a.u.)
Charge (a.u.)
Y (mm)
Y (mm)
C.W.Lerche, et.al., NIM A, Vol 537, pp. 326-330, Jan. 2005

## Slide 32
Position reconstruction
Gaussian fitting
Reference peak fitting
Linear for 50 mm
Field of view = 28 cm2
Pos. X (mm)
Gaussian fitting works relatively well in the central region
Average spatial resolution in X and Y ~ 1mm
Pos. X (mm)

## Slide 33
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Method to characterize the pulse shape of HPGe detectors

## Slide 34
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Method to characterize the pulse shape of HPGe detectors

## Slide 35
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Method to characterize the pulse shape of HPGe detectors

## Slide 36
Requirements:
Excellent resolution Δx = 2 mm
Large field of view FOV = 8x9 cm2
Method to characterize the pulse shape of HPGe detectors

## Slide 37
Characteristics:
Faster
Precision: 1-2 mm
Imaging capability
Requirements:
1. Position sensitive detector
- Excellent Δx/x
- Large field of view
2. Method to compare the pulses
Rotating table
Position sensitive detector
22Na
Scanner at GSI

## Slide 38
Advantage over conventional scanner: Full detector can be scanned in one measurement 10 times faster than a conventional scanner Accuracy of simulations can be checked for complex regions of electric field
Superiority over conventional scanner
BGO
BGO
coincidence between the Germanium and BGO detectors for 90 degree Compton scattered events for depth determination
137Cs

## Slide 39
a)
F.C.L. Crespi, et al. NIM A 593 (2008), 440
Scanner based on pulse shape comparison scan
a)

## Slide 40
a)
b)
b)
Geometric crossing point: x,y,z
Common pulse out of data sets (a) & (b)
a)
Collimated source
Scanner based on pulse shape comparison scan
F.C.L. Crespi, et al. NIM A 593 (2008), 440

## Slide 41
22Na
Position sensitive
detector
a)
b)
Rotated by 900
Recording pulse shapes for positions (a) and (b)
Identical signals at the crossing point.
511 keV
22Na
Pulse shape comparison scan method based on
a position sensitive detector

## Slide 42
χ2 minimization method
0° measurement
t(ns)
t(ns)
amplitude, Φ
distribution
t(ns)
amplitude, Φ
Average pulse
amplitude, Φ
threshold
90° measurement

## Slide 43
Characterisation of a planar HPGe detector
Front view
Side view
Planar Ge
d = 4 cm
t = 2 cm
22Na
Position sensitive detector

## Slide 44
Detector scan (test measurements)
Front view (0 deg):
Side view (90 deg):

## Slide 45
Detector scan (test measurements)
Front view (0 deg):
Side view (90 deg):

## Slide 46
Detector scan (data analysis)

## Slide 47
Experimental validation of the method

## Slide 48
AGATA: Advanced Gamma Tracking Array
4π array of germanium crystals
180 segmented crystals arranged around the reaction target
3D sensitivity
Symmetric AGATA prototype crystal

## Slide 49
Signal shapes from all 36 segments
Photopeak event
Most significant transient charge signals are from the direct neighbouring segments

## Slide 50
left
right
top F5
bottom F3
F4
E4
A4
Azimuthal position

## Slide 51
F4
E4
A4
Azimuthal position
left
right
top F5
bottom F3

## Slide 52
F4
E4
A4
Azimuthal position
left
right
top F5
bottom F3

## Slide 53
F4
E4
A4
Azimuthal position
left
right
top F5
bottom F3

## Slide 54
F4
E4
A4
Azimuthal position
left
right
top F5
bottom F3

## Slide 55
We have the method, the device and the detector ready, lets do the scan of AGATA!
Direct neighbours of segment F3
Combined trace for pulse shape comparison

## Slide 57
2D projected images for 511 keV coincident photopeak events in position sensitive detector and AGATA
Intensity distribution

## Slide 58
Experimental
Simulated
t(ns)
Electric field
Multi Geometry Simulation
t(ns)
V/cm
+
-
Risetime distribution plots

## Slide 59
Intensity distribution for segments in row F
Segment F3
Segment F2
Segment F1
Geometric
segmentation
MGS Segmentation
radius (mm)
Effective segmentation

## Slide 60
Experimental
Simulated
Discrepancy in the T90 values near the core in ring 1 ~ 50 ns
Extremely important to have an experimental pulse shape basis for PSA to be applied to the complicated geometries.
t(ns)
t(ns)
From 2D to 3D: first deep insight into the detector

## Slide 61
Summary & outlook
We have developed a g-camera with spatial resolution, linearity and field of view substantially improved with respect to similar existing devices (3 times larger FOV, 2 times better resolution).
These improvements in the detection system allow us to characterize the pulse shape of HPGe detectors with an spatial matrix resolution of about 2 mm and in a short period of time (about 2 days per crystal of 9x7 cm2 size compared to 3 months needed by other approaches).
The good performance of this new detection system makes it very suitable for many g-ray imaging applications, not only in RIB experiments but also e.g. for medical physics
Our system uses conventional NIM and VME electronics, which makes it not easily portable, not easily scalable and rather expensive if one wants to build many of these devices. However, this drawback could be overcome thanks to the increasing technology of electronics, e.g. a new acquisition system based on ASIC, FPGA, etc technologies. This would also make the system more suitable for medical applications.
Applications with thicker scintillation crystals (1 cm) may become possible, without compromising its good performance, thanks to the more accurate measurement of the DOI. (Tests are in progress).

## Slide 62
Summary & outlook
Our system uses conventional NIM and VME electronics, which makes it not easily portable, not easily scalable and rather expensive if one wants to build many of these devices. However, this drawback could be overcome thanks to the increasing technology of electronics, e.g. a new acquisition system based on ASIC, FPGA, etc technologies. This would also make the system more suitable for medical applications.
Applications with thicker scintillation crystals (1 cm) may become possible, without compromising its good performance, thanks to the more accurate measurement of the DOI. (Tests are in progress).

## Slide 63
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
Conclusion and summary

## Slide 64
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
4.Development of a gamma camera to achieve superior
position resolution of 1 mm
Conclusion and summary

## Slide 65
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
4.Development of a gamma camera to achieve superior
position resolution
5.Succesful test with a planar HPGe crystal
Conclusion and summary

## Slide 66
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
4.Development of a gamma camera to achieve superior
position resolution
5.Succesful test with a planar HPGe crystal
6.Spatial characterisation of an AGATA detector
Conclusion and summary

## Slide 67
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
4.Development of a gamma camera to achieve superior
position resolution
5.Succesful test with a planar HPGe crystal
6.Spatial characterisation of an AGATA detector
7.Comparison with simulation
Conclusion and summary

## Slide 68
1.Next generation of segmented HPGe based gamma arrays
for inflight spectroscopy
2.Pulse shape analysis and gamma ray tracking
3.A novel scanner based on pulse shape comparison scan
4.Development of a gamma camera to achieve superior
position resolution
5.Succesful test with a planar HPGe crystal
6.Spatial characterisation of an AGATA detector
7.Comparison with simulation
8.Implement signal basis for PSA
Conclusion and summary

## Slide 69
Potential map
Electric field
Multi Geometry Simulation

## Slide 70
Planar Geometry
Coaxial Geometry
It is not sufficient to find the impurity charge concentration applying
only the assumption of cylindrical or planar geometry.
Extremely important to have an experimental pulse shape basis for PSA to be applied to the complicated geometries.
Impurity concentration from capacitance-voltage measurements
Necessity to scan detectors experimentally

## Slide 71
AGATA S001 Detector Scan
511 keV coincident events

## Slide 72
Position information from the polarity and amplitude of the image charges
12 mm
30 mm
Radius
90°
30°
Angle