## Slide 1: Experimental Storage Ring – ESR Emax = 420 MeV/u, 10 Tm

## Slide 2: Specification of the ESR
Fast Injection
e- cooler
I = 10...500 mA
Six 600 dipoles
Bρ ≤ 10 T· m
Schottky
pick-ups
Re-injection
to SIS
Extraction
L = 108 m =1/2 LSIS
p = 2· 10-11 mbar
E = 3...420 MeV/u
f ≈ 1...2 MHz
β = 0.08...0.73
Qh,v ≈ 2.65
Particle
detectors
Two 5 kV rf-cavities
Gas jet
│

## Slide 3: Bunch dimensions
Y
X
Z
σX
σY
σZ
For uniform charge distributions
we may use “hard edge values”
For Gaussian charge distributions
use rms values σx, σy, σz
We will discuss measurements of bunch size and charge distribution later

## Slide 4: But rms values can be misleading
Gaussian beam
Beam with halo
We need to measure the particle distribution!
σ
σ

## Slide 5: Coordinate space
orbit traces
Each of Nb particles is tracked in ordinary 3D-space
Not too helpful!

## Slide 6: Configuration space
6 Nb-dimensional space for Nb particles; coordinates (xi, pi), i = 1, …, Nb
The bunch is represented by a single point that moves in time
Useful for Hamiltonian dynamics

## Slide 7: Configuration space example: 1 particle in an harmonic potential
But for many problems this description carries much more information than needed:
We don’t care about each of 1010 individual particles
But seeing both x & px looks useful

## Slide 8: Phase space (gas space in statistical mechanics)
6-dimensional space for Nb particles
The ith particle has coordinates (xi, pi), i = x, y, z
The bunch is represented by Nb points that move in time
In most cases, the three planes are to very good approximation decoupled
One can study the particle evolution independently in each planes

## Slide 9: Particle Systems & Ensembles
The set of possible states for a system of N particles is referred as an ensemble in statistical mechanics.
In the statistical approach, particles lose their individuality.
Properties of the whole system are fully represented by particle density functions and :
where

## Slide 10: Longitudinal phase space
In most accelerators the phase space planes are only weakly coupled.
→ Treat the longitudinal plane independently from the transverse one
→ Effects of weak coupling can be treated as a perturbation of the uncoupled solution
In the longitudinal plane, electric fields accelerate the particles
→ Use energy as longitudinal variable together with its canonical conjugated time
Frequently, we use relative energy variation and relative time with respect to a reference particle
According to Liouville, in the presence of Hamiltonian forces, the area occupied by the beam in the longitudinal phase space is conserved

## Slide 11: Transverse phase space
For transverse planes and , use a modified phase space, where the momentum components are replaced by:
where s is in the direction of motion
We can relate the old and new variables (for )
where and
Note: xi and pi are canonical conjugate variables while x and x’ are not, unless there is no acceleration ( and constant)

## Slide 12: Emittance describes the area in phase space of the ensemble of beam particles

## Slide 13: Why is emittance an important concept
Liouville: Under conservative forces phase space evolves like an incompressible fluid
Under linear forces macroscopic (such as focusing magnets) & emittanceis an invariant of motion
Under acceleration is an adiabatic invariant
Is there any way to decrease the emittance?
This means taking away mean transverse momentum
but
keeping mean longitudinal momentum

## Slide 14: Beam cooling
Beam cooling: By analogy with kinetic theory of gases, where heat is equivalent to disorder, “cooling” here denotes the reduction of disorder in the beam.
Small emittance and momentum spread: reduce phase space volume.
Beam cooling processes are not following the Liouville’s Theorem:
“In a system where the particle motion is controlled by external conservative forces the
phase space density is conserved”
Cooling force: dissipative in nature.
phase space is used for representing particles
As a particle beam propagates along magnets and other beam-manipulating components of an accelerator, the position spread may change, but in a way that does not change the emittance.

## Slide 15: Specification of the ESR
Fast Injection
e- cooler
I = 10...500 mA
Six 600 dipoles
Bρ ≤ 10 T· m
Schottky
pick-ups
Re-injection
to SIS
Extraction
L = 108 m =1/2 LSIS
p = 2· 10-11 mbar
E = 3...420 MeV/u
f ≈ 1...2 MHz
β = 0.08...0.73
Qh,v ≈ 2.65
Particle
detectors
Two 5 kV rf-cavities
Gas jet
│

## Slide 16: What is beam cooling?
Beam cooling is synonymous for a reduction of beam temperature
Temperature is equivalent to terms as
phase space volume, emittance and momentum spread
Beam cooling processes are not following Liouville’s Theorem:
(which neglects interactions between beam particles)
“In a system where the particle motion is controlled by external
conservative forces the phase density is conserved”
Beam cooling techniques are non-Liouvillean processes
e.g. interaction of beam particles with other particles (electrons, photons)
Benefit of beam cooling:
● Improved beam quality (precision experiments, luminosity increase)

## Slide 17: Beam cooling at the ESR
Cooling methods:
Electron cooling
Stochastic cooling
Laser cooling
What is cooling? What is temperature?
=
=
v is the velocity relative to a reference particle, which moves with an average ion-velocity.
The temperature is a measure of the random movement.
In an accelerator
=
Why beam cooling?
Improve of the beam quality
smaller beam size and reduction of the emittance
broadening of the energy
better beam intensity, accumulation
lifetime of the beam
Makroskopische
Emittanz

## Slide 18: Beam temperature
Thermal particle motion (temperature is conserved)
at rest (source) low energy high energy
temperature
Where does the beam temperature originate from?
The beam particles are generated in a ‘hot’ source

## Slide 19: Benefits of beam cooling
Improve beam quality
  Precision experiments
  Luminosity increase
Compensation of heating
  Experiments with internal target
  Colliding beams
Intensity increase by accumulation
  Weak beams from source can be increased
  Secondary beams (antiprotons, rare isotopes)

## Slide 20: Electron cooling
electron collector
electron gun
high voltage platform
magnetic field
electron beam
ion beam
ve‖ = vion‖
Ee = me/Mion ·Eion
e.g.: 200 keV electrons
cool 400 MeV/u ions
electron temperature:
momentum transfer by Coulomb collisions
cooling force results from energy loss
in the co-moving gas of free electrons
in beam frame:
cold electrons interacting with hot ions
superposition of a cold
intense electron beam
with the same velocity
G.I. Budker, At. En. 22 (1967) 346
G.I. Budker, A.N. Skrinsky et al., IEEE NS-22 (1975) 2093
I: 5-500 mA
G. Budker
Notes: ions interact 106 s-1 with collinear beam of cold electrons

## Slide 21: Characteristics of electron cooling force
Analogy: energy loss in matter
(electrons in the shell)
cooling force F
for small relative velocity:
for large relative velocity:
increase with charge:
maximum cooling force at effective electron temperature
Notes: ions interact 106 s-1 with collinear beam of cold electrons

## Slide 22: Simple derivation of electron cooling force
Analogy: energy loss in matter
(electrons in the shell)
Rutherford scattering:
Energy transfer:
Minimum impact parameter:
Energy loss:
Coulomb logarithm
Notes: ions interact 106 s-1 with collinear beam of cold electrons

## Slide 23: Example of electron cooling
transverse cooling at ESR
measured with residual gas ionization beam profile monitor
cooling of 350 MeV/u Ar18+ ions 0.05 A, 192 keV electron beam ne = 0.8∙106 cm-3
Notes: ions interact 106 s-1 with collinear beam of cold electrons

## Slide 24: Electron cooling
momentum spread Δp/p = 10-5
diameter 2 mm
The ions get the sharp velocity of electrons,
small size and divergence
G.I. Budker, At. En. 22 (1967) 346
G.I. Budker, A.N. Skrinsky et al., IEEE NS-22 (1975) 2093

## Slide 25: Ionization cooling
Hot muon beam:
- large transverse momentum
- cannot fit in the beam pipe in muon accelerator
Ionization cooling:
Based on use of ionization energy loss of accelerated charged particles
Reduce the transfers motion and accelerate them in forward direction

## Slide 26: Stochastic cooling: Implementation at the ESR
Combiner-
Station
long. Pick-up
transv. Pick-up
long. Kicker
transv. Kicker
ESR storage ring
Stochastic cooling is in particular efficient for hot ion beams
Simon van der Meer

## Slide 27: Principle of ‘stochastic’ cooling
A Feedback System: A detector or pick-up which measures the motion of the particle and a corrector, the kicker, which adjusts their angles.
Measures the deviation of the center of gravity of a sample of particles with respect to the requisite orbit and sends an error signal to the kicker.
The kicker applies an electric field to the same sample to correct the deviation measured.

## Slide 28: Principle of ‘stochastic’ cooling
Self correction of ion trajectory
Using a pick-up probe, the position of the ion beam is measured at a fixed position via the induced signal. A deviation of the beam from the ideal orbit can be corrected by amplification of this signal.
The amplified signal is now used as a correction signal which acts on the beam at a second position (zero crossing of the betatron function) via a "kicker“.
This method was invented for the cooling of hot p(bar) by van der Meer. He showed that after a cooling time of   N/C (N: particle number, C = Bandwidth of the amplifier) a momentum width of the beam of about p/p 10-3 can be achieved by stochastic cooling.
Detection of the W boson from p ↔ p(bar)

## Slide 29: Stochastic cooling at GSI
electrodes installed inside magnets
combination of signals from electrodes
power amplifiers for generation of correction kicks
fast pre-cooling of hot fragment beams
energy 400 (-550) MeV/u
bandwidth 0.8 GHz (range 0.9-1.7 GHz)

## Slide 30: Comparison of Cooling Methods
 | Stochastic Cooling | Electron Cooling
Useful for: | low intensity beams hot (secondary) beams high charge full 3-D control | low energy all intensities warm beams (pre-cooled) high charge bunched beams
Limitations: /problems | high intensity beams beam quality limited bunched beams | space charge effects recombination losses high energy

## Slide 31: Principle of laser cooling (snowplow)
Absorption of photons from a laser beam: Energy and momentum must be conserved.
2. Absorption of photons:
Momentum transfer in a defined direction
(directed momentum transfer).
No defined direction for the spontaneous
emission (isotropic re-emission):
Momentum transfer cancels out over many
absorption-emission-cycles.
typical cooling times ~ 10 μs
only longitudinal cooling

## Slide 32: Principle of laser cooling 2-step process

## Slide 33: Laser cooling at ESR
Argon ion laser (257.3 nm)
frequency doubled
Fluorescence light detection

## Slide 34: Cooling
D. Boutin

## Slide 35: Cooling with the ESR

## Slide 36: Recording the Schottky-noise
____________________________ 128 msec
→ FFT
64 msec_____________________
→ FFT
Real time analyzer Sony-Tektronix 3066

## Slide 37
time
Schottky-Mass-Spectroscopy
4 particles with different m/q

## Slide 38: Schottky mass spectroscopy
Sin(w1)
Sin(w2)
Sin(w3)
Sin(w4)
w1
w2
w3
w4
time
Fast Fourier Transform

## Slide 39: Schottky mass spectroscopy Small-band Schottky frequency spectra