## Slide 1: Particle and Radiation Detectors: Advances & Applications
Lecture: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de

## Slide 2: Particle Interaction with Matter
Aurora Borealis
Ionization

## Slide 3: Particle Interaction with Matter
Cherenkov Light
Characteristic glow from a reactor
Cherenkov radiation is an effect similar to sonic booms when the plane exceeds the velocity of sound

## Slide 4: Particle Interaction with Matter
Bremsstrahlung
Bremsstrahlung or ‘braking radiation’
Spectrum of the X-rays emitted by an X-ray tube with a rhodium target, operated at 60 kV. The continuous curve is due to bremsstrahlung, and the spikes are characteristic K lines for rhodium.

## Slide 5: First Detectors – photographic plates
First X-ray image by Wilhelm Conrad Roentgen (1895)
Henri Bequerel’s first “picture” of Uranium (1896)

## Slide 6: Interaction of gamma rays with matter

## Slide 7: Energy loss – dE/dx
Particles interact differently with matter. Important for detectors is the energy loss per path length. The total energy loss per path length is the sum of all contributions.
Depending on the particle type, the particle energy and the material some processes dominate, other do not occur. For instance only charged particles will interact with electrons of atoms and produce ionization, etc.

## Slide 8: Measurement Principles
A measurement requires an interaction of the particle with the material of the detector. The interaction provokes two effects:
1st Creation of a detectable signal, e.g.
ionization → charges
excitation → scintillation
excitation of phonons → heat
2nd Alternation of the particles properties, e.g.
energy loss
change of trajectory due to scattering
absorption
unwanted side effects. They need to be as small as possible and well understood.

## Slide 9: Measurement Principles
A particle detector is an instrument to measure one or more properties of a particle …
Properties of a particle |  | Type of detection principle:
- position and direction |  | position and tracking
- momentum |  | tracking in a magnetic field
- energy |  | calorimetry
- mass |  | spectroscopy and PID
- velocity |  | Cherenkov radiation or time of flight
- transition radiation |  | TRD
- spin, lifetime |  | 
Properties of a particle |  | Type of detection principle:
- position and direction |  | position and tracking
- momentum |  | tracking in a magnetic field
- energy |  | calorimetry
- mass |  | spectroscopy and PID
- velocity |  | Cherenkov radiation or time of flight
- transition radiation |  | TRD
- spin, lifetime |  | 

## Slide 10: What is a Particle?
Strong force
Electromagnetic force
Weak force

## Slide 11: How do we see Particles?
A light bulb shines on a hand and the different reflections make the fine structure visible.
With a magnifying glass or microscope more details can be seen, but there is a fundamental limit:
The wavelength of the light (1/1000 mm) determines the size of the resolvable objects.
light bulb → accelerator
magnifying glass or microscope → detector
LW | 3000 m | 
MW | 300 m | 
KW | 30 m | 
UKW | 3 m | 
GPS | 0.3 m | 
Infrared | 10-6 m | 
light | 5·10-7 m | 2 eV
UV | 10-7 m | 10 eV
X-ray | 10-10 m | 104 eV
γ-ray | 10-12 m | 106 eV
→ electromagnetic waves
available wavelength

## Slide 12: Energy, Wavelength and Resolution
10-1m
10-9m
10-10m
10-14m
10-15m
wavelength versus resolution
all particles have wave properties:
Small objects (smaller than λ) do not disturb the wave → small object is not visible
Large objects disturb the wave → large object is visible
de Broglie wavelength
Louis de Broglie
h·c = 1239.84 [MeV fm]

## Slide 13: Detection and Identification of Particles
Detection = particle counting (is there a particle?)
Identification = measurement of mass and charge of the particle
(most elementary particle have )
How:
- charged particles are deflected by B fields such that:
- particle velocity measured with time-of-flight (ToF) method
ToF for known distance
Ionization
Cherenkov radiation
Transition radiation

## Slide 14: Detection and Identification of Particles
Detection = particle counting (is there a particle?)
Identification = measurement of mass and charge of the particle
(most elementary particle have )
How:
- kinetic energy determined via a calorimetric measurement
- for Z=1 the mass is extracted from and
- to determine Z (particle charge) a Z-sensitive variable is e.g. the ionization
energy loss
a = material-dependent constant

## Slide 15: Energetic charged particles in matter
Three types of electromagnetic interactions:
Ionization (of the atoms of the transversed material)
Emission of Cherenkov light
Emission of transition radiation
1) Interaction with the atomic electrons. The incoming particle looses energy and the atoms are excited or ionized.
2) Interaction with the atomic nucleus. The particle is deflected (scattered) causing multiple scattering of the particle in the material. During this scattering a Bremsstrahlung photon can be emitted.
3) In case the particle’s velocity is larger than the velocity of light in the medium, the resulting EM shockwave manifests itself as Cherenkov Radiation. When the particle crosses the boundary between two media, there is a probability of the order of 1% to produce an X-ray photon, called Transition Radiation.

## Slide 16: Energetic charged particles in matter
Charged particle identification with
segmented or stacked detectors
Si
Bethe-Bloch formula

## Slide 17: Energetic charged particles in matter
α-particles are highly ionized and lose their energy very fast by ionization and excitation
when passing through matter.
maximum energy transfer Tmax of a projectile with mass m
and velocity β on an electron me at rest
for all heavy primary particles except electrons and positrons
number of α-particles as a function of distance x
energy loss of α-particles
per distant unit
average range <R> of α-particles with 5 MeV
2,5cm in air, 2,3cm in Al, 4,3cm in tissue

## Slide 18: Energy loss and range of charged particles
-dE/dε is independent of the material for equal particles
the average range for particles with kin. energy T is obtained by integration
7.7 MeV α-particles in air:
range is not exact but there is range straggling,
the number of interactions is a statistical process.
energy loss
distance
5.5 MeV α´s in air
deuteron beam scintillating in air
Several empirical and semi-empirical formulae have been proposed to compute range of α-particles in air.
Scaling the range of other materials

## Slide 19: Interaction of charged particles in matter
Bethe-Bloch formula describes the energy loss of heavy particles passing through matter
= 0.3071 MeV g-1cm2
Specific energy loss rate
for muons, pions and protons in different materials
Dependence on mass A, charge Z of target nucleus
Minimum ionization: 1-2 MeV/g cm-2 [H2: 4 MeV/g cm-2]
Muon momentum (GeV/c)
Pion momentum (GeV/c)
Proton momentum (GeV/c)

## Slide 20: Energy loss of charged particles – dE/dx for different particles
for heavy particles in this momentum regime is well described by Bethe-Bloch formula, i.e. the dominant energy loss is collisions with atoms
for electrons does not follow Bethe-Bloch formula. The dominant process is Bremsstrahlung
[ALICE TPC, 2009]
momentum p (GeV/c)
TPC signal (a.u.)

## Slide 21: Energy loss for electrons and positrons
e± are exceptional cases due to their low mass. They will be deflected significantly in each collision.
In addition to the energy loss due to ionization, the energy loss due to Bremsstrahlung is of importance.
For high energies the energy loss due to Bremsstrahlung is given by
and
Other particles like muons also radiate,
especially at higher energies.

## Slide 22: Bremsstrahlung
fit to data:
X0 is the radiation length. It is the mean distance over which a high-energy electron loses all but 1/e of its energy by Bremsstrahlung
Usual definition for the critical energy Ec (electron)
example: Pb (Z=82, ρ = 11.34 [g/cm3] → Ec = 7.34 MeV

## Slide 23: Comparison between electrons (β-) and positrons (β+) on their way through matter
β+ particles behave similarly as β- particles; they are ionizing and attenuated on their way through matter.
But at the end of the their attenuation one observes a pair annihilation with an electron, which yields high energetic γ-emission. Positrons are hence more dangerous than electrons.
electron
source
positron
source
detector

## Slide 24: Cherenkov radiation
Cherenkov radiation is emitted if the particle velocity is larger than the velocity of light in the medium.
symmetric orientation
no resulting dipole field
asymmetric orientation
resulting dipole field
change of dipole field → radiation
δ ≡ polarization of medium
atomic dipoles
fast orientation of dipoles
= 0.3071 MeV g-1cm2

## Slide 25: Cherenkov radiation
Pavel Alekseyevich
Cherenkov

## Slide 26: Cherenkov radiation
threshold velocity:
threshold angle:
Parameters of typical radiators
medium | n |  |  | 
air | 1.000283 | 0.9997 | 1.36 | 0.208
isobutene | 1.00127 | 0.9987 | 2.89 | 0.941
water | 1.33 | 0.752 | 41.2 | 160.8
quartz | 1.46 | 0.685 | 46.7 | 196.4
medium | n |  |  | 
air | 1.000283 | 0.9997 | 1.36 | 0.208
isobutene | 1.00127 | 0.9987 | 2.89 | 0.941
water | 1.33 | 0.752 | 41.2 | 160.8
quartz | 1.46 | 0.685 | 46.7 | 196.4
Note: Energy loss due to Cherenkov radiation very small compared to ionization (<1%)

## Slide 27: Interaction of gamma rays with matter

## Slide 28: Interaction of gamma rays with matter
total absorption coefficient: μ/ρ [cm2/g]
Aluminum
Lead
i=1 photoelectric effect
i=2 Compton scattering
i=3 pair production

## Slide 29: Interaction of gamma rays with matter
Photo effect:
Absorption of a photon by a bound electron and conversion of the γ-energy in potential and kinetical energy of the ejected electron.
(Nucleus preserves the momentum conservation.)

## Slide 30: Interaction of gamma rays with matter
Compton scattering:
Elastic scattering of a γ-ray on a free electron. A fraction of the γ-ray energy is transferred to the Compton electron. The wave length of the scattered γ-ray is increased: λ‘ > λ.
Maximum energy of the
scattered electron:
Energy of the scattered
γ-photon:
Special case for E >> mec2:
γ-ray energy after 1800 scatter
is approximately
Gap between the incoming γ-ray and the maximum electron energy.

## Slide 31: Interaction of gamma rays with matter
Pair production:
If γ-ray energy is >> 2m0c2 (electron rest mass 511 keV), a positron-electron pair can be formed in the strong Coulomb field of a nucleus. This pair carries the γ-ray energy minus 2m0c2.
Pair production for Eγ>2mec2=1.022MeV
γ-ray > 1 MeV
magnetic field
γ’s
e-
picture of a bubble chamber

## Slide 32: Gamma-ray interaction cross section
All three interaction (photo effect, Compton scattering and pair production) lead to an attenuation of the γ-ray or X-ray radiation when passing through matter. The particular contribution depends on the γ-ray energy:
The absorption attenuates the intensity, but the energy and the frequency of the γ-ray and X-ray radiation is preserved!
Photo effect: ~Z4-5, Eγ-3.5
Compton: ~Z, Eγ-1
Pair: ~Z2, increases with Eγ

## Slide 33: Literature
Recommended Textbook
Recommended Textbook

## Slide 34: Some Nuclear Units
Nuclear energies are very high compared to atomic processes, and need larger units. The most commonly used unit is the MeV.
1 electron Volt = 1 eV = 1.6·10-19 Joules
1 MeV = 106 eV; 1 GeV = 109 eV; 1 TeV = 1012 eV
However, the nuclear size are quite small and need smaller units:
Atomic sizes are on the order of 0.1 nm = 1 Angstrom = 10-10 m. Nuclear sizes are on the order of femtometers which in the nuclear context are usually called fermis:
1 fermi = 1 fm = 10-15 m
Atomic masses are measured in terms of atomic mass units with the carbon-12 atom defined as having a mass of exactly 12 amu. It is also common practice to quote the rest mass energy E=m0c2 as if it were the mass. The conversion to amu is:
1 u = 1.66054·10-27 kg = 931.494 MeV/c2
electron mass = 0.511 MeV/c2; proton mass = 938.27 MeV/c2; neutron mass = 939.56 MeV/c2
Mass data: www.nndc.bnl.gov/qcalc/

## Slide 35: Some Nuclear Units

## Slide 36: Relevant Formulae
The relevant formulae are calculated if A1, Z1 and A2, Z2 are the mass number (amu) and charge number of the projectile and target nucleus, respectively, and Tlab is the laboratory energy (MeV)
beam velocity:
Lorentz contraction factor:

## Slide 37: Radiation protection
The biological dose, sometimes also known as the dose equivalent is expressed in units of Sieverts [Sv]. This dose reflects the fact that the biological damage caused by a particle depends not only on the total energy deposited but also on the rate of energy loss per unit distance traversed by the particle.
equivalent dose = energy dose · quality factor Q
radiation | quality factor Q
X-ray, γ, β | 1
thermal neutrons | 2.3
fast neutrons | 10
α-particles, heavy ions | 20

## Slide 38: Radiation protection
range in air [m]
concrete
Pb
Al
α´s
β´s
X-rays
γ-rays
neutrons
radioactive
source

## Slide 39: Solid angle
d
1 Ci = 3.7·1010 Bq
Ω = solid angle between source and detector (sr)
For a point source:
d (cm) r = 3cm |  | 
5 | 7.13 | 55
10 | 2.11 | 2.25
15 | 0.97 | 1
d (cm) r = 3cm |  | 
5 | 7.13 | 55
10 | 2.11 | 2.25
15 | 0.97 | 1