GROUP boot

NAME		boot-automatically
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Boot Automatically
SNMP NAME	ncdBootServerAutomatically
SNMP PATH	ncdBoot 1
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies whether the terminal automatically boots
		or simply stops in the boot monitor with the > prompt.
		
		This parameter is ignored if the terminal has been
		put in one of the secure modes.


NAME		boot-custom-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Custom File
SNMP NAME	ncdBootCustomFile
SNMP PATH	ncdBoot 20
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies a non-standard name for the server
		download file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.
		
		This feature is only available with boot monitor
		version 2.6.0 or later.


NAME		boot-default-server-when-prom-booting
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Default Server when PROM Booting
SNMP NAME	ncdBootDefaultServer
SNMP PATH	ncdBoot 7
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		When the terminal is booted via the network, the
		boot server is considered the default server to
		be used when a particular server has not been
		specified. This parameter specifies the default
		server when the terminal is booted locally.


NAME		boot-desired-source
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Desired Source
SNMP NAME	ncdBootDesiredSource
SNMP PATH	ncdBoot 5
TYPE		CHOICE
CHOICES		{ tcpip tftp nfs ncdnet local prom }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the desired source of the server code
		on the next boot of the terminal.
		
		'Local' describes a number of options including
		PROM's, Flash Memory cards, battery-backed static
		RAM cards, and OTP (One-Time Programmable) cards.
		'PROM' is an alias for 'Local' provided for
		backwards compatibility.
		
		'TCPIP' is an alias for 'TFTP' provided for
		backwards compatibility.


NAME		boot-monitor-inverse-video
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Boot Monitor Inverse Video
SNMP NAME	ncdBootMonitorReverseVideo
SNMP PATH	ncdBoot 8
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies whether the boot monitor should use
		inverse video -- dark characters on a light
		background.


NAME		boot-mop
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Try MOP
SNMP NAME	ncdBootMop
SNMP PATH	ncdBoot 18
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that MOP should be used to request
		a server download file.


NAME		boot-mop-with-file-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Try MOP with File Name
SNMP NAME	ncdBootMopWithFileName
SNMP PATH	ncdBoot 19
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that a MOP download request should
		specify a file name.
		
		Normally MOP requests do not specify the name of
		the file to be loaded.


NAME		boot-nfs-directory
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>NFS Directory
SNMP NAME	ncdBootNfsDirectory
SNMP PATH	ncdBoot 22
TYPE		STRING
DEFAULT		/tftpboot/
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the UNIX directory where the terminal should
		search when using NFS to download the server file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.
		
		This feature is only available with boot monitor
		version 2.6.0 or later.


NAME		boot-persistent-loading
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Persistent Loading
SNMP NAME	ncdBootPersist
SNMP PATH	ncdBoot 6
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies whether the terminal should continue
		attempting to boot until it succeeds.
		This feature is only available with boot monitor
		version 2.3.3 or later.


NAME		boot-previous-server
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Previous Server
SNMP NAME	ncdBootActualServer
SNMP PATH	ncdBoot 4
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the most recent boot server.


NAME		boot-previous-source
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Previous Source
SNMP NAME	ncdBootActualSource
SNMP PATH	ncdBoot 3
TYPE		CHOICE
CHOICES		{ tcpip tftp nfs ncdnet local prom }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the most recent boot source.
		
		'Local' describes a number of options including
		PROM's, Flash Memory cards, battery-backed static
		RAM cards, and OTP (One-Time Programmable) cards.
		'PROM' is an alias for 'Local' provided for
		backwards compatibility.
		
		'TCPIP' is an alias for 'TFTP' provided for
		backwards compatibility.


NAME		boot-send-broadcast-icmp-for-subnet-mask
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Send Broadcast ICMP for Subnet Mask
SNMP NAME	ncdBootEnableICMPSubnetMaskRequest
SNMP PATH	ncdBoot 16
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Use an ICMP message sent to the broadcast address
		to determine the appropriate subnet mask at server
		boot. If this is disabled, only the boot server is
		sent the ICMP message.
		
		Note that this option can produce a lot of network
		traffic.
		
		This feature is only available with boot monitor
		version 2.3.3 or later.


NAME		boot-tcpip-broadcast-boot-request
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Broadcast Boot Request
SNMP NAME	ncdBootBroadcastInetRequest
SNMP PATH	ncdBoot 17
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the boot monitor should broadcast
		download file requests.
		
		Note that this option can produce a lot of network
		traffic.
		
		This feature is only available with boot monitor
		version 2.2.0 or later.


NAME		boot-tcpip-desired-server
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Desired Server
SNMP NAME	ncdBootDesiredInetServer
SNMP PATH	ncdBoot 9
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the IP address of the boot server
		when the desired boot source is TCP/IP.


NAME		boot-tcpip-product-name-and-memory-size-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Product Name and Memory Size File
SNMP NAME	ncdBootUseRelativeMemSizeFile
SNMP PATH	ncdBoot 12
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the product model form of server
		download file name with the memory size suffix
		should be used to request a server download file.
		
		This feature is only available with boot monitor
		version 2.0.0 or later.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-tcpip-product-name-and-memory-size-with-path-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Product Name and Memory Size with Path File
SNMP NAME	ncdBootUseAbsoluteMemSizeFile
SNMP PATH	ncdBoot 13
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the product model form of server
		download file name with the memory size suffix
		prefixed with the string /tftpboot/ should be
		used to request a server download file.
		
		This feature is only available with boot monitor
		version 2.0.0 or later.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-tcpip-product-name-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Product Name File
SNMP NAME	ncdBootUseRelativeProductFile
SNMP PATH	ncdBoot 14
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the product model form of server
		download file name should be used to request a
		server download file.
		
		This feature is only available with boot monitor
		version 2.0.0 or later.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-tcpip-product-name-with-path-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Product Name with Path File
SNMP NAME	ncdBootUseAbsoluteProductFile
SNMP PATH	ncdBoot 15
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the product model form of server
		download file name with the prefix /tftpboot/
		should be used to request a server download file.
		
		This feature is only available with boot monitor
		version 2.0.0 or later.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-tcpip-unit-address-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Unit Address File
SNMP NAME	ncdBootUseRelativeHexFile
SNMP PATH	ncdBoot 10
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the hexidecimal representation of
		the IP address should be used to request a server
		download file.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-tcpip-unit-address-with-path-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TCPIP Unit Address with Path File
SNMP NAME	ncdBootUseAbsoluteHexFile
SNMP PATH	ncdBoot 11
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the hexidecimal representation of
		the IP address prefixed with the string /tftpboot/
		should be used to request a server download file.
		
		This feature is only available with boot monitor
		version 2.0.0 or later.
		
		This feature can only be disabled when using boot
		monitor version 2.2.0 or later.


NAME		boot-test-ram
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>Test RAM
SNMP NAME	ncdBootRamTest
SNMP PATH	ncdBoot 2
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies whether RAM self tests are performed
		at power up.
		
		It is suggested that this self test not be
		disabled.


NAME		boot-tftp-directory
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Booting=>TFTP Directory
SNMP NAME	ncdBootTftpDirectory
SNMP PATH	ncdBoot 21
TYPE		STRING
DEFAULT		/tftpboot/
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the UNIX directory where the terminal should
		search when using TFTP to download the server file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.
		
		This feature is only available with boot monitor
		version 2.6.0 or later.



GROUP config

NAME		config-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable Config Access Control
SNMP NAME	ncdAccessConfigdAccessControlEnabled
SNMP PATH	ncdAccess 8
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether requests for connections to the
		configuration daemon from outside the terminal will
		be checked against the host access control list


NAME		config-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Config Access Control List
SNMP NAME	ncdAccessConfigdHostTable
SNMP PATH	ncdAccess 9
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list for the
		configuration daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessCHTIndex
SNMP PATH	ncdAccessConfigdHostTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Config Access Control List


NAME		host
SNMP NAME	ncdAccessCHTAddress
SNMP PATH	ncdAccessConfigdHostTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the configuration
		daemon.


NAME		family
SNMP NAME	ncdAccessCHTFamily
SNMP PATH	ncdAccessConfigdHostTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of network connection for
		which this entry applies.


END TABLE ROW ENTRIES

NAME		config-add-domain-to-unit-name-as-filename
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Add Domain to Unit Name as Filename
SNMP NAME	ncdConfigInitUseFQUnitName
SNMP PATH	ncdConfig 7
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's symbolic name
		should include the domain, e.g. ncdu4.ncd.com.
		when being used as the file name of the initial
		configuration file.


NAME		config-auto-save-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Auto Save File
SNMP NAME	ncdConfigAutoSaveFile
SNMP PATH	ncdConfig 16
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that any changes made to the terminal's
		configuration are automatically saved to a file.


NAME		config-auto-save-file-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Auto Save File Name
SNMP NAME	ncdConfigAutoSaveFileName
SNMP PATH	ncdConfig 17
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file to which automatic saves of
		configuration changes are made.


NAME		config-auto-save-nvram
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Auto Save NVRAM
SNMP NAME	ncdConfigAutoSaveNvram
SNMP PATH	ncdConfig 15
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that any changes made to the terminal's
		configuration that are stored in NVRAM, are
		automatically saved.


NAME		config-auto-saved-info
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Auto Saved Info
SNMP NAME	ncdConfigAutoSaveChanges
SNMP PATH	ncdConfig 18
TYPE		CHOICE
CHOICES		{ user-changes all-changes all-info }
DEFAULT		user-changes
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what information is automatically
		saved to file when configuration changes are made.


NAME		config-custom-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Custom File
SNMP NAME	ncdConfigInitFile
SNMP PATH	ncdConfig 5
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies a non-standard name for the initial
		configuration file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.


NAME		config-default-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Default File
SNMP NAME	ncdConfigDfltFile
SNMP PATH	ncdConfig 14
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the configuration file which is
		considered to define the default configuration
		of the terminal. This will be initialized to
		the name of the file that is loaded as the
		initial configuration file.


NAME		config-enforce-passwords-locally
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enforce Config Passwords Locally
SNMP NAME	ncdAccessConfigdEnforePasswdsLocally
SNMP PATH	ncdAccess 7
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that a password is required to access
		configuration information at the terminal. Normally,
		the local unit does not require a password to access
		it's own configuration information.


NAME		config-generic-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Generic File
SNMP NAME	ncdConfigInitUseGenericFile
SNMP PATH	ncdConfig 11
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the standard generic file
		should be used as the file name for the
		initial configuration file.


NAME		config-load-initial-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Load Initial File
SNMP NAME	ncdConfigInitFileLoad
SNMP PATH	ncdConfig 1
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies whether an initial configuration file
		should be loaded.


NAME		config-ncdnet-object-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>NCDnet Object Name
SNMP NAME	ncdConfigDnetObject
SNMP PATH	ncdConfig 23
TYPE		STRING
DEFAULT		CONFIGD
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the configuration
		daemon.


NAME		config-persistent-loading
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Persistent Loading
SNMP NAME	ncdConfigInitPersistentFileLoad
SNMP PATH	ncdConfig 2
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies whether the terminal is to persist in
		attempting to load an initial configuration file
		until it succeeds.


NAME		config-pref-enforce-passwords-locally
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enforce User Preferences Passwords Locally
SNMP NAME	ncdAccessPrefdEnforcePasswdsLocally
SNMP PATH	ncdAccess 12
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that a password is required to access
		user preferences information at the terminal. Normally,
		the local unit does not require a password to access
		it's own user preferences information.


NAME		config-pref-ncdnet-object-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>NCDnet Object Name
SNMP NAME	ncdConfigPrefdDnetObject
SNMP PATH	ncdConfig 21
TYPE		STRING
DEFAULT		PREFD
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the user
		preferences daemon.


NAME		config-pref-read-only-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>User Preferences Read-Only Password
SNMP NAME	ncdAccessPrefdReadOnlyPasswd
SNMP PATH	ncdAccess 10
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain read-only access
		to the user preference information.


NAME		config-pref-read-write-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>User Preferences Read-Write Password
SNMP NAME	ncdAccessPrefdReadWritePasswd
SNMP PATH	ncdAccess 11
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain read-write access
		to the user preferences information.


NAME		config-pref-tcp-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>TCP Port
SNMP NAME	ncdConfigPrefdTcpPort
SNMP PATH	ncdConfig 20
TYPE		INTEGER
MIN		1024
DEFAULT		5977
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the user
		preferences daemon.


NAME		config-pref-telnet-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Telnet Port
SNMP NAME	ncdConfigPrefdTelnetPort
SNMP PATH	ncdConfig 19
TYPE		INTEGER
MIN		1024
DEFAULT		5997
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for telnet connections to the user
		preferences daemon.


NAME		config-read-only-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Config Read-Only Password
SNMP NAME	ncdAccessConfigdReadOnlyPasswd
SNMP PATH	ncdAccess 5
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain read-only access
		to the configuration information.


NAME		config-read-write-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Config Read-Write Password
SNMP NAME	ncdAccessConfigdReadWritePasswd
SNMP PATH	ncdAccess 6
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain read-write access
		to the configuration information.


NAME		config-tcp-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>TCP Port
SNMP NAME	ncdConfigTcpPort
SNMP PATH	ncdConfig 13
TYPE		INTEGER
MIN		1024
DEFAULT		5979
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the configuration
		daemon.


NAME		config-telnet-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Telnet Port
SNMP NAME	ncdConfigTelnetPort
SNMP PATH	ncdConfig 12
TYPE		INTEGER
MIN		1024
DEFAULT		5999
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for telnet connections to the configuration
		daemon.


NAME		config-unit-ethernet-address-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Unit Ethernet Address File
SNMP NAME	ncdConfigInitUseEnetUnitAddrFile
SNMP PATH	ncdConfig 8
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's Ethernet addresss,
		e.g. 0000A7001234, should be used as the file name
		for the initial configuration file.


NAME		config-unit-ip-address-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Unit IP Address File
SNMP NAME	ncdConfigInitUseInetUnitAddrFile
SNMP PATH	ncdConfig 9
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's IP addresss,
		e.g. C02B9A04, should be used as the file name
		for the initial configuration file.


NAME		config-unit-name-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Unit Name File
SNMP NAME	ncdConfigInitUseUnitNameFile
SNMP PATH	ncdConfig 6
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's symbolic name,
		e.g. ncdu4, should be used as the file name
		for the initial configuration file.


NAME		config-unit-ncdnet-address-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Unit NCDnet Address File
SNMP NAME	ncdConfigInitUseDnetUnitAddrFile
SNMP PATH	ncdConfig 22
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's NCDnet addresss,
		e.g. 1.17, should be used as the file name
		for the initial configuration file.


NAME		config-unix-directory
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>UNIX Directory
SNMP NAME	ncdConfigDfltUnixDirectory
SNMP PATH	ncdConfig 3
TYPE		STRING
DEFAULT		/usr/lib/X11/ncd/configs/
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the UNIX directory where the terminal should
		search for it's initial configuration file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.


NAME		config-use-decimal-ip-address-notation-as-filename
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>Use Decimal IP Address Notation as Filename
SNMP NAME	ncdConfigInitUseDecimalInetUnitAddr
SNMP PATH	ncdConfig 10
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the terminal's IP address
		should be used in decimal dotted notation,
		e.g. 192.43.154.4, when being used as the
		file name of the initial configuration file.


NAME		config-vms-directory
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Configuration=>VMS Directory
SNMP NAME	ncdConfigDfltVmsDirectory
SNMP PATH	ncdConfig 4
TYPE		STRING
DEFAULT		NCD_ROOT:[CONFIGS]
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the VMS directory where the terminal should
		search for it's initial configuration file.
		
		If specified this parameter consumes space in
		the optional string space of NVRAM.



GROUP diag

NAME		diag-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable Diagnostic Access Control
SNMP NAME	ncdAccessDiagdAccessControlEnabled
SNMP PATH	ncdAccess 24
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether requests for connections to the
		diagnostic daemon from outside the terminal will
		be checked against the host access control list.


NAME		diag-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Diagnostic Access Control List
SNMP NAME	ncdAccessDiagdAccessControlTable
SNMP PATH	ncdAccess 25
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list
		for the diagnostic daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessDiagdACTIndex
SNMP PATH	ncdAccessDiagdAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Diagd Access Control List


NAME		host
SNMP NAME	ncdAccessDiagdACTAddress
SNMP PATH	ncdAccessDiagdAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the diagnostic
		daemon.


NAME		family
SNMP NAME	ncdAccessDiagdACTFamily
SNMP PATH	ncdAccessDiagdAccessControlTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of network connection for
		which this entry applies.


END TABLE ROW ENTRIES

NAME		diag-add-timestamps
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>Add Timestamps
SNMP NAME	ncdDiagTimestampEnabled
SNMP PATH	ncdDiag 1
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the diagnostic daemon should
		add timestamps to the diagnostic log.


NAME		diag-buffer-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>Buffer Size
SNMP NAME	ncdDiagConfiguredBufferSize
SNMP PATH	ncdDiag 3
TYPE		INTEGER
MIN		2048
DEFAULT		8192
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum size (in bytes)
		of the diagnostic log.


NAME		diag-log-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>Log File
SNMP NAME	ncdDiagLogFile
SNMP PATH	ncdDiag 4
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file name where to write a copy of the
		diagnostic log.


NAME		diag-ncdnet-object-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>NCDnet Object Name
SNMP NAME	ncdDiagDnetObject
SNMP PATH	ncdDiag 7
TYPE		STRING
DEFAULT		DIAGD
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the diagnostics
		daemon.


NAME		diag-tcp-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>TCP Port
SNMP NAME	ncdDiagTcpPort
SNMP PATH	ncdDiag 6
TYPE		INTEGER
MIN		1024
DEFAULT		5978
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the diagnostics
		daemon.


NAME		diag-telnet-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>Telnet Port
SNMP NAME	ncdDiagTelnetPort
SNMP PATH	ncdDiag 5
TYPE		INTEGER
MIN		1024
DEFAULT		5998
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for telnet connections to the diagnostics
		daemon.


NAME		diag-timestamp-frequency
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Diagnostics=>Timestamp Frequency
SNMP NAME	ncdDiagTimestampGranularity
SNMP PATH	ncdDiag 2
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum frequency (in seconds)
		at which timestamps are added to the diagnostic log.



GROUP dps

NAME		dps-resource-path
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Display PostScript=>DPS/X resource Path
SNMP NAME	ncdDpsResourcePath
SNMP PATH	ncdDps 1
TYPE		STRING
DEFAULT		/usr/lib/X11/ncd/dps::
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The path to search for DPS resource files.



GROUP enet

NAME		enet-interfaces-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Ethernet=>Interfaces Table
SNMP NAME	ncdEtherTable
SNMP PATH	ncdEther 1
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The table of Ethernet interfaces.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdEtherTableIndex
SNMP PATH	ncdEtherTable 11
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Ethernet Interfaces Table


NAME		packets-received-with-crc-errors
SNMP NAME	ncdEtherInCrcErrors
SNMP PATH	ncdEtherTable 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times a incoming frame failed the
		Cyclic Redundancy Check (CRC).


NAME		packets-missed
SNMP NAME	ncdEtherInMisseds
SNMP PATH	ncdEtherTable 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an incoming frame was
		not received due to a lack of buffers.


NAME		packets-received-with-framing-errors
SNMP NAME	ncdEtherInFrameErrors
SNMP PATH	ncdEtherTable 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an incoming frame had a bad bit
		alignment.


NAME		single-collisions-on-packet-transmission
SNMP NAME	ncdEtherSingleCollisions
SNMP PATH	ncdEtherTable 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an outbound frame had a single
		collision occur during transmission.


NAME		multiple-collisions-on-packet-transmission
SNMP NAME	ncdEtherMultipleCollisions
SNMP PATH	ncdEtherTable 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an outbound frame had multiple
		collisions occur during transmission.


NAME		late-collisions-on-packet-transmission
SNMP NAME	ncdEtherLateCollisions
SNMP PATH	ncdEtherTable 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the collision signal was asserted
		after the preamble of a frame was transmitted.


NAME		deferrals-on-packet-transmission
SNMP NAME	ncdEtherOutDeferreds
SNMP PATH	ncdEtherTable 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an outbound frame could not be
		transmitted directly due to the Ethernet being busy,
		and the Ethernet exponentail backoff algorithm was
		invoked.


NAME		retry-failures-on-packet-transmission
SNMP NAME	ncdEtherOutRetryErrors
SNMP PATH	ncdEtherTable 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an outbound frame could not be
		transmitted after 16 backed-off attempts due to
		repeated collisions on the Ethernet.


NAME		lost-carrier
SNMP NAME	ncdEtherLostCarriers
SNMP PATH	ncdEtherTable 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times carrier (Receiver Enable)
		was lost during the transmission of a frame.


NAME		restarts
SNMP NAME	ncdEtherRestarts
SNMP PATH	ncdEtherTable 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the software has restarted the
		Ethernet controller, possibly due to a heuristic for
		determining an inoperable controller.


END TABLE ROW ENTRIES


GROUP exec

NAME		exec-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable Execution Access Control
SNMP NAME	ncdAccessExecdAccessControlEnabled
SNMP PATH	ncdAccess 28
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether xhost-style access control
		is on or off for remote requests for local
		command execution.


NAME		exec-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Execution Access Control List
SNMP NAME	ncdAccessExecdAccessControlTable
SNMP PATH	ncdAccess 29
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list for the local
		command execution daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessExecdACTIndex
SNMP PATH	ncdAccessExecdAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Execution Access Control List


NAME		host
SNMP NAME	ncdAccessExecdACTAddress
SNMP PATH	ncdAccessExecdAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely request the execution
		of local commands.


NAME		family
SNMP NAME	ncdAccessExecdACTFamily
SNMP PATH	ncdAccessExecdAccessControlTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of network connection for
		which this entry applies.


END TABLE ROW ENTRIES

NAME		exec-disabled-commands
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Commands and Startup=>Disabled Commands
SNMP NAME	ncdExecDisabledCommandsTable
SNMP PATH	ncdExec 2
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the list of local commands that should
		be disabled so that the user of the unit is
		prevented from using these commands.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdExecDCIndex
SNMP PATH	ncdExecDisabledCommandsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Disabled Commands Table


NAME		command
SNMP NAME	ncdExecDCCommands
SNMP PATH	ncdExecDisabledCommandsTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name of the local command
		that should be disabled.


END TABLE ROW ENTRIES

NAME		exec-startup-commands
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Commands and Startup=>Startup Commands
SNMP NAME	ncdExecStartupCommandsTable
SNMP PATH	ncdExec 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of commands to be executed
		when a session is started.  The commands can
		be anything allowed by the exec daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdExecSTCIndex
SNMP PATH	ncdExecStartupCommandsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Startup Commands Table


NAME		command
SNMP NAME	ncdExecSTCCommands
SNMP PATH	ncdExecStartupCommandsTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the command to be executed.


END TABLE ROW ENTRIES


GROUP file

NAME		file-default-vms-file-name-extension
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Default VMS File Name Extension
SNMP NAME	ncdFileDfltVmsExtension
SNMP PATH	ncdFile 11
TYPE		STRING
DEFAULT		.DAT
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default file extension appended to file
		names if one does not already exist when referencing
		the file on a file server with VMS style names.


NAME		file-extended-diagnostics
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Extended Diagnostics
SNMP NAME	ncdFileExtendedDiagnostics
SNMP PATH	ncdFile 7
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies that the unit should generate more detailed
		diagnostic messages regarding file service.


NAME		file-failed-server-ignore-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Failed Server Ignore Timeout
SNMP NAME	ncdFileServerHolddownTime
SNMP PATH	ncdFile 9
TYPE		INTEGER
MIN		1
DEFAULT		120
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to ignore a file server
		which has failed due to a network timeout error.
		An ignored server is skipped over when attempt to open
		a new file. This behavior speeds up unit booting and
		session reset when the primary file server has failed.


NAME		file-initial-protocol-1
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Initial Protocol 1
SNMP NAME	ncdFileInitialFileServer1Protocol
SNMP PATH	ncdFile 2
TYPE		CHOICE
CHOICES		{ tftp nfs ncdnet nfs/tcp }
DEFAULT		tftp
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the file service protocol to be used
		in conjunction with the primary initial file server.


NAME		file-initial-protocol-2
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Initial Protocol 2
SNMP NAME	ncdFileInitialFileServer2Protocol
SNMP PATH	ncdFile 4
TYPE		CHOICE
CHOICES		{ tftp nfs ncdnet nfs/tcp }
DEFAULT		tftp
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the file service protocol to be used
		in conjunction with the secondary initial file server.


NAME		file-initial-server-1
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Initial Server 1
SNMP NAME	ncdFileInitialFileServer1
SNMP PATH	ncdFile 1
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the host to be used as the primary file server
		at boot time to load the initial config file.
		
		A value of 0.0.0.0 implies that the boot server should be
		used for this value.


NAME		file-initial-server-2
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Initial Server 2
SNMP NAME	ncdFileInitialFileServer2
SNMP PATH	ncdFile 3
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the host to be used as the secondary file server
		at boot time to load the initial config file.
		
		A value of 0.0.0.0 implies that the boot server should be
		used for this value.


NAME		file-manager-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable File Manager Access Control
SNMP NAME	ncdAccessFiledAccessControlEnabled
SNMP PATH	ncdAccess 34
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether xhost-style access control
		is on or off for remote requests for file
		manager daemon.


NAME		file-manager-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>File Manager Access Control List
SNMP NAME	ncdAccessFiledAccessControlTable
SNMP PATH	ncdAccess 35
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list for the
		file manager daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessFiledACTIndex
SNMP PATH	ncdAccessFiledAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the File Manager Access Control List


NAME		host
SNMP NAME	ncdAccessFiledACTAddress
SNMP PATH	ncdAccessFiledAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely request the execution
		of local commands.


NAME		family
SNMP NAME	ncdAccessFiledACTFamily
SNMP PATH	ncdAccessFiledAccessControlTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of network connection for
		which this entry applies.


END TABLE ROW ENTRIES

NAME		file-manager-ncdnet-object-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Manager=>NCDnet Object Name
SNMP NAME	ncdFileManagerDnetObject
SNMP PATH	ncdFile 14
TYPE		STRING
DEFAULT		FILED
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the file manager
		daemon.


NAME		file-manager-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Password
SNMP NAME	ncdAccessFileManagerPasswd
SNMP PATH	ncdAccess 33
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain access
		to the file manager.


NAME		file-manager-tcp-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Manager=>TCP Port
SNMP NAME	ncdFileManagerTcpPort
SNMP PATH	ncdFile 13
TYPE		INTEGER
MIN		1024
DEFAULT		5976
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the file
		manager daemon.


NAME		file-manager-telnet-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Manager=>Telnet Port
SNMP NAME	ncdFileManagerTelnetPort
SNMP PATH	ncdFile 12
TYPE		INTEGER
MIN		1024
DEFAULT		5996
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for telnet connections to the file manager
		daemon.


NAME		file-name-type-for-initial-tftp-servers
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Name Type for Initial TFTP Servers
SNMP NAME	ncdFileInitialFileServersUseVmsTftp
SNMP PATH	ncdFile 5
TYPE		CHOICE
CHOICES		{ unix vms }
DEFAULT		unix
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the type of file names to be sent via TFTP
		in conjunction with the initial file servers.


NAME		file-nfs-gid
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>NFS Group ID
SNMP NAME	ncdAccessNfsGroupId
SNMP PATH	ncdAccess 27
TYPE		INTEGER
MIN		-2147483648
DEFAULT		-2
MAX		2147483647
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the GID (Group ID) to be used for NFS and RPC
		requests.


NAME		file-nfs-uid
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>NFS User ID
SNMP NAME	ncdAccessNfsUserId
SNMP PATH	ncdAccess 26
TYPE		INTEGER
MIN		-2147483648
DEFAULT		-2
MAX		2147483647
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the UID (User ID) to be used for NFS and RPC
		requests.


NAME		file-nfs-unmount-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>NFS Unmount Timeout
SNMP NAME	ncdFileUnmountTime
SNMP PATH	ncdFile 10
TYPE		INTEGER
MIN		1
DEFAULT		1800
MAX		3600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) after the last reference
		to an NFS file service entry that the unit automatically
		notifies the server that it no longer requires access
		to the file system.


NAME		file-service-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>File Service Table
SNMP NAME	ncdFileServiceTable
SNMP PATH	ncdFile 6
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file service table.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdFileSTIndex
SNMP PATH	ncdFileServiceTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the File Service Table


NAME		local-unix-mount-point
SNMP NAME	ncdFileSTLocalUnixMountPoint
SNMP PATH	ncdFileServiceTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the unit's UNIX style local name
		for this file service access point.


NAME		local-vms-mount-point
SNMP NAME	ncdFileSTLocalVmsMountPoint
SNMP PATH	ncdFileServiceTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the unit's VMS style local name
		for this file service access point.


NAME		server
SNMP NAME	ncdFileSTServerAddress
SNMP PATH	ncdFileServiceTable 4
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file server.


NAME		protocol
SNMP NAME	ncdFileSTProtocol
SNMP PATH	ncdFileServiceTable 5
TYPE		CHOICE
CHOICES		{ tftp nfs ncdnet nfs/tcp }
DEFAULT		tftp
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file service protocol.


NAME		server-mount-point
SNMP NAME	ncdFileSTServerMountPoint
SNMP PATH	ncdFileServiceTable 6
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name on the file server
		of the file service access point.


NAME		file-name-type
SNMP NAME	ncdFileSTFileNameType
SNMP PATH	ncdFileServiceTable 7
TYPE		CHOICE
CHOICES		{ unknown unix vms }
DEFAULT		unknown
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of file names
		used by the file server. This is not
		used with NFS file servers.


NAME		retransmission-timeout
SNMP NAME	ncdFileSTRetransTimeout
SNMP PATH	ncdFileServiceTable 8
TYPE		INTEGER
MIN		0
DEFAULT		3
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) between
		successive transmissions of a file service
		request. Note this is only used with file
		service protocols running over connectionless
		transport services, e.g. NFS or TFTP.


NAME		transaction-timeout
SNMP NAME	ncdFileSTTransTimeout
SNMP PATH	ncdFileServiceTable 9
TYPE		INTEGER
MIN		0
DEFAULT		30
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to attempt
		a file service request before a failure
		situation is declared.


NAME		read-size
SNMP NAME	ncdFileSTReadSize
SNMP PATH	ncdFileServiceTable 10
TYPE		INTEGER
MIN		0
DEFAULT		8192
MAX		8192
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of data in bytes
		to be requested in a single read request.
		This parameter is only used with NFS or
		NFS/TCP. If you are having problems reading
		files with NFS across gateways, try decreasing
		this parameter to 1024.


NAME		write-size
SNMP NAME	ncdFileSTWriteSize
SNMP PATH	ncdFileServiceTable 11
TYPE		INTEGER
MIN		0
DEFAULT		8192
MAX		8192
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of data in bytes
		to be requested in a single write request.
		This parameter is only used with NFS or
		NFS/TCP. If you are having problems writing
		files with NFS across gateways, try decreasing
		this parameter to 1024.


END TABLE ROW ENTRIES

NAME		file-try-all-matches-on-open
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  File Service=>Try All Matches on Open
SNMP NAME	ncdFileRegressiveSearch
SNMP PATH	ncdFile 8
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the unit should try all file service
		entries that match when opening a file, until it
		succeeds in opening the file, or there are no more
		matches remain. If this is not enabled, then the unit
		only tries the longest match(es) in the file service table.



GROUP font

NAME		font-cache-hits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Cache Hits
SNMP NAME	ncdFontServiceCacheHits
SNMP PATH	ncdFontService 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of fonts cache hits


NAME		font-cache-size
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Cache Size
SNMP NAME	ncdFontServiceCacheSize
SNMP PATH	ncdFontService 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the total size of the font cache


NAME		font-cache-used
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Cache Used
SNMP NAME	ncdFontServiceCacheUsed
SNMP PATH	ncdFontService 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the portion of cache memory that is in use


NAME		font-number-of-fonts-in-cache
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Number of Fonts in Cache
SNMP NAME	ncdFontServiceNumCachedFonts
SNMP PATH	ncdFontService 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of fonts currently in cache


NAME		font-object-count
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Object Count
SNMP NAME	ncdFontServiceFontsInUse
SNMP PATH	ncdFontService 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the current number of fonts objects


NAME		font-objects-currently-in-use
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Objects Currently in Use
SNMP NAME	ncdFontServiceReferenceIncs
SNMP PATH	ncdFontService 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of fonts objects that are
		in use currently


NAME		font-total-fonts-loaded
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Font Usage=>Total Fonts Loaded
SNMP NAME	ncdFontServiceNetLoads
SNMP PATH	ncdFontService 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the total number of fonts loaded
		since the terminal has been in use



GROUP icmp

NAME		icmp-address-mask-replies-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Address Mask Replies Received
SNMP NAME	icmpInAddrMasksReps
SNMP PATH	icmp 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Address Mask Reply messages received.


NAME		icmp-address-mask-replies-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Address Mask Replies Transmitted
SNMP NAME	icmpOutAddrMaskReps
SNMP PATH	icmp 26
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Address Mask Reply messages sent.


NAME		icmp-address-mask-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Address Mask Requests Received
SNMP NAME	icmpInAddrMasks
SNMP PATH	icmp 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Address Mask Request messages received.


NAME		icmp-address-mask-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Address Mask Requests Transmitted
SNMP NAME	icmpOutAddrMasks
SNMP PATH	icmp 25
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Address Mask Request messages sent.


NAME		icmp-destination-unreachables-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Destination Unreachables Received
SNMP NAME	icmpInDestUnreachs
SNMP PATH	icmp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Destination Unreachable messages received.


NAME		icmp-destination-unreachables-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Destination Unreachables Transmitted
SNMP NAME	icmpOutDestUnreachs
SNMP PATH	icmp 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Destination Unreachable messages sent.


NAME		icmp-echo-replies-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Echo Replies Received
SNMP NAME	icmpInEchoReps
SNMP PATH	icmp 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Echo Reply messages received.


NAME		icmp-echo-replies-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Echo Replies Transmitted
SNMP NAME	icmpOutEchoReps
SNMP PATH	icmp 22
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Echo Reply messages sent.


NAME		icmp-echo-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Echo Requests Received
SNMP NAME	icmpInEchos
SNMP PATH	icmp 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Echo (request) messages received.


NAME		icmp-echo-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Echo Requests Transmitted
SNMP NAME	icmpOutEchos
SNMP PATH	icmp 21
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Echo (request) messages sent.


NAME		icmp-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Packets Received
SNMP NAME	icmpInMsgs
SNMP PATH	icmp 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of ICMP messages which the
		entity received.  Note that this counter includes
		all those counted by ICMP Packets Received with Errors.


NAME		icmp-packets-received-with-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Packets Received with Errors
SNMP NAME	icmpInErrors
SNMP PATH	icmp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP messages which the entity
		received but determined as having ICMP-specific
		errors (bad ICMP checksums, bad length, etc.).


NAME		icmp-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Packets Transmitted
SNMP NAME	icmpOutMsgs
SNMP PATH	icmp 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of ICMP messages which this
		entity attempted to send.  Note that this counter
		includes all those counted by ICMP Packets Unable
		to be Transmitted.


NAME		icmp-packets-unable-to-be-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Packets Unable to be Transmitted
SNMP NAME	icmpOutErrors
SNMP PATH	icmp 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP messages which this entity did
		not send due to problems discovered within ICMP
		such as a lack of buffers.  This value should not
		include errors discovered outside the ICMP layer
		such as the inability of IP to route the resultant
		datagram.  In some implementations there may be no
		types of error which contribute to this counter's value.


NAME		icmp-parameter-problems-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Parameter Problems Received
SNMP NAME	icmpInParamProbs
SNMP PATH	icmp 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Parameter Problem messages received.


NAME		icmp-parameter-problems-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Parameter Problems Transmitted
SNMP NAME	icmpOutParamProbs
SNMP PATH	icmp 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Parameter Problem messages sent.


NAME		icmp-redirects-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Redirects Received
SNMP NAME	icmpInRedirects
SNMP PATH	icmp 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Redirect messages received.


NAME		icmp-redirects-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Redirects Transmitted
SNMP NAME	icmpOutRedirects
SNMP PATH	icmp 20
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Redirect messages sent.  For an
		NCD unit, this object will always be zero, since non-routers
		do not send redirects.


NAME		icmp-source-quenches-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Source Quenches Received
SNMP NAME	icmpInSrcQuenchs
SNMP PATH	icmp 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Source Quench messages received.


NAME		icmp-source-quenches-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Source Quenches Transmitted
SNMP NAME	icmpOutSrcQuenches
SNMP PATH	icmp 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Source Quench messages sent.


NAME		icmp-time-exceededs-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Time Exceededs Received
SNMP NAME	icmpInTimeExcds
SNMP PATH	icmp 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Time Exceeded messages received.


NAME		icmp-time-exceededs-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Time Exceededs Transmitted
SNMP NAME	icmpOutTimeExcds
SNMP PATH	icmp 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Time Exceeded messages sent.


NAME		icmp-timestamp-replies-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Timestamp Replies Received
SNMP NAME	icmpInTimestampReps
SNMP PATH	icmp 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Timestamp Reply messages received.


NAME		icmp-timestamp-replies-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Timestamp Replies Transmitted
SNMP NAME	icmpOutTimestampReps
SNMP PATH	icmp 24
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Timestamp Reply messages sent.


NAME		icmp-timestamp-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Timestamp Requests Transmitted
SNMP NAME	icmpOutTimestamps
SNMP PATH	icmp 23
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Timestamp (request) messages sent.


NAME		icmp-timestamps-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  ICMP=>Timestamps Requests Received
SNMP NAME	icmpInTimestamps
SNMP PATH	icmp 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of ICMP Timestamp (request) messages received.



GROUP ip

NAME		ip-address
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>IP Address
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		YES
DESCRIPTION
		Specifies the current IP address of the unit.


NAME		ip-address-at-next-boot
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>IP Address At Next Boot
SNMP NAME	ncdIpNewAddress
SNMP PATH	ncdIp 2
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the IP address for the unit
		the next time it is booted.
		
		Note that if the current IP address is
		0.0.0.0, the value of this parameter is
		used immediately as the current IP address.
		Otherwise, the current IP address cannot
		be modified while the unit is running because
		this would lead to bizarre and unexpected behaviors
		on both the unit and any connected hosts.


NAME		ip-address-table
SNMP NAME	ipAddrTable
SNMP PATH	ip 20
TYPE		TABLE
VIEW		SNMP ONLY
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		IP addressing information relative to the respective interfaces


BEGIN TABLE ROW ENTRIES

NAME		ip-entry-address
SNMP NAME	ipAdEntAddr
SNMP PATH	ipAddrTable 1
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the current IP address of the unit.


NAME		ip-entry-if-index
SNMP NAME	ipAdEntIfIndex
SNMP PATH	ipAddrTable 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Interface Table for this Interface


NAME		ip-entry-subnet-mask
SNMP NAME	ipAdEntNetMask
SNMP PATH	ipAddrTable 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the IP subnet mask that is used to
		determine which portion of the unit's IP address
		corresponds to the network number and which
		portion to the host number.


NAME		ip-entry-broadcast-address
SNMP NAME	ipAdEntBcastAddr
SNMP PATH	ipAddrTable 4
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the IP broadcast address to be used
		when the unit sends a broadcast packet, and in
		recognizing the receipt of broadcast IP packets
		to a non-standard IP broadcast address.


NAME		largest-ip-datagram-reassembled
SNMP NAME	ipAdEntReasmMaxSize
SNMP PATH	ipAddrTable 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The size of the largest IP datagram that
		can be reassembled from incoming IP fragmented
		datagrams received on this interface.


END TABLE ROW ENTRIES

NAME		ip-broadcast-address
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Broadcast Address
TYPE		STRING
DEFAULT		255.255.255.255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the IP broadcast address to be used
		when the unit sends a broadcast packet, and in
		recognizing the receipt of broadcast IP packets
		to a non-standard IP broadcast address.


NAME		ip-default-packet-time-to-live
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Default Packet Time-to-Live
SNMP NAME	ipDefaultTTL
SNMP PATH	ip 2
TYPE		INTEGER
MIN		1
DEFAULT		255
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The default value inserted into the Time-To-Live
		field of the IP header of datagrams originated at
		this entity, whenever a TTL value is not supplied
		by the transport layer protocol.


NAME		ip-equivalent-addresses
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Equivalent IP Addresses
SNMP NAME	ncdIpEquivAddressesTable
SNMP PATH	ncdIp 11
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of equivalent IP addresses.


BEGIN TABLE ROW ENTRIES

NAME		equivalent-ip-address-table-index
SNMP NAME	ncdIpEATIndex
SNMP PATH	ncdIpEquivAddressesTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The index into the Equivalent IP Address Table


NAME		addresses
SNMP NAME	ncdIpEATAddresses
SNMP PATH	ncdIpEquivAddressesTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a list of IP addresses or IP host
		names that are to be considered as originating
		from the same host system. This is useful
		when the unit will be receiving UDP packets
		from a multihomed host.


END TABLE ROW ENTRIES

NAME		ip-extended-routing-diagnostics
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Extended Routing Diagnostics
SNMP NAME	ncdIpRouteExtendedDiagnostics
SNMP PATH	ncdIp 9
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the unit should generate more detailed
		diagnostic messages regarding IP routing.


NAME		ip-forwarding-type
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>IP Forwarding Type
SNMP NAME	ipForwarding
SNMP PATH	ip 1
TYPE		CHOICE
CHOICES		{ gateway host }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The indication of whether this entity is acting
		as an IP gateway in respect to the forwarding of
		datagrams received by, but not addressed to, this
		entity.  IP gateways forward datagrams.  IP hosts
		do not (except those source-routed via the host).
		(NCD units will never act as a gateway).


NAME		ip-initial-default-gateway-1
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Initial Default Gateway 1
SNMP NAME	ncdIpInitDfltGatewy1
SNMP PATH	ncdIp 3
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the primary default IP gateway to
		be used initially in the IP routing table.
		The IP routing table can change over time due
		to normal operation and various management events.


NAME		ip-initial-default-gateway-2
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Initial Default Gateway 2
SNMP NAME	ncdIpInitDfltGatewy2
SNMP PATH	ncdIp 4
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the secondary default IP gateway to
		be used initially in the IP routing table.
		The IP routing table can change over time due
		to normal operation and various management events.


NAME		ip-packet-fragmentations-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Fragmentations Completed
SNMP NAME	ipFragOKs
SNMP PATH	ip 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP datagrams that have been
		successfully fragmented at this entity.


NAME		ip-packet-fragmentations-not-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Fragmentations Not Completed
SNMP NAME	ipFragFails
SNMP PATH	ip 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP datagrams that have been
		discarded because they needed to be fragmented at
		this entity but could not be, e.g., because their
		Don't Fragment flag was set.


NAME		ip-packet-fragments-created
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Fragments Created
SNMP NAME	ipFragCreates
SNMP PATH	ip 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP datagram fragments that have
		been generated as a result of fragmentation at
		this entity.


NAME		ip-packet-reassemblies-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Reassemblies Completed
SNMP NAME	ipReasmOKs
SNMP PATH	ip 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP datagrams successfully re-assembled.


NAME		ip-packet-reassemblies-not-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Reassemblies Not Completed
SNMP NAME	ipReasmFails
SNMP PATH	ip 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of failures detected by the IP re-
		assembly algorithm (for whatever reason: timed
		out, errors, etc).


NAME		ip-packet-reassemblies-required
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Reassemblies Required
SNMP NAME	ipReasmReqds
SNMP PATH	ip 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP fragments received which needed
		to be reassembled at this entity.


NAME		ip-packet-reassembly-timeout
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Reassembly Timeout
SNMP NAME	ipReasmTimeout
SNMP PATH	ip 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The maximum number of seconds which received
		fragments are held while they are awaiting
		reassembly at this entity.


NAME		ip-packet-transmission-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Transmission Requests
SNMP NAME	ipOutRequests
SNMP PATH	ip 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of IP datagrams which local IP
		user-protocols (including ICMP) supplied to IP in
		requests for transmission.  Note that this counter
		does not include any datagrams counted in
		ipForwDatagrams.


NAME		ip-packet-transmission-requests-discarded
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Transmission Requests Discarded
SNMP NAME	ipOutDiscards
SNMP PATH	ip 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of output IP datagrams for which no
		problem was encountered to prevent their
		transmission to their destination, but which were
		discarded (e.g., for lack of buffer space).  Note
		that this counter would include datagrams counted
		in Packets Forwarded if any such packets met this
		(discretionary) discard criterion.


NAME		ip-packet-transmission-requests-without-routes
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packet Transmission Requests without Routes
SNMP NAME	ipOutNoRoutes
SNMP PATH	ip 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of IP datagrams discarded because no
		route could be found to transmit them to their
		destination.  Note that this counter includes any
		packets counted in Packets Forwarded which meet this
		`no-route' criterion.  Note that this includes any
		datagrams which a host cannot route because all of
		its default gateways are down.


NAME		ip-packets-forwarded
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packets Forwarded
SNMP NAME	ipForwDatagrams
SNMP PATH	ip 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of input datagrams for which this
		entity was not their final IP destination, as a
		result of which an attempt was made to find a
		route to forward them to that final destination.
		In entities which do not act as IP Gateways, this
		counter will include only those packets which were
		Source-Routed via this entity, and the Source-
		Route option processing was successful.


NAME		ip-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packets Received
SNMP NAME	ipInReceives
SNMP PATH	ip 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of input datagrams received from
		interfaces, including those received in error.


NAME		ip-packets-received-and-delivered
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Received Packets Delivered
SNMP NAME	ipInDiscards
SNMP PATH	ip 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of input datagrams successfully
		delivered to IP user-protocols (including ICMP).


NAME		ip-packets-received-and-discarded
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Received Packets Discarded
SNMP NAME	ipInDiscards
SNMP PATH	ip 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of input IP datagrams for which no
		problems were encountered to prevent their
		continued processing, but which were discarded
		(e.g., for lack of buffer space).  Note that this
		counter does not include any datagrams discarded
		while awaiting re-assembly.


NAME		ip-packets-received-with-errors-in-ip-header
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packets Received with Errors in IP Header
SNMP NAME	ipInHdrErrors
SNMP PATH	ip 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of input datagrams discarded due to
		errors in their IP headers, including bad
		checksums, version number mismatch, other format
		errors, time-to-live exceeded, errors discovered
		in processing their IP options, etc.


NAME		ip-packets-received-with-incorrect-address
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packets Received with Incorrect Address
SNMP NAME	ipInAddrErrors
SNMP PATH	ip 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of input datagrams discarded because
		the IP address in their IP header's destination
		field was not a valid address to be received at
		this entity.  This count includes invalid
		addresses (e.g., 0.0.0.0) and addresses of
		unsupported Classes (e.g., Class E).  For entities
		which are not IP Gateways and therefore do not
		forward datagrams (read all NCD's), this counter
		includes datagrams discarded because the destination
		address was not a local address.


NAME		ip-packets-received-with-unknown-protocols
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  IP=>Packets Received with Unknown Protocols
SNMP NAME	ipInUnknownProtos
SNMP PATH	ip 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of locally-addressed datagrams
		received successfully but discarded because of an
		unknown or unsupported protocol.


NAME		ip-respond-to-broadcast-icmp
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Respond to Broadcast ICMP
SNMP NAME	ncdIpRspToBcastIcmp
SNMP PATH	ncdIp 10
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the NCD should responsd to ICMP
		request messages that were sent to an IP broadcast
		address.


NAME		ip-routing-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Routing Table
SNMP NAME	ipRouteTable
SNMP PATH	ip 21
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP routing table.


BEGIN TABLE ROW ENTRIES

NAME		destination
SNMP NAME	ipRouteDest
SNMP PATH	ipRouteTable 1
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The destination IP address of this route.  An
		entry with a value of 0.0.0.0 is considered a
		default route.  Multiple routes to a single
		destination can appear in the table.


NAME		gateway
SNMP NAME	ipRouteNextHop
SNMP PATH	ipRouteTable 7
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The IP address of the next hop of this route.
		(In the case of a route bound to an interface
		which is realized via a broadcast media, the value
		of this field is the agent's IP address on that
		interface.)


NAME		preference
SNMP NAME	ipRouteMetric1
SNMP PATH	ipRouteTable 3
TYPE		INTEGER
MIN		-2147483648
DEFAULT		0
MAX		2147483647
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a value for determining which route
		is preferred when there are multiple routes
		to a particular destination. The ICMP router
		discovery messages will convey this information
		dynamically, otherwise the values are statically
		configured by network administration.


NAME		type
SNMP NAME	ipRouteType
SNMP PATH	ipRouteTable 8
TYPE		CHOICE
CHOICES		{ dynamic static }
DEFAULT		static
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the route can be automatically
		deleted if the unit detects failures using the route.


NAME		creation-method
SNMP NAME	ipRouteProto
SNMP PATH	ipRouteTable 9
TYPE		CHOICE
CHOICES		{ snmp icmp local proxy-arp }
DEFAULT		snmp
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the method by which the route was
		created.


NAME		birth
SNMP NAME	ipRouteAge
SNMP PATH	ipRouteTable 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies when the route was created. The
		time value is relative to the unit's boot
		in seconds.


NAME		time-to-live
SNMP NAME	ipRouteMetric5
SNMP PATH	ipRouteTable 12
TYPE		INTEGER
MIN		-1
DEFAULT		-1
MAX		2147483647
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how much time (in seconds) remains
		before the route will be automatically deleted.
		This information is conveyed in the ICMP router
		discovery messages. A value of -1 indicates
		that the route should not be automatically
		deleted.


NAME		destination-type
SNMP NAME	ncdIpDestType
SNMP PATH	ipRouteTable 12
TYPE		CHOICE
CHOICES		{ network host }
DEFAULT		network
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the route has a destination
		of a host or a network. Most routes are network
		routes, the exceptions being proxy arp routes,
		and the routes used for SLIP connections.


NAME		route-mask
SNMP NAME	ipRouteMask
SNMP PATH	ipRouteTable 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the mask to be logical-ANDed with the
		destination address before being compared to the
		value in the gateway field.


NAME		interface-index
SNMP NAME	ipRouteIfIndex
SNMP PATH	ipRouteTable 2
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		1
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Index that identifies the interface of this route


NAME		metric-2
SNMP NAME	ipRouteMetric2
SNMP PATH	ipRouteTable 4
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		1
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Alternative routing metric not currently used


NAME		metric-3
SNMP NAME	ipRouteMetric3
SNMP PATH	ipRouteTable 5
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		1
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Alternative routing metric not currently used


NAME		metric-4
SNMP NAME	ipRouteMetric4
SNMP PATH	ipRouteTable 6
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		1
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Alternative routing metric not currently used


END TABLE ROW ENTRIES

NAME		ip-subnet-mask
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Subnet Mask
TYPE		INTEGER
MIN		0
DEFAULT		4294967040
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the IP subnet mask that is used to
		determine which portion of the unit's IP address
		corresponds to the network number and which
		portion to the host number.


NAME		ip-use-address-discovery
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Use Address Discovery
SNMP NAME	ncdIpDynamicAddressDiscovery
SNMP PATH	ncdIp 5
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that IP addresses supplied via BOOTP
		should be used, if available.


NAME		ip-use-proxy-arp
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Use Proxy Arp
SNMP NAME	ncdIpUseProxyArp
SNMP PATH	ncdIp 6
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies that proxy arp should be used to
		resolve routes to hosts for which there are
		no routes in the IP routing table. Note that
		using default gateways overrides any use of
		proxy arp.


NAME		ip-use-router-discovery
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Use Router Discovery
SNMP NAME	ncdIpUseRouterDiscovery
SNMP PATH	ncdIp 7
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies that the unit should modify its
		IP routing table based on the receipt of
		ICMP router discovery messages as detailed
		in RFC 1256.


NAME		ip-use-router-solicit
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  IP=>Use Router Solicit
SNMP NAME	ncdIpUseRouterDiscoverySolicit
SNMP PATH	ncdIp 8
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the unit should send ICMP
		router discovery solicitation messages at
		boot time as detailed in RFC 1256.



GROUP lat

NAME		lat-circuit-flush-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Circuit Flush Timeout
SNMP NAME	ncdLatCircuitFlushTimeout
SNMP PATH	ncdLat 2
TYPE		INTEGER
MIN		0
DEFAULT		80
MAX		2000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in milliseconds) during which input
		characters should be queued before the unit flushes
		queued data by sending a LAT packet to the host.


NAME		lat-connect-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Connect Timeout
SNMP NAME	ncdLatConnectTimeout
SNMP PATH	ncdLat 1
TYPE		INTEGER
MIN		1
DEFAULT		20
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) that must elapse
		between a LAT connection attempt and a lack of
		response for a failure situation to be declared.


NAME		lat-keepalive-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Keepalive Timeout
SNMP NAME	ncdLatKeepaliveTimeout
SNMP PATH	ncdLat 5
TYPE		INTEGER
MIN		0
DEFAULT		20
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) of inactivity on
		an established LAT connection before a LAT keepalive
		packet is sent.


NAME		lat-retransmission-limit
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Retransmission Limit
SNMP NAME	ncdLatRetransLimit
SNMP PATH	ncdLat 4
TYPE		INTEGER
MIN		4
DEFAULT		8
MAX		120
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of times a LAT packet is
		to be retransmitted before the connection is
		considered to have failed.


NAME		lat-retransmission-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Retransmission Timeout
SNMP NAME	ncdLatRetransTimeout
SNMP PATH	ncdLat 3
TYPE		INTEGER
MIN		100
DEFAULT		2000
MAX		60000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in milliseconds) between consecutive
		retransmissions of LAT data packets on an established
		connection.


NAME		lat-service-directory-max-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Service Directory Max Size
SNMP NAME	ncdLatMaxDirEntries
SNMP PATH	ncdLat 7
TYPE		INTEGER
MIN		25
DEFAULT		100
MAX		1000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum number of entries
		in the LAT service directory.


NAME		lat-service-groups
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  LAT=>Service Groups
SNMP NAME	ncdLatGroupCodes
SNMP PATH	ncdLat 6
TYPE		STRING
DEFAULT		0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the LAT service groups from which service
		advertisements will be added to the LAT service
		directory.



GROUP login

NAME		login-default-hosts
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Default Hosts
SNMP NAME	ncdLoginDfltHostsTable
SNMP PATH	ncdLogin 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default list of hosts to present
		to the user in the login box.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdLoginDHTIndex
SNMP PATH	ncdLoginDfltHostsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index into the Default Hosts Table


NAME		network
SNMP NAME	ncdLoginDHTNetwork
SNMP PATH	ncdLoginDfltHostsTable 2
TYPE		CHOICE
CHOICES		{ tcp ncdnet }
DEFAULT		tcp
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the protocol to use.


NAME		host
SNMP NAME	ncdLoginDHTHost
SNMP PATH	ncdLoginDfltHostsTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name of the login host.


NAME		description
SNMP NAME	ncdLoginDHTDescription
SNMP PATH	ncdLoginDfltHostsTable 4
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a description of the login host.


END TABLE ROW ENTRIES

NAME		login-disabled-networks
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Disabled Networks
SNMP NAME	ncdLoginDisabledNetTable
SNMP PATH	ncdLogin 3
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of networks to disable.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdLoginDNTIndex
SNMP PATH	ncdLoginDisabledNetTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index into the Disabled Networks Table


NAME		network
SNMP NAME	ncdLoginDNTName
SNMP PATH	ncdLoginDisabledNetTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name of the network
		to disable.


END TABLE ROW ENTRIES

NAME		login-dwlogin-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Login Name
SNMP NAME	ncdLoginDwLoginAccount
SNMP PATH	ncdLogin 13
TYPE		STRING
DEFAULT		NDS_LOGIN
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the login account name to use to invoke
		the VMS DECWindows login box.


NAME		login-dwlogin-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Login Password
SNMP NAME	ncdLoginDwPassword
SNMP PATH	ncdLogin 14
TYPE		STRING
DEFAULT		
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the login account password to use to invoke
		the VMS DECWindows login box.


NAME		login-restrict-host-choices
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Restrict Host Choices
SNMP NAME	ncdLoginRestrictConnectionChoices
SNMP PATH	ncdLogin 2
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the user should only be allowed
		to choose a login host specified in the default
		login hosts list.


NAME		login-window-delay-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Window Delay Time
SNMP NAME	ncdLoginAutoMapDelay
SNMP PATH	ncdLogin 4
TYPE		INTEGER
MIN		0
DEFAULT		3
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to wait before
		displaying the login window when starting from
		a command line.


NAME		login-xdm-action-on-disconnect
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>What to do when XDM disconnects
SNMP NAME	ncdXdmcpWhenFirstClientExits
SNMP PATH	ncdXdmcp 8
TYPE		CHOICE
CHOICES		{ logout prompt ignore }
DEFAULT		prompt
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what to do when the host XDM program
		disconnects from the display.


NAME		login-xdm-authentication-key
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>XDM Authentication Key
SNMP NAME	ncdAccessXdmAuthCookie
SNMP PATH	ncdAccess 1
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		AT_SESSION_STARTUP
NVRAM		YES
DESCRIPTION
		Specifies the key that must be used in conjunction
		with authorized client connection requests.


NAME		login-xdm-broadcast-wait-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>Broadcast Wait Time
SNMP NAME	ncdXdmcpBroadcastWaitTime
SNMP PATH	ncdXdmcp 5
TYPE		INTEGER
MIN		0
DEFAULT		3
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to wait for responses
		to the XDM broadcast query before displaying the results
		to the user via the login box. Any responses which
		arrive after this time are appended to the end of
		the displayed list.


NAME		login-xdm-broadcasts
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>What to do with XDMCP Broadcasts
SNMP NAME	ncdXdmcpBroadcasts
SNMP PATH	ncdXdmcp 6
TYPE		CHOICE
CHOICES		{ use-first prompt ignore }
DEFAULT		prompt
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what to do with responses to XDM broadcast
		and indirect queries.  If set to Ignore, then
		broadcasts are not sent.


NAME		login-xdm-display-class
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>XDMDisplayClass
SNMP NAME	ncdXdmcpcpDisplayClass
SNMP PATH	ncdXdmcp 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a specific XDMCP Display Class to use
		instead of the default, which is NCD-unittype.


NAME		login-xdm-indirects
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>What to do with XDMCP Indirects
SNMP NAME	ncdXdmcpIndirects
SNMP PATH	ncdXdmcp 7
TYPE		CHOICE
CHOICES		{ use-first prompt }
DEFAULT		prompt
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what to do with responses to XDM indirect
		queries.


NAME		login-xdm-keepalives-begin-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>SendKeepalivesTime
SNMP NAME	ncdXdmcpSendKeepAlivesTime
SNMP PATH	ncdXdmcp 1
TYPE		INTEGER
MIN		0
DEFAULT		3
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the length of time (in minutes) after which
		the unit is to verify that the XDM session host
		is still running by sending an XDMCP keepalive.


NAME		login-xdm-keepalives-wait-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>KeepalivesDeadTime
SNMP NAME	ncdXdmcpKeepAlivesDeadTime
SNMP PATH	ncdXdmcp 2
TYPE		INTEGER
MIN		0
DEFAULT		30
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) from the start
		of XDM dead session testing that must elapse
		without receiving a response from the login
		host to the XDM keepalive messages before a
		dead session failure situation is declared.


NAME		login-xdm-manufacturer-display-id
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Login=>XDM Manufacturer Display ID
SNMP NAME	ncdXdmcpMfgDisplayId
SNMP PATH	ncdXdmcp 4
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the XDM Manufacturer Display ID
		used for this unit.  This parameter is not settable.



GROUP ncdnet

NAME		ncdnet-address
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>NCDnet Address
SNMP NAME	ncdDecnetAddress
SNMP PATH	ncdDecnet 8
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the current NCDnet address of the unit.


NAME		ncdnet-address-at-next-boot
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>NCDnet Address At Next Boot
SNMP NAME	ncdDecnetNewAddress
SNMP PATH	ncdDecnet 9
TYPE		STRING
DEFAULT		0.0
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the NCDnet address for the unit
		the next time it is booted.
		
		Note that the current NCDnet address cannot
		be modified while the unit is running because
		this would require changing the unit's Ethernet
		address while established connections are running.
		This would lead to bizarre and unexpected behaviors
		on both the unit and the connected hosts.


NAME		ncdnet-bytes-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Bytes Received
SNMP NAME	ncdDecnetDataBytesRcv
SNMP PATH	ncdDecnet 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of bytes received over NCDnet


NAME		ncdnet-bytes-sent
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Bytes Sent
SNMP NAME	ncdDecnetDataBytesXmt
SNMP PATH	ncdDecnet 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of bytes transmitted over NCDnet


NAME		ncdnet-connect-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Connect Timeout
SNMP NAME	ncdDecnetConnectTimeout
SNMP PATH	ncdDecnet 1
TYPE		INTEGER
MIN		1
DEFAULT		120
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) that must elapse
		between a NCDnet connection attempt and a lack of a response
		for a failure situation to be declared.


NAME		ncdnet-count-circuit-down
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Count Circuit Down
SNMP NAME	ncdDecnetCntCircDown
SNMP PATH	ncdDecnet 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of circuit down events


NAME		ncdnet-data-blocks-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Data Blocks Received
SNMP NAME	ncdDecnetDataBlocksRcv
SNMP PATH	ncdDecnet 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of data messages received over NCDnet


NAME		ncdnet-data-blocks-sent
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Data Blocks Sent
SNMP NAME	ncdDecnetDataBlocksXmt
SNMP PATH	ncdDecnet 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of data messages transmitted over NCDnet


NAME		ncdnet-default-router
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Default Router
SNMP NAME	ncdDecnetDesignatedRouter
SNMP PATH	ncdDecnet 10
TYPE		STRING
DEFAULT		0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the NCDnet address or symbolic name
		of the default router on the NCDnet network.


NAME		ncdnet-hello-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Hello Packets Received
SNMP NAME	ncdDecnetHelloPacketsRcv
SNMP PATH	ncdDecnet 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of NCDnet hello packets received


NAME		ncdnet-hello-packets-sent
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Hello Packets Sent
SNMP NAME	ncdDecnetHelloPacketsXmt
SNMP PATH	ncdDecnet 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of NCDnet hello packets transmitted


NAME		ncdnet-hello-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Hello Timeout
SNMP NAME	ncdDecnetHelloTimeout
SNMP PATH	ncdDecnet 4
TYPE		INTEGER
MIN		1
DEFAULT		60
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) between successive
		transmissions of NCDnet Hello packets. As a part
		of normal operation, routers send Hello packets to
		end-node systems that specify a suggested Hello
		timeout value. NCD units will use this value if it
		is present.


NAME		ncdnet-inbound-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Inbound Errors
SNMP NAME	ncdDecnetInErrs
SNMP PATH	ncdDecnet 20
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of NCDnet receive errors


NAME		ncdnet-keepalive-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Keepalive Timeout
SNMP NAME	ncdDecnetKeepaliveTimeout
SNMP PATH	ncdDecnet 3
TYPE		INTEGER
MIN		1
DEFAULT		60
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) of inactivity
		on an established NCDnet connection before an
		NCDnet keepalive packet is sent.


NAME		ncdnet-mop-allow-reset
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Allow MOP Reset
SNMP NAME	ncdDecnetMopResetEnabled
SNMP PATH	ncdDecnet 12
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the unit should allow remote reboot via MOP.


NAME		ncdnet-mop-identify-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>MOP Identify Timeout
SNMP NAME	ncdDecnetMopIdTimeout
SNMP PATH	ncdDecnet 6
TYPE		INTEGER
MIN		1
DEFAULT		300
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) between successive
		transmissions of NCDnet MOP identify packets.


NAME		ncdnet-mop-reset-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>MOP Reset Password
SNMP NAME	ncdAccessMopResetPasswd
SNMP PATH	ncdAccess 23
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the password that must be contained in the MOP
		reset packet. Note that this value must be composed of 16
		hexadecimal digits.


NAME		ncdnet-name-bad-name-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Bad Name Errors
SNMP NAME	ncdDnetNameResolverBadNameErrs
SNMP PATH	ncdDnetNameResolver 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of 'Bad Name' errors returned by the
		NCDnet name servers for name requests. This indicates
		a badly formed name.


NAME		ncdnet-name-cache-hits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Name Cache Hits
SNMP NAME	ncdDnetNameResolverCacheHits
SNMP PATH	ncdDnetNameResolver 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the answer
		was found in the local NCDnet name cache.


NAME		ncdnet-name-cache-max-lifetime
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet Name Service=>Name Cache Max Lifetime
SNMP NAME	ncdDnetNameResolverNameCacheMaxTimeout
SNMP PATH	ncdDnetNameResolver 13
TYPE		INTEGER
MIN		0
DEFAULT		1800
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of time (in seconds) that a
		NCDnet name service entry should be used before it
		is automatically deleted.


NAME		ncdnet-name-cache-max-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet Name Service=>Name Cache Max Size
SNMP NAME	ncdDnetNameResolverNameCacheMaxSize
SNMP PATH	ncdDnetNameResolver 12
TYPE		INTEGER
MIN		0
DEFAULT		32
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum number of entries in the NCDnet
		name cache.


NAME		ncdnet-name-cache-overflows
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Name Cache Overflows
SNMP NAME	ncdDnetNameResolverCacheOverflows
SNMP PATH	ncdDnetNameResolver 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times a valid entry in the local NCDNet name cache
		had to be deleted to make room for a new entry.


NAME		ncdnet-name-local-cache
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet Name Service=>Local Name Cache
SNMP NAME	ncdDnetNameResolverNameCacheTable
SNMP PATH	ncdDnetNameResolver 14
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet name service cache.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdDnetNameResolverIndex
SNMP PATH	ncdDnetNameResolverNameCacheTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index to the NCDnet Name Table


NAME		name
SNMP NAME	ncdDnetNameResolverName
SNMP PATH	ncdDnetNameResolverNameCacheTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the symbolic name of the host.


NAME		address
SNMP NAME	ncdDnetNameResolverAddress
SNMP PATH	ncdDnetNameResolverNameCacheTable 3
TYPE		STRING
DEFAULT		0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet address of the host.


NAME		lifetime
SNMP NAME	ncdDnetNameResolverExpTime
SNMP PATH	ncdDnetNameResolverNameCacheTable 4
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the time (relative to the unit boot time
		in seconds) at which the entry will become invalid.


END TABLE ROW ENTRIES

NAME		ncdnet-name-memory-allocation-failures
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Memory Allocation Failures
SNMP NAME	ncdDnetNameResolverNoMemErrs
SNMP PATH	ncdDnetNameResolver 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the NCDnet name resolver
		was unable to allocated required memory.


NAME		ncdnet-name-no-server-responses
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>No Server Responses
SNMP NAME	ncdDnetNameResolverNoRspErrs
SNMP PATH	ncdDnetNameResolver 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times no response was received from a
		NCDnet name server.


NAME		ncdnet-name-no-such-name-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>No Such Name Errors
SNMP NAME	ncdDnetNameResolverNoNameErrs
SNMP PATH	ncdDnetNameResolver 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of 'No Such Name' errors returned by the
		NCDnet name servers for name requests.


NAME		ncdnet-name-numerical-addresses
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Numerical Addresses
SNMP NAME	ncdDnetNameResolverNumericalAddrs
SNMP PATH	ncdDnetNameResolver 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the NCDnet name was
		in numerical format, e.g. 1.17.


NAME		ncdnet-name-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Name Requests
SNMP NAME	ncdDnetNameResolverRequests
SNMP PATH	ncdDnetNameResolver 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the NCDnet name resolver
		was invoked.


NAME		ncdnet-name-server-hits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Name Server Hits
SNMP NAME	ncdDnetNameResolverServerHits
SNMP PATH	ncdDnetNameResolver 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the answer
		was found by consulting the NCDnet name servers.


NAME		ncdnet-name-server-response-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>Name Server Response Errors
SNMP NAME	ncdDnetNameResolverRspErrs
SNMP PATH	ncdDnetNameResolver 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of badly formed responses returned by the
		NCDnet name servers for name requests.


NAME		ncdnet-name-server-transaction-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet Name Service=>Name Server Transaction Timeout
SNMP NAME	ncdDnetNameResolverTransactTimeout
SNMP PATH	ncdDnetNameResolver 15
TYPE		INTEGER
MIN		1
DEFAULT		10
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to attempt
		an NCDnet name service request before a failure
		situation is declared.


NAME		ncdnet-name-servers
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet Name Service=>Name Servers
SNMP NAME	ncdDnetNameResolverServersTable
SNMP PATH	ncdDnetNameResolver 16
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet name cache.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdDnetNameResolverServerIndex
SNMP PATH	ncdDnetNameResolverServersTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index into the NCDnet Name Servers Table


NAME		server
SNMP NAME	ncdDnetNameResolverServer
SNMP PATH	ncdDnetNameResolverServersTable 2
TYPE		STRING
DEFAULT		0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet address of the name server.


END TABLE ROW ENTRIES

NAME		ncdnet-name-system-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet Name Service=>System Errors
SNMP NAME	ncdDnetNameResolverSysErrs
SNMP PATH	ncdDnetNameResolver 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the NCDnet name resolver
		encountered an general system error.


NAME		ncdnet-node-address
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Node Address
SNMP NAME	ncdDecnetAddress
SNMP PATH	ncdDecnet 23
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the current NCDnet address of the unit.


NAME		ncdnet-outbound-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Outbound Errors
SNMP NAME	ncdDecnetOutErrs
SNMP PATH	ncdDecnet 21
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of NCDnet transmit errors


NAME		ncdnet-retransmission-limit
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Retransmission Limit
SNMP NAME	ncdDecnetRetransLimit
SNMP PATH	ncdDecnet 2
TYPE		INTEGER
MIN		1
DEFAULT		10
MAX		32767
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of times NCDnet should
		retransmit data on an established connection
		before a failure situation is declared.


NAME		ncdnet-router-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>Router Timeout
SNMP NAME	ncdDecnetRouterTimeout
SNMP PATH	ncdDecnet 5
TYPE		INTEGER
MIN		1
DEFAULT		60
MAX		32767
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) after which
		a Router Hello message is received that the
		sending router is used as the default router.


NAME		ncdnet-seconds-since-zeroed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NCDnet=>Seconds Since Zeroed
SNMP NAME	ncdDecnetLastZeroTime
SNMP PATH	ncdDecnet 22
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the number of seconds since the NCDnet stats
		were last reset to zero


NAME		ncdnet-user-account-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  NCDnet=>User Account Name
SNMP NAME	ncdDecnetDnetUserName
SNMP PATH	ncdDecnet 11
TYPE		STRING
DEFAULT		NCD_NDS
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the account name used in NCDnet
		connection requests. This is used by the peer
		to map to a proxy or default account.



GROUP net

NAME		net-arp-table-entry-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>ARP Table Entry Buffers
SNMP NAME	ncdMbufATTable
SNMP PATH	ncdMbuf 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing ARP table entries.


NAME		net-available-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Available Buffers
SNMP NAME	ncdMbufAvail
SNMP PATH	ncdMbuf 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers which are unallocated.


NAME		net-available-cluster-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Available Cluster Buffers
SNMP NAME	ncdMbufClusterAvail
SNMP PATH	ncdMbuf 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of large contiguous network buffers
		which are unallocated.


NAME		net-buffer-not-available-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Buffer Not Available Errors
SNMP NAME	ncdMbufDrops
SNMP PATH	ncdMbuf 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the networking code was unable to
		allocate a network buffer, and initiated error recovery
		procedures due to this failure.


NAME		net-buffer-waits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Buffer Waits
SNMP NAME	ncdMbufWaits
SNMP PATH	ncdMbuf 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the networking code had to block waiting
		for network buffers to become available.


NAME		net-connection-control-structure-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Connection Control Structure Buffers
SNMP NAME	ncdMbufConnCtrlStructs
SNMP PATH	ncdMbuf 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing connection control structures.


NAME		net-connection-name-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Connection Name Buffers
SNMP NAME	ncdMbufConnNames
SNMP PATH	ncdMbuf 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing connection names.


NAME		net-connection-option-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Connection Option Buffers
SNMP NAME	ncdMbufConnOptions
SNMP PATH	ncdMbuf 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing connection options.


NAME		net-ethernet-snap-encapsulation
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Network Interfaces=>Ethernet SNAP Encapsulation
SNMP NAME	ncdEtherUseSNAPEncap
SNMP PATH	ncdEther 11
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		For most networks, this field should be FALSE which
		will cause Ethernet packets to be sent in the
		common, original encapsulation for Ethernet.
		However for a few networks Ethernet packets are
		sent using SNAP (IEEE 802.2 LLC) encapsulation.
		Setting this parameter to TRUE causes the NCD to send
		Ethernet packets in this form.
		
		NOTE: This parameter effects the unit's fundamental
		ability to communicate with other stations on the
		network and should only be enabled by an administrator
		knowledgable about the technical details of the
		network.


NAME		net-interface-address-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Interface Address Buffers
SNMP NAME	ncdMbufInterfaceAddr
SNMP PATH	ncdMbuf 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated to storing network
		interface address information.


NAME		net-interfaces-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Interfaces=>Interfaces Table
SNMP NAME	ifTable
SNMP PATH	if 2
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The table of network interfaces.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ifIndex
SNMP PATH	ifTable 1
TYPE		INTEGER
MIN		1
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A unique value for each interface.  Its value
		ranges between 1 and the value of Number of
		Interfaces.  The value for each interface remains
		constant.


NAME		description
SNMP NAME	ifDescr
SNMP PATH	ifTable 2
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A textual string containing information about the
		interface.


NAME		type
SNMP NAME	ifType
SNMP PATH	ifTable 3
TYPE		CHOICE
CHOICES		{ ethernet slip ppp token-ring software-loopback }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The type of interface, distinguished according to
		the physical/link protocol(s) immediately `below'
		the network layer in the protocol stack.


NAME		maximum-transmission-unit
SNMP NAME	ifMtu
SNMP PATH	ifTable 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The size of the largest datagram which can be
		sent/received on the interface, specified in
		octets.  For interfaces that are used for
		transmitting network datagrams, this is the size
		of the largest network datagram that can be sent
		on the interface.


NAME		speed
SNMP NAME	ifSpeed
SNMP PATH	ifTable 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		An estimate of the interface's current bandwidth
		in bits per second.  For interfaces which do not
		vary in bandwidth or for those where no accurate
		estimation can be made, this object should contain
		the nominal bandwidth.


NAME		physical-address
SNMP NAME	ifPhysAddress
SNMP PATH	ifTable 6
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The interface's address at the protocol layer
		immediately `below' the network layer in the
		protocol stack.  For interfaces which do not have
		such an address (e.g., a serial line), this object
		should contain an octet string of zero length.


NAME		administrative-status
SNMP NAME	ifAdminStatus
SNMP PATH	ifTable 7
TYPE		CHOICE
CHOICES		{ up down testing }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The desired state of the interface.  The
		testing state indicates that no operational
		packets can be passed.


NAME		operational-status
SNMP NAME	ifOperStatus
SNMP PATH	ifTable 8
TYPE		CHOICE
CHOICES		{ up down testing }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The current operational state of the interface.
		The testing state indicates that no operational
		packets can be passed.


NAME		last-administrative-change
SNMP NAME	ifLastChange
SNMP PATH	ifTable 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The time (in seconds relative to unit boot)
		at which the interface entered its current
		operational state.  If the current state was
		entered prior to the last re-initialization
		of the local network management subsystem,
		then this object contains a zero value.


NAME		bytes-received
SNMP NAME	ifInOctets
SNMP PATH	ifTable 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of octets received on the
		interface, including framing characters.


NAME		unicast-packets-received
SNMP NAME	ifInUcastPkts
SNMP PATH	ifTable 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of subnetwork-unicast packets
		delivered to a higher-layer protocol.


NAME		multicast-packets-received
SNMP NAME	ifInNUcastPkts
SNMP PATH	ifTable 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of non-unicast (i.e., subnetwork-
		broadcast or subnetwork-multicast) packets
		delivered to a higher-layer protocol.


NAME		received-packets-discarded
SNMP NAME	ifInDiscards
SNMP PATH	ifTable 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of inbound packets which were chosen
		to be discarded even though no errors had been
		detected to prevent their being deliverable to a
		higher-layer protocol.  One possible reason for
		discarding such a packet could be to free up
		buffer space.


NAME		packets-received-with-errors
SNMP NAME	ifInErrors
SNMP PATH	ifTable 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of inbound packets that contained
		errors preventing them from being deliverable to a
		higher-layer protocol.


NAME		packets-received-with-unknown-protocols
SNMP NAME	ifInUnknownProtos
SNMP PATH	ifTable 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of packets received via the interface
		which were discarded because of an unknown or
		unsupported protocol.


NAME		bytes-transmitted
SNMP NAME	ifOutOctets
SNMP PATH	ifTable 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of octets transmitted out of the
		interface, including framing characters.


NAME		unicast-packets-transmitted
SNMP NAME	ifOutUcastPkts
SNMP PATH	ifTable 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of packets that higher-level
		protocols requested be transmitted to a
		subnetwork-unicast address, including those that
		were discarded or not sent.


NAME		multicast-packets-transmitted
SNMP NAME	ifOutNUcastPkts
SNMP PATH	ifTable 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of packets that higher-level
		protocols requested be transmitted to a non-
		unicast (i.e., a subnetwork-broadcast or
		subnetwork-multicast) address, including those
		that were discarded or not sent.


NAME		packets-discarded-on-transmission
SNMP NAME	ifOutDiscards
SNMP PATH	ifTable 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of outbound packets which were chosen
		to be discarded even though no errors had been
		detected to prevent their being transmitted.  One
		possible reason for discarding such a packet could
		be to free up buffer space.


NAME		errors-on-packet-transmission
SNMP NAME	ifOutErrors
SNMP PATH	ifTable 20
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of outbound packets that could not be
		transmitted because of errors.


NAME		packets-waiting-to-be-transmitted
SNMP NAME	ifOutQLen
SNMP PATH	ifTable 21
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The length of the output packet queue (in packets).


END TABLE ROW ENTRIES

NAME		net-number-of-interfaces
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Interfaces=>Number of Interfaces
SNMP NAME	ifNumber
SNMP PATH	if 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network interfaces (regardless of
		their current state) present on this system.


NAME		net-packet-data-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Packet Data Buffers
SNMP NAME	ncdMbufPacketDatas
SNMP PATH	ncdMbuf 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing user data within the protocol stacks.


NAME		net-packet-fragment-reassembly-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Packet Fragment Reassembly Buffers
SNMP NAME	ncdMbufFrags
SNMP PATH	ncdMbuf 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing IP packet fragments for reassembly.


NAME		net-packet-header-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Packet Header Buffers
SNMP NAME	ncdMbufPacketHeaders
SNMP PATH	ncdMbuf 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing protocol header information.


NAME		net-protocol-control-structure-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Protocol Control Structure Buffers
SNMP NAME	ncdMbufProtoCtrlStructs
SNMP PATH	ncdMbuf 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers allocated
		to storing protocol control structures.


NAME		net-reserved-data-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Reserved Data Buffers
SNMP NAME	ncdMbufReserved
SNMP PATH	ncdMbuf 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of network buffers that are reserved, but as yet
		unallocated, for storing user data within the protocol stacks.


NAME		net-token-ring-speed
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Network Interfaces=>Token Ring Speed
SNMP NAME	ncdTokenRingSpeed
SNMP PATH	ncdTokenRing 1
TYPE		CHOICE
CHOICES		{ 4-mbit 16-mbit }
DEFAULT		4-mbit
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The speed at which to run the token ring interface (if present).
		Note that at boot the unit will attempt to automatically
		configure itself to run at the correct ring speed. It will
		first attempt to enter the ring at the speed described by this
		parameter. If that fails the unit will try the other speed, and
		adjust this parameter to the new speed so that subsequent boots
		occur more rapidly.


NAME		net-total-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Total Buffers
SNMP NAME	ncdMbufTotal
SNMP PATH	ncdMbuf 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of network buffers that currently
		exist in the unit.


NAME		net-total-cluster-buffers
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Network Buffers=>Total Cluster Buffers
SNMP NAME	ncdMbufClusterTotal
SNMP PATH	ncdMbuf 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of large contiguous network buffers
		that currently exist in the unit.



GROUP nfs

NAME		nfs-directory-contents-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Directory Contents Requests
SNMP NAME	ncdNfsClientReadDirs
SNMP PATH	ncdNfs 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Read Directory operations requested by
		the NFS client.


NAME		nfs-directory-create-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Directory Create Requests
SNMP NAME	ncdNfsClientMakeDirs
SNMP PATH	ncdNfs 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Create Directory operations requested by
		the NFS client.


NAME		nfs-directory-remove-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Directory Remove Requests
SNMP NAME	ncdNfsClientRemoveDirs
SNMP PATH	ncdNfs 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Remove Directory operations requested by
		the NFS client.


NAME		nfs-file-create-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>File Create Requests
SNMP NAME	ncdNfsClientCreates
SNMP PATH	ncdNfs 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS File Create operations requested by
		the NFS client.


NAME		nfs-file-remove-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>File Remove Requests
SNMP NAME	ncdNfsClientRemoves
SNMP PATH	ncdNfs 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS File Remove operations requested by
		the NFS client.


NAME		nfs-file-rename-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>File Rename Requests
SNMP NAME	ncdNfsClientRenames
SNMP PATH	ncdNfs 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS File Rename operations requested by
		the NFS client.


NAME		nfs-get-attributes-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Get Attributes Requests
SNMP NAME	ncdNfsClientGetAttributes
SNMP PATH	ncdNfs 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Get Attribute operations requested by
		the NFS client.


NAME		nfs-get-file-system-stats-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Get File System Stats Requests
SNMP NAME	ncdNfsClientFileSysStats
SNMP PATH	ncdNfs 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Stat File System operations requested by
		the NFS client.


NAME		nfs-get-root-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Get Root Requests
SNMP NAME	ncdNfsClientGetRoots
SNMP PATH	ncdNfs 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Get File System Root operations
		requested by the NFS client.


NAME		nfs-link-create-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Link Create Requests
SNMP NAME	ncdNfsClientCreateLinks
SNMP PATH	ncdNfs 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Create Link operations requested by
		the NFS client.


NAME		nfs-null-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Null Requests
SNMP NAME	ncdNfsClientNulls
SNMP PATH	ncdNfs 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Null operations requested by the
		NFS client.


NAME		nfs-path-lookup-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Path Lookup Requests
SNMP NAME	ncdNfsClientLookups
SNMP PATH	ncdNfs 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS File Name Component Lookup
		operations requested by the NFS client.


NAME		nfs-read-data-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Read Data Requests
SNMP NAME	ncdNfsClientReads
SNMP PATH	ncdNfs 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Read operations requested by the NFS client.


NAME		nfs-read-symlink-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Read Symlink Requests
SNMP NAME	ncdNfsClientReadLinks
SNMP PATH	ncdNfs 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Read Link operations requested
		by the NFS client.


NAME		nfs-set-attributes-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Set Attributes Requests
SNMP NAME	ncdNfsClientSetAttributes
SNMP PATH	ncdNfs 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Set Attribute operations requested by
		the NFS client.


NAME		nfs-symlink-create-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Symlink Create Requests
SNMP NAME	ncdNfsClientCreateSymlinks
SNMP PATH	ncdNfs 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Create Symbolic Link operations
		requested by the NFS client.


NAME		nfs-write-data-cache-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Write Data Cache Requests
SNMP NAME	ncdNfsClientWriteCaches
SNMP PATH	ncdNfs 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Write Cache operations requested by
		the NFS client.


NAME		nfs-write-data-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  NFS=>Write Data Requests
SNMP NAME	ncdNfsClientWrites
SNMP PATH	ncdNfs 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of NFS Write operations requested by the NFS
		client.



GROUP parallel

NAME		parallel-daemons-lat-service-passwords
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Parallel Daemon LAT Service Passwords
SNMP NAME	ncdAccessParalleldLatPasswdTable
SNMP PATH	ncdAccess 36
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the LAT service passwords required to
		gain access to the parallel port daemon using LAT.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessParalleldLPTIndex
SNMP PATH	ncdAccessParalleldLatPasswdTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Parallel Daemons LAT Passwds Table


NAME		port-number
SNMP NAME	ncdAccessParalleldLPTPortNumber
SNMP PATH	ncdAccessParalleldLatPasswdTable 2
TYPE		INTEGER
MIN		1
MAX		1
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the parallel port.


NAME		password
SNMP NAME	ncdAccessParalleldLPTPassword
SNMP PATH	ncdAccessParalleldLatPasswdTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the LAT service password.


END TABLE ROW ENTRIES

NAME		parallel-daemons-statistics-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Parallel Daemons=>Parallel Daemon Statistics Table
SNMP NAME	ncdParallelDStatsTbl
SNMP PATH	ncdParallel 2
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the table of parallel daemon statistics.


BEGIN TABLE ROW ENTRIES

NAME		port-number
SNMP NAME	ncdParallelDStatsTblPortNumber
SNMP PATH	ncdParallelDStatsTbl 1
TYPE		INTEGER
MIN		1
MAX		1
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the parallel port.


NAME		connections-accepted
SNMP NAME	ncdParallelDStatsTblConnAccepts
SNMP PATH	ncdParallelDStatsTbl 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections made to the parallel daemon.


NAME		connections-with-access-control-errors
SNMP NAME	ncdParallelDStatsTblConnBadAccesses
SNMP PATH	ncdParallelDStatsTbl 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		parallel daemon due to the remote address not being
		present in the parallel daemon's access control list.


NAME		connections-with-io-errors
SNMP NAME	ncdParallelDStatsTblConnIOErrors
SNMP PATH	ncdParallelDStatsTbl 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		parallel daemon due to the a local I/O error. This
		includes the user aborting the connection via local
		mechanisms.


NAME		connections-with-normal-completion
SNMP NAME	ncdParallelDStatsTblConnEofCloses
SNMP PATH	ncdParallelDStatsTbl 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		remote host. This is the normal mode of ending a
		connection to the parallel daemon.


END TABLE ROW ENTRIES

NAME		parallel-daemons-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Parallel=>Parallel Daemons Table
SNMP NAME	ncdParallelDTable
SNMP PATH	ncdParallel 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the table of parallel daemon parameters.


BEGIN TABLE ROW ENTRIES

NAME		parallel-daemon-table-index
SNMP NAME	ncdParallelDTableIndex
SNMP PATH	ncdParallelDTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The index into the parallel daemons table


NAME		port-number
SNMP NAME	ncdParallelDTablePortNumber
SNMP PATH	ncdParallelDTable 2
TYPE		INTEGER
MIN		1
MAX		1
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the parallel port.


NAME		use-parallel-protocol
SNMP NAME	ncdParallelDTableUseParaProt
SNMP PATH	ncdParallelDTable 3
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the parallel daemon control protocol
		should be used.  Note that this could cause some data
		loss if enabled with old host software.


NAME		tcp-port
SNMP NAME	ncdParallelDTableTCPPort
SNMP PATH	ncdParallelDTable 4
TYPE		INTEGER
MIN		1
DEFAULT		5964
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the parallel
		daemon.


NAME		ncdnet-object-name
SNMP NAME	ncdParallelDTableNCDnetObjName
SNMP PATH	ncdParallelDTable 5
TYPE		STRING
DEFAULT		PARALLELD
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the parallel
		daemon.


NAME		enable-lat-service
SNMP NAME	ncdParallelDTableEnableLAT
SNMP PATH	ncdParallelDTable 6
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies that the unit is to accept incoming 
		LAT solicit messages for a service which 
		allows access to the parallel daemon. This is used
		to support VMS print services to the unit.


NAME		lat-service-name
SNMP NAME	ncdParallelDTableLATServName
SNMP PATH	ncdParallelDTable 7
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the name of the parallel daemon LAT service.


NAME		lat-service-rating
SNMP NAME	ncdParallelDTableLATServRating
SNMP PATH	ncdParallelDTable 8
TYPE		INTEGER
MIN		0
DEFAULT		50
MAX		255
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the rating of the parallel daemon LAT service.


END TABLE ROW ENTRIES


GROUP pex

NAME		pex-max-model-clip-planes
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX=>Maximum Model Clip Planes
SNMP NAME	ncdPexSetupMaxModelClipPlanes
SNMP PATH	ncdPex 1
TYPE		INTEGER
MIN		6
DEFAULT		64
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The maximum number of half-spaces that can be defined
		for the purpose of model clipping.


NAME		pex-max-nameset-names
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX=>Maximum Nameset Names
SNMP NAME	ncdPexSetupMaxNamesetNames
SNMP PATH	ncdPex 3
TYPE		CHOICE
CHOICES		{ 64 128 256 512 1024 2048 4096 8192 16384 32768 }
DEFAULT		256
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The maximum number of NameSet names (identifiers) that
		can be defined.  This value must be a power of two.


NAME		pex-max-non-ambient-lights
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX=>Maximum Non-Ambient Lights
SNMP NAME	ncdPexSetupMaxNonAmbientLights
SNMP PATH	ncdPex 2
TYPE		INTEGER
MIN		0
DEFAULT		64
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The maximum number of non-ambient light sources that
		can be defined.


NAME		pex-monitor-reference-blue-u
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Blue u
SNMP NAME	ncdPexSetupMonRefBlueu
SNMP PATH	ncdPex 10
TYPE		FLOAT
MIN		0
DEFAULT		0.1756
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the u' CIE-chromaticity coordinate for the
		blue color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-blue-v
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Blue v
SNMP NAME	ncdPexSetupMonRefBluev
SNMP PATH	ncdPex 11
TYPE		FLOAT
MIN		0
DEFAULT		0.1785
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the v' CIE-chromaticity coordinate for the
		blue color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-blue-y
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Blue Y
SNMP NAME	ncdPexSetupMonRefBlueY
SNMP PATH	ncdPex 12
TYPE		FLOAT
MIN		0
DEFAULT		1
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the Y CIE-luminance coordinate for the
		blue color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-green-u
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Green u
SNMP NAME	ncdPexSetupMonRefGreenu
SNMP PATH	ncdPex 7
TYPE		FLOAT
MIN		0
DEFAULT		0.1169
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the u' CIE-chromaticity coordinate for the
		green color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-green-v
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Green v
SNMP NAME	ncdPexSetupMonRefGreenv
SNMP PATH	ncdPex 8
TYPE		FLOAT
MIN		0
DEFAULT		0.559
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the v' CIE-chromaticity coordinate for the
		green color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-green-y
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Green Y
SNMP NAME	ncdPexSetupMonRefGreenY
SNMP PATH	ncdPex 9
TYPE		FLOAT
MIN		0
DEFAULT		1
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the Y CIE-luminance coordinate for the
		green color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-red-u
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Red u
SNMP NAME	ncdPexSetupMonRefRedu
SNMP PATH	ncdPex 4
TYPE		FLOAT
MIN		0
DEFAULT		0.4288
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the u' CIE-chromaticity coordinate for the
		red color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-red-v
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Red v
SNMP NAME	ncdPexSetupMonRefRedv
SNMP PATH	ncdPex 5
TYPE		FLOAT
MIN		0
DEFAULT		0.5249
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the v' CIE-chromaticity coordinate for the
		red color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-red-y
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference Red Y
SNMP NAME	ncdPexSetupMonRefRedY
SNMP PATH	ncdPex 6
TYPE		FLOAT
MIN		0
DEFAULT		1
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the Y CIE-luminance coordinate for the
		red color component of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-white-u
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference White u
SNMP NAME	ncdPexSetupMonRefWhiteu
SNMP PATH	ncdPex 13
TYPE		FLOAT
MIN		0
DEFAULT		0.1884
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the u' CIE-chromaticity coordinate for the
		reference white value of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-white-v
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference White v
SNMP NAME	ncdPexSetupMonRefWhitev
SNMP PATH	ncdPex 14
TYPE		FLOAT
MIN		0
DEFAULT		0.4463
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the v' CIE-chromaticity coordinate for the
		reference white value of the the properly-adjusted
		display monitor.


NAME		pex-monitor-reference-white-y
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PEX Color=>Monitor Reference White Y
SNMP NAME	ncdPexSetupMonRefWhiteY
SNMP PATH	ncdPex 15
TYPE		FLOAT
MIN		0
DEFAULT		1
MAX		1
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the Y CIE-luminance coordinate for the
		reference white value of the the properly-adjusted
		display monitor.



GROUP ppp

NAME		ppp-interfaces-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PPP and SLIP=>PPP Interfaces Table
SNMP NAME	ncdPppIfTable
SNMP PATH	ncdPpp 2
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies PPP configuration parameters.


BEGIN TABLE ROW ENTRIES

NAME		port-number
SNMP NAME	ncdPppIfTablePortNumber
SNMP PATH	ncdPppIfTable 1
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The serial port number.


NAME		ctrl-char-map
SNMP NAME	ncdPppIfTableCtlCharMap
SNMP PATH	ncdPppIfTable 2
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Bit map specifying which control characters
		should not be sent in plain text form.  The most
		signficant bit corresponds to control character
		0x1f, the least signficant bit corresponds to
		character 0x00.  Not used for SLIP connections.


NAME		mtu
SNMP NAME	ncdPppIfTableMTU
SNMP PATH	ncdPppIfTable 3
TYPE		INTEGER
MIN		128
DEFAULT		1000
MAX		1500
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum number of bytes that should
		be sent/received in the information field of a PPP
		frame.  Not used for SLIP connections.


NAME		compress-protocol-field
SNMP NAME	ncdPppIfTableProtocolComp
SNMP PATH	ncdPppIfTable 4
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that PPP frames may be sent using
		compressed protocol fields.  Not used for
		SLIP connections.


NAME		compress-addr-ctrl-fields
SNMP NAME	ncdPppIfTableACComp
SNMP PATH	ncdPppIfTable 5
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that PPP frames may be sent with
		the address and control fields compressed.
		Not used for SLIP connections.


NAME		passive-mode
SNMP NAME	ncdPppIfTablePassive
SNMP PATH	ncdPppIfTable 6
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Normally the NCD unit will attempt to initiate
		the PPP negotiation with the remote host.  If this
		option is enabled, the NCD unit will wait for
		the remote host to initiate the negotiation.
		Not used for SLIP connections.


NAME		use-old-format
SNMP NAME	ncdPppIfTableOldOptions
SNMP PATH	ncdPppIfTable 7
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The format for exchanging some configuration options
		has changed in the latest PPP RFC's (1331/1332).
		Although the NCD unit should be able to negotiate
		with older PPP implementations, it may sometimes be
		necessary to enable this feature to allow correct
		option negotiation.  Not used for SLIP connections.


END TABLE ROW ENTRIES

NAME		ppp-slip-interfaces-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  PPP and SLIP=>PPP and SLIP Interfaces Table
SNMP NAME	ncdPppSlipIfTable
SNMP PATH	ncdPpp 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies PPP and SLIP configuration parameters.


BEGIN TABLE ROW ENTRIES

NAME		port-number
SNMP NAME	ncdPppSlipIfTablePortNumber
SNMP PATH	ncdPppSlipIfTable 1
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The serial port number.


NAME		ip-address
SNMP NAME	ncdPppSlipIfTableIpAddress
SNMP PATH	ncdPppSlipIfTable 2
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP address to be used for the PPP/SLIP
		connection.  For PPP, if the address is 0.0.0.0,
		then it is expected that the IP address will be
		supplied by the remote host.


NAME		peer-ip-address
SNMP NAME	ncdPppSlipIfTablePeerIpAddress
SNMP PATH	ncdPppSlipIfTable 3
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP address of the system at the other
		end of the PPP/SLIP link.  For PPP, if the address is
		0.0.0.0, then the NCD unit will attempt to obtain
		the address from the remote host.


NAME		dflt-gateway
SNMP NAME	ncdPppSlipIfTableDfltGateway
SNMP PATH	ncdPppSlipIfTable 4
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies if the remote host should be used as a
		default gateway.


NAME		compress-headers
SNMP NAME	ncdPppSlipIfTableVJCompression
SNMP PATH	ncdPppSlipIfTable 5
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that TCP/IP packets may be sent using
		Van Jacobsen compressed TCP/IP headers.


END TABLE ROW ENTRIES


GROUP pref

NAME		pref-audio-maximum-gain
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Audio=>Maximum Gain
SNMP NAME	ncdPrefMaximumGain
SNMP PATH	ncdPref 41
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Maximum volume of an audio client.


NAME		pref-bell-duration
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Bell=>Bell Duration
SNMP NAME	ncdPrefBellDuration
SNMP PATH	ncdPref 10
TYPE		INTEGER
MIN		0
DEFAULT		100
MAX		1800
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies bell duration in milliseconds.


NAME		pref-bell-enable
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Bell=>Enable Bell
SNMP NAME	ncdPrefBellEnabled
SNMP PATH	ncdPref 7
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Toggles bell on and off.


NAME		pref-bell-pitch
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Bell=>Bell Pitch
SNMP NAME	ncdPrefBellPitch
SNMP PATH	ncdPref 9
TYPE		INTEGER
MIN		0
DEFAULT		800
MAX		3000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies bell pitch in Hertz  (Hz).


NAME		pref-bell-volume
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Bell=>Bell Volume
SNMP NAME	ncdPrefBellVolume
SNMP PATH	ncdPref 8
TYPE		INTEGER
MIN		0
DEFAULT		50
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the bell's base volume in percentage of max volume.


NAME		pref-compatibility-decwindows-images
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Compatibility=>Be Compatible With Old DECwindows Images
SNMP NAME	ncdPrefOldDwImageCompatibility
SNMP PATH	ncdPref 34
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether to byte swap incoming X images which
		some old DECwindows applications fail to do.


NAME		pref-compatibility-decwindows-keyboards
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Compatibility=>Be Compatible With Old DECwindows Keyboards
SNMP NAME	ncdPrefOldDwKbdCompatibility
SNMP PATH	ncdPref 33
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the right modifiers should pretend to be
		left modifiers like old DEC keyboards.


NAME		pref-compatibility-decwindows-vendor-string
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Compatibility=>Be Compatible With Old DECwindows Vendor String
SNMP NAME	ncdPrefOldDwCompatibility
SNMP PATH	ncdPref 32
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether to not to prefix the display vendor
		string with DECWINDOWS for older DECwindows applications.


NAME		pref-compatibility-permit-old-x-bugs
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Compatibility=>Permit Old X Bugs
SNMP NAME	ncdPrefPermitOldBugs
SNMP PATH	ncdPref 31
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether to bypass error checks on requests which old
		X clients don't expect to fail.


NAME		pref-console-auto-lock-idle-time
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Auto Lock Idle Time
SNMP NAME	ncdPrefConsoleAutoLockTime
SNMP PATH	ncdPref 37
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		How long the terminal should be idle  (in minutes)
		before automatically locking the screen.


NAME		pref-console-auto-logout-cancel-delay
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Auto Logout Cancel Delay
SNMP NAME	ncdPrefConsoleAutoLogoutCancelDelay
SNMP PATH	ncdPref 36
TYPE		INTEGER
MIN		0
DEFAULT		5
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		How long the terminal should wait  (in seconds)
		for the user to cancel an automatic logout.


NAME		pref-console-auto-logout-idle-time
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Auto Logout Idle Time
SNMP NAME	ncdPrefConsoleAutoLogoutIdleTime
SNMP PATH	ncdPref 35
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		How long the terminal should be idle  (in minutes)
		before automatically logging out the user.


NAME		pref-console-blank-screen-delay
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Console Blank Screen Delay
SNMP NAME	ncdPrefConsoleBlankScreenDelay
SNMP PATH	ncdPref 39
TYPE		INTEGER
MIN		0
DEFAULT		500
MAX		5000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Time (in milliseconds) to wait after selecting Blank Screen.


NAME		pref-console-key-sequence
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Console Key Sequence
SNMP NAME	ncdPrefConsoleKeyString
SNMP PATH	ncdPref 44
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		The key seqeunce used to bring up the Console.


NAME		pref-console-lock-screen-default-password
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Lock Screen Default Password
SNMP NAME	ncdPrefConsoleLockScreenPasswdDflt
SNMP PATH	ncdPref 38
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The password for the screen lock.


NAME		pref-console-show-timestamps
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Console and Utilities=>Show Console Timestamps
SNMP NAME	ncdPrefConsoleShowTimestamps
SNMP PATH	ncdPref 40
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether to display timestamps with console messages.


NAME		pref-font-extended-diagnostics
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Fonts=>Show Extended Font Diagnostics
SNMP NAME	ncdPrefFontExtendedDiagnostics
SNMP PATH	ncdPref 26
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether to report all font actions which require
		file system or network access.


NAME		pref-font-path
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Fonts=>Current Font Path
SNMP NAME	ncdPrefFontPathTable
SNMP PATH	ncdPref 27
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the current font search path.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdPrefFontPathTableIndex
SNMP PATH	ncdPrefFontPathTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Font Path Table


NAME		font-path-entry
SNMP NAME	ncdPrefFontPathTableEntry
SNMP PATH	ncdPrefFontPathTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a current font path entry in the table


END TABLE ROW ENTRIES

NAME		pref-keyboard-auto-repeat
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>Enable Keyboard Autorepeat
SNMP NAME	ncdPrefKbdAutoRepeat
SNMP PATH	ncdPref 2
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Toggles whether keys repeat.


NAME		pref-keyboard-auto-repeat-rate
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>Autorepeat Rate
SNMP NAME	ncdPrefKbdAutoRepeatRate
SNMP PATH	ncdPref 4
TYPE		INTEGER
MIN		2
DEFAULT		20
MAX		30
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Times per second that keys auto-repeat.


NAME		pref-keyboard-auto-repeat-start
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>Autorepeat Begin After
SNMP NAME	ncdPrefKdbAutoRepeatAfter
SNMP PATH	ncdPref 3
TYPE		INTEGER
MIN		0
DEFAULT		500
MAX		1000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Number of milliseconds key must be held down before it starts
		autorepeating.


NAME		pref-keyboard-function-key-style
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>Function Key Style
SNMP NAME	ncdPrefKbdFuncKeyMap
SNMP PATH	ncdPref 1
TYPE		CHOICE
CHOICES		{ vms unix }
DEFAULT		vms
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Determines how function keys should be interpreted.


NAME		pref-keyboard-keyclick-volume
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>Keyclick Volume
SNMP NAME	ncdPrefKeyClickVolume
SNMP PATH	ncdPref 5
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Volume of keyclick in percentage of maximum volume.


NAME		pref-keyboard-leds
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Keyboard=>LEDs
SNMP NAME	ncdPrefKbdLedsTable
SNMP PATH	ncdPref 6
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Describes what LEDs indicate.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdPrefLedsTableIndex
SNMP PATH	ncdPrefKbdLedsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the LED Table


NAME		led-entry
SNMP NAME	ncdPrefLedsTableEntry
SNMP PATH	ncdPrefKbdLedsTable 2
TYPE		CHOICE
CHOICES		{ x1 x2 x3 x4 net warn ctrl shift caps num mod1 mod2 mod3 mod4 mod5 }
DEFAULT		x1
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the LED values


END TABLE ROW ENTRIES

NAME		pref-mouse-acceleration
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Acceleration Ratio
SNMP NAME	ncdPrefMouseAcceration
SNMP PATH	ncdPref 12
TYPE		INTEGER
MIN		10
DEFAULT		300
MAX		1000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the percentage by which physical mouse motion
		past the mouse threshold has been passed should be multipled
		to obtain the distance traveled by the pointer cursor.  A
		value of less than 100 makes the mouse slower; a value over
		than 100 makes it faster.


NAME		pref-mouse-arrangement
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Button Arrangement
SNMP NAME	ncdPrefMouseButtonArragement
SNMP PATH	ncdPref 13
TYPE		CHOICE
CHOICES		{ right-handed left-handed }
DEFAULT		right-handed
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the mouse buttons are mapped with Button1
		at the right or left.


NAME		pref-mouse-threshold
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Threshold Distance
SNMP NAME	ncdPrefMouseThresholdDistance
SNMP PATH	ncdPref 11
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		20
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of pixels the mouse must be moved
		before the acceleration factor is applied.


NAME		pref-pex-color-clipping-method
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Color Clipping Method
SNMP NAME	ncdPrefPexColorClipMethod
SNMP PATH	ncdPrefPex 9
TYPE		CHOICE
CHOICES		{ none scale desaturate clamp }
DEFAULT		none
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how to correct over-saturated colors:
		 `None'	-- do not correct color values
		 `Scale'	-- scale the RGB components to 0-1;
				   maintains hue & saturation,
				   clips intensity
		 `Desaturate'	-- reduce color saturation (contrast);
				   maintains hue & intensity,
				   clips saturation
		 `Clamp'	-- truncate RGB components to 0-1;
				   alters hue, saturation & intensity


NAME		pref-pex-dither-flat-shaded-surface
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Dither Flat Shaded Surface
SNMP NAME	ncdPrefPexDitFlatShadedSurface
SNMP PATH	ncdPrefPex 4
TYPE		CHOICE
CHOICES		{ by-request off on }
DEFAULT		by-request
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies when to dither flat-shaded surfaces:
		 `By Request'	-- only when the client requests it
		 `Off'		-- never dither
		 `On'		-- always dither


NAME		pref-pex-dither-interpolated-surface
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Dither Interpolated Surface
SNMP NAME	ncdPrefPexDitInterpSurface
SNMP PATH	ncdPrefPex 5
TYPE		CHOICE
CHOICES		{ by-request off on }
DEFAULT		on
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies when to dither Gouraud-shaded surfaces:
		 `By Request'	-- only when the client requests it
		 `Off'		-- never dither
		 `On'		-- always dither


NAME		pref-pex-nominal-edge-width
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Nominal Edge Width
SNMP NAME	ncdPrefPexNomEdgeWidth
SNMP PATH	ncdPrefPex 2
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		64
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the `standard' width (in pixels) of edges
		of surface primitives, when such edges are displayed.


NAME		pref-pex-nominal-line-width
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Nominal Line Width
SNMP NAME	ncdPrefPexNomLinWidth
SNMP PATH	ncdPrefPex 1
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		64
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the `standard' width (in pixels) of lines
		and curves.


NAME		pref-pex-nominal-marker-size
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Nominal Marker Size
SNMP NAME	ncdPrefPexNomMarkSiz
SNMP PATH	ncdPrefPex 3
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		64
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the `standard' size (in pixels) of marker
		primitives.  A default `+' (plus) marker, for example,
		is 3 pixels wide -- a nominal marker size of two
		would make that plus marker be 6 pixels wide.  Other
		marker types (except `dot') would scale accordingly.


NAME		pref-pex-surface-interior-style
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Surface Interior Style
SNMP NAME	ncdPrefPexSurfaceInterStyle
SNMP PATH	ncdPrefPex 6
TYPE		CHOICE
CHOICES		{ by-request hollow solid empty }
DEFAULT		by-request
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how to render interiors of surfaces:
		 `By Request'	-- in the manner requested by client
		 `Hollow'	-- render all surfaces hollow
		 `Solid'	-- render all surfaces solid
		 `Empty'	-- render all surfaces empty


NAME		pref-pex-surface-interp-method
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Surface Interpolation Method
SNMP NAME	ncdPrefPexSurfaceInterpMethod
SNMP PATH	ncdPrefPex 7
TYPE		CHOICE
CHOICES		{ by-request none color }
DEFAULT		by-request
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how to shade interiors of surfaces:
		 `By Request'	-- in the manner requested by client
		 `None'	-- flat-shade all surfaces
		 `Color'	-- Gouraud-shade all surfaces


NAME		pref-pex-surface-reflect-model
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  PEX=>Surface Reflection Model
SNMP NAME	ncdPrefPexSurfaceReflectModel
SNMP PATH	ncdPrefPex 8
TYPE		CHOICE
CHOICES		{ by-request none ambient diffuse specular }
DEFAULT		by-request
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how to apply lighting effects to surfaces:
		 `By Request'	-- in the manner requested by client
		 `None'	-- do not light any surfaces
		 `Ambient'	-- use only ambient lighting
		 `Diffuse'	-- use ambient & diffuse lighting
		 `Specular'	-- use all lighting parmameters


NAME		pref-screen-background-bitmap-background
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Bitmap Background Color
SNMP NAME	ncdPrefScreenBackBitmapBackground
SNMP PATH	ncdPref 18
TYPE		STRING
DEFAULT		white
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the color to use for the background of the
		screen background bitmap.


NAME		pref-screen-background-bitmap-file
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Bitmap File
SNMP NAME	ncdPrefScreenBitmapFile
SNMP PATH	ncdPref 16
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the bitmap file to be used if the screen background
		is Bitmap.


NAME		pref-screen-background-bitmap-foreground
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Bitmap Foreground Color
SNMP NAME	ncdPrefScreenBackBitmapForeground
SNMP PATH	ncdPref 17
TYPE		STRING
DEFAULT		black
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the color to use for the foreground of the
		screen background bitmap.


NAME		pref-screen-background-color
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Solid Color
SNMP NAME	ncdPrefScreenSolidColor
SNMP PATH	ncdPref 15
TYPE		STRING
DEFAULT		#0183c6
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the solid color used if the screen background is Solid Color.


NAME		pref-screen-background-overscan
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Overscan
SNMP NAME	ncdPrefScreenOverscan
SNMP PATH	ncdPref 19
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the overscan should be white or black.


NAME		pref-screen-background-type
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Background=>Screen Background Type
SNMP NAME	ncdPrefScreenBackground
SNMP PATH	ncdPref 14
TYPE		CHOICE
CHOICES		{ default solid-color bitmap }
DEFAULT		default
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what the screen backround should look like.


NAME		pref-screensaver-bitmap-file
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Screen Saver Bitmap File
SNMP NAME	ncdPrefScreenSaverBitmapFile
SNMP PATH	ncdPref 25
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the bitmap file to use if the screen saver is using
		Bitmap mode.


NAME		pref-screensaver-enable
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Enable Screen Saver
SNMP NAME	ncdPrefScreenSaverEnabled
SNMP PATH	ncdPref 20
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the screen saver should work.


NAME		pref-screensaver-exposures
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Allow Exposures After Screen Saver
SNMP NAME	ncdPrefScreenSaverAllowExposures
SNMP PATH	ncdPref 21
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the screen saver should have clients redraw
		themselves when it restores the screen.


NAME		pref-screensaver-interval
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Change Screen Saver After
SNMP NAME	ncdPrefScreenSaverChangeAfter
SNMP PATH	ncdPref 23
TYPE		INTEGER
MIN		0
DEFAULT		60
MAX		3000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		How many seconds the screen saver waits
		before modifying its pattern.


NAME		pref-screensaver-style
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Screen Saver Style
SNMP NAME	ncdPrefScreenSaverStyle
SNMP PATH	ncdPref 24
TYPE		CHOICE
CHOICES		{ blank bitmap x-logo hardware }
DEFAULT		blank
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of screen saver image to use.


NAME		pref-screensaver-time
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Screen Saver=>Save Screen After
SNMP NAME	ncdPrefScreenSaverAfter
SNMP PATH	ncdPref 22
TYPE		INTEGER
MIN		0
DEFAULT		600
MAX		3000
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		How long the terminal needs to be idle  (in seconds)
		before the screen saver starts.


NAME		pref-sie-contrast-threshold
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>SIE Contrast Threshold
SNMP NAME	ncdPrefSIEContrast
SNMP PATH	ncdPref 43
TYPE		INTEGER
MIN		0
DEFAULT		50
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Contrast value used in SIE scaling operations.
		Applies only to Bilinear-Interp & 4x4-Area-methods.


NAME		pref-sie-sampling-method
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>SIE Sampling Method
SNMP NAME	ncdPrefSIESamplingMethod
SNMP PATH	ncdPref 42
TYPE		CHOICE
CHOICES		{ nearest-neighbor any-neighbor bilinear-interp 4x4-area }
DEFAULT		nearest-neighbor
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the SIE sampling method to use when scaling.


NAME		pref-xserver-backing-store
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>Use Backing Store
SNMP NAME	ncdPrefUseBackingStore
SNMP PATH	ncdPref 30
TYPE		CHOICE
CHOICES		{ when-mapped by-request disabled }
DEFAULT		by-request
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default backing store given to client windows.


NAME		pref-xserver-benchmark-optimizations
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>Enable Benchmark Optimizations
SNMP NAME	ncdPrefBenchmarkOptimizationsEnabled
SNMP PATH	ncdPref 28
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		When enabled, some graphics operations are optimized for
		benchmarks.


NAME		pref-xserver-current-pointing-device
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Current Pointing Device
SNMP NAME	ncdPrefCurrentPointingDevice
SNMP PATH	ncdPref 46
TYPE		CHOICE
CHOICES		{ mouse mouse-and-extension-device input-extension-device-only }
DEFAULT		mouse
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether the pointer is a mouse
		 or one of the input extension devices


NAME		pref-xserver-graphics-optimizations
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>Enable Graphics Optimizations
SNMP NAME	ncdPrefGraphicsOptimizationsEnabled
SNMP PATH	ncdPref 28
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		When enabled, some graphics operations are optimized with
		a possible loss in accuracy.


NAME		pref-xserver-screen-resolution
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  X, Graphics, and SIE=>Screen Resolution
SNMP NAME	ncdPrefScreenRes
SNMP PATH	ncdPref 29
TYPE		INTEGER
MIN		20
DEFAULT		100
MAX		300
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what the server reports for its resolution
		(in dots per inch) to X clients and the font server.


NAME		pref-xserver-touchscreen-button-press-threshold
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Button Press Threshold
SNMP NAME	ncdPrefTouchscreenButtonPressThreshold
SNMP PATH	ncdPref 47
TYPE		INTEGER
MIN		1
DEFAULT		8
MAX		15
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the relative force which the user must exert
		on the touchscreen before a button press event is generated.
		The button press threshold should be greater than the button
		release threshold


NAME		pref-xserver-touchscreen-button-release-threshold
HIDEBOX		Console=>Setup=>Change User Preferences=>
		  Pointing Devices=>Button Release Threshold
SNMP NAME	ncdPrefTouchscreenButtonReleaseThreshold
SNMP PATH	ncdPref 45
TYPE		INTEGER
MIN		1
DEFAULT		5
MAX		15
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the relative force which the user must exert
		on the touchscreen before a button release event is generated.



GROUP serial

NAME		serial-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable Serial and Parallel Access Control
SNMP NAME	ncdAccessSerialdAccessControlEnabled
SNMP PATH	ncdAccess 31
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether xhost-style access control
		is on or off for requests to connect to the
		serial or parallel port daemon.


NAME		serial-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Serial and Parallel Access Control List
SNMP NAME	ncdAccessSerialdAccessControlTable
SNMP PATH	ncdAccess 32
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list for the serial
		or parallel port daemon.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessSerialdACTIndex
SNMP PATH	ncdAccessSerialdAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Serial Access Control List


NAME		host
SNMP NAME	ncdAccessSerialdACTAddress
SNMP PATH	ncdAccessSerialdAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the serial or parallel
		port daemon.


NAME		family
SNMP NAME	ncdAccessSerialdACTFamily
SNMP PATH	ncdAccessSerialdAccessControlTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet lat }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the type of network connection for
		which this entry applies.


END TABLE ROW ENTRIES

NAME		serial-daemons-lat-service-passwords
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Serial Daemon LAT Service Passwords
SNMP NAME	ncdAccessSerialdLatPasswdTable
SNMP PATH	ncdAccess 30
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the LAT service passwords required to
		gain access to the serial port daemons using LAT.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessSerialdLPTIndex
SNMP PATH	ncdAccessSerialdLatPasswdTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Serial Daemons LAT Passwds Table


NAME		port-number
SNMP NAME	ncdAccessSerialdLPTPortNumber
SNMP PATH	ncdAccessSerialdLatPasswdTable 2
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the serial port.


NAME		password
SNMP NAME	ncdAccessSerialdLPTPassword
SNMP PATH	ncdAccessSerialdLatPasswdTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the LAT service password.


END TABLE ROW ENTRIES

NAME		serial-daemons-statistics-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Serial Daemons=>Serial Daemon Statistics Table
SNMP NAME	ncdSerialDaemonStatsTable
SNMP PATH	ncdSerialDaemon 1
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the table of serial daemon statistics.


BEGIN TABLE ROW ENTRIES

NAME		port-number
SNMP NAME	ncdSerialDaemonPortNumber
SNMP PATH	ncdSerialDaemonStatsTable 1
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the serial port.


NAME		connections-accepted
SNMP NAME	ncdSerialDaemonConnAccepts
SNMP PATH	ncdSerialDaemonStatsTable 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections made to the serial daemon.


NAME		connections-with-access-control-errors
SNMP NAME	ncdSerialDaemonConnBadAccesses
SNMP PATH	ncdSerialDaemonStatsTable 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		serial daemon due to the remote address not being
		present in the serial daemon's access control list.


NAME		connections-with-io-errors
SNMP NAME	ncdSerialDaemonConnIOErrors
SNMP PATH	ncdSerialDaemonStatsTable 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		serial daemon due to the a local I/O error. This
		includes the user aborting the connection via local
		mechanisms.


NAME		connections-with-normal-completion
SNMP NAME	ncdSerialDaemonConnEofCloses
SNMP PATH	ncdSerialDaemonStatsTable 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections that were closed by the
		remote host. This is the normal mode of ending a
		connection to the serial daemon.


END TABLE ROW ENTRIES

NAME		serial-daemons-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Serial=>Serial Daemons Table
SNMP NAME	ncdSerialSDTable
SNMP PATH	ncdSerial 3
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the table of serial daemon parameters.


BEGIN TABLE ROW ENTRIES

NAME		serial-daemon-table-index
SNMP NAME	ncdSerialSDTableIndex
SNMP PATH	ncdSerialSDTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The index into the serial daemons interface table


NAME		port-number
SNMP NAME	ncdSerialSDTablePortNumber
SNMP PATH	ncdSerialSDTable 2
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the serial port.


NAME		use-serial-protocol
SNMP NAME	ncdSerialSDTableUseSerialProt
SNMP PATH	ncdSerialSDTable 3
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the new serial daemon control protocol
		should be used.  Note that this could cause some data
		loss if enabled with old host software.


NAME		tcp-port
SNMP NAME	ncdSerialSDTableTCPPort
SNMP PATH	ncdSerialSDTable 4
TYPE		INTEGER
MIN		1
DEFAULT		87
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port on which the terminal
		listens for raw TCP connections to the serial
		daemon.


NAME		ncdnet-object-name
SNMP NAME	ncdSerialSDTableUseNCDnetObjName
SNMP PATH	ncdSerialSDTable 5
TYPE		STRING
DEFAULT		SERIALD
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the NCDnet object on which the terminal
		listens for NCDnet connections to the serial
		daemon.


NAME		enable-lat-service
SNMP NAME	ncdSerialSDTableEnableLAT
SNMP PATH	ncdSerialSDTable 6
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies that the unit is to accept incoming 
		LAT solicit messages for a service which 
		allows access to the serial daemon. This is used
		to support VMS print services to the unit.


NAME		lat-service-name
SNMP NAME	ncdSerialSDTableLATServName
SNMP PATH	ncdSerialSDTable 7
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the name of the serial daemon LAT service.


NAME		lat-service-rating
SNMP NAME	ncdSerialSDTableLATServRating
SNMP PATH	ncdSerialSDTable 8
TYPE		INTEGER
MIN		0
DEFAULT		50
MAX		255
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the rating of the serial daemon LAT service.


END TABLE ROW ENTRIES

NAME		serial-interface-statistics-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Serial=>Interface Statistics Table
SNMP NAME	ncdSerialTable
SNMP PATH	ncdSerial 1
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The table of serial interfaces.


BEGIN TABLE ROW ENTRIES

NAME		port-number
SNMP NAME	ncdSerialInPortNumber
SNMP PATH	ncdSerialTable 5
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the serial port.


NAME		reception-overruns
SNMP NAME	ncdSerialInOverruns
SNMP PATH	ncdSerialTable 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an incoming octet overwrote a
		previously received octet in the UART's buffer.


NAME		reception-frame-errors
SNMP NAME	ncdSerialInFrameErrors
SNMP PATH	ncdSerialTable 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an incoming octet had bad bit
		alignment.


NAME		reception-parity-errors
SNMP NAME	ncdSerialInParityErrors
SNMP PATH	ncdSerialTable 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the parity bit of an incoming
		octet was incorrect.


NAME		reception-break-errors
SNMP NAME	ncdSerialInBreakErrors
SNMP PATH	ncdSerialTable 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times a stop bit was not received
		at the expected time after a start bit, and the
		intervening bits were all zero.


NAME		total-characters-transmitted
SNMP NAME	ncdSerialInTotCharXmit
SNMP PATH	ncdSerialTable 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Total characters transmitted


NAME		total-transmit-interrupts
SNMP NAME	ncdSerialInTotXmitInt
SNMP PATH	ncdSerialTable 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Total transmission interrupts


NAME		total-characters-received
SNMP NAME	ncdSerialInTotCharRcv
SNMP PATH	ncdSerialTable 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Total of characters received


NAME		total-receive-interrupts
SNMP NAME	ncdSerialInTotRcvInt
SNMP PATH	ncdSerialTable 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Total of reception interrupts


NAME		total-receive-errors
SNMP NAME	ncdSerialInTotRcvErr
SNMP PATH	ncdSerialTable 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Total of reception errors


END TABLE ROW ENTRIES

NAME		serial-interfaces-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Serial=>Serial Interfaces Table
SNMP NAME	ncdSerialIfTable
SNMP PATH	ncdSerial 2
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the table of serial port parameters.


BEGIN TABLE ROW ENTRIES

NAME		serial-interface-table-index
SNMP NAME	ncdSerialIfTableIndex
SNMP PATH	ncdSerialIfTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The index into the serial interface table


NAME		port-number
SNMP NAME	ncdSerialIfTablePortNumber
SNMP PATH	ncdSerialIfTable 2
TYPE		INTEGER
MIN		1
MAX		3
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The name of the serial port.


NAME		mode
SNMP NAME	ncdSerialIfTableMode
SNMP PATH	ncdSerialIfTable 3
TYPE		CHOICE
CHOICES		{ terminal printer serial-daemon slip console input-device xremote ppp }
DEFAULT		terminal
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies what the serial port should be used for, but takes
		effect the next time the unit
is booted.  The choices
		'Printer' and 'Serial Daemon' are equivalent.


NAME		current-mode
SNMP NAME	ncdSerialIfTableCurMode
SNMP PATH	ncdSerialIfTable 9
TYPE		CHOICE
CHOICES		{ terminal printer serial-daemon slip console input-device xremote ppp }
DEFAULT		terminal
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what the serial port should be used for.  Any
		change takes effect immediately, but the value of this
		parameter is ignored at boot time in favor of the 'mode'
		value.


NAME		baud-rate
SNMP NAME	ncdSerialIfTableBaudRate
SNMP PATH	ncdSerialIfTable 4
TYPE		CHOICE
CHOICES		{ 50 75 110 134.5 150 200 300 600 1050 1200 1800 2000 2400 4800 7200 9600 14400 19200 38400 57600 76800 115200 }
DEFAULT		9600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the baud rate of the serial port.


NAME		data-bits
SNMP NAME	ncdSerialIfTableDataBits
SNMP PATH	ncdSerialIfTable 5
TYPE		CHOICE
CHOICES		{ 8 7 }
DEFAULT		8
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the number of data bits per
		character of the serial port.


NAME		stop-bits
SNMP NAME	ncdSerialIfTableStopBits
SNMP PATH	ncdSerialIfTable 6
TYPE		CHOICE
CHOICES		{ 1 2 }
DEFAULT		1
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the number of stop bits per
		character of the serial port.


NAME		parity
SNMP NAME	ncdSerialIfTableParity
SNMP PATH	ncdSerialIfTable 7
TYPE		CHOICE
CHOICES		{ none odd even space mark }
DEFAULT		none
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the form of parity generated by
		and expected by the serial port.


NAME		handshake
SNMP NAME	ncdSerialIfTableHandshake
SNMP PATH	ncdSerialIfTable 8
TYPE		CHOICE
CHOICES		{ none xon/xoff dtr/dsr rts/cts }
DEFAULT		none
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the type of flow control
		of the serial port.


NAME		hangup
SNMP NAME	ncdSerialIfTableActionOnDiscon
SNMP PATH	ncdSerialIfTable 10
TYPE		CHOICE
CHOICES		{ none drop-dtr send-break }
DEFAULT		none
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies what a local NCDterm client will do
		when closing the serial port.  Also specifies
		what the serial daemon will do to
		signal the end of a network connection.


END TABLE ROW ENTRIES


GROUP snmp

NAME		snmp-allow-reset
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Allow SNMP Reset
SNMP NAME	ncdAccessSnmpResetEnabled
SNMP PATH	ncdAccess 21
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether remote reset via SNMP is enabled.


NAME		snmp-bad-variable-name-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Bad Variable Name Error Responses Received
SNMP NAME	snmpInNoSuchNames
SNMP PATH	snmp 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		delivered to the SNMP protocol entity and for
		which the value of the error-status field is
		`noSuchName'.


NAME		snmp-bad-variable-name-error-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Bad Variable Name Error Responses Transmitted
SNMP NAME	snmpOutNoSuchNames
SNMP PATH	snmp 21
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		generated by the SNMP protocol entity and for
		which the value of the error-status is `noSuchName'.


NAME		snmp-bad-variable-values-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Bad Variable Values Error Responses Received
SNMP NAME	snmpInBadValues
SNMP PATH	snmp 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		delivered to the SNMP protocol entity and for
		which the value of the error-status field is
		`badValue'.


NAME		snmp-bad-variable-values-error-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Bad Variable Values Error Responses Transmitted
SNMP NAME	snmpOutBadValues
SNMP PATH	snmp 22
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		generated by the SNMP protocol entity and for
		which the value of the error-status field is
		`badValue'.


NAME		snmp-general-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>General Error Responses Received
SNMP NAME	snmpInGenErrs
SNMP PATH	snmp 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		delivered to the SNMP protocol entity and for
		which the value of the error-status field is
		`genErr'.


NAME		snmp-general-error-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>General Error Responses Transmitted
SNMP NAME	snmpOutTooBigs
SNMP PATH	snmp 24
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		generated by the SNMP protocol entity and for
		which the value of the error-status field is
		`genErr'.


NAME		snmp-get-next-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get-Next Requests Received
SNMP NAME	snmpInGetNexts
SNMP PATH	snmp 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Next PDUs which have
		been accepted and processed by the SNMP protocol
		entity.


NAME		snmp-get-next-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get-Next Requests Transmitted
SNMP NAME	snmpOutGetNexts
SNMP PATH	snmp 26
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Next PDUs which have
		been generated by the SNMP protocol entity.


NAME		snmp-get-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get Requests Received
SNMP NAME	snmpInGetRequests
SNMP PATH	snmp 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Request PDUs which
		have been accepted and processed by the SNMP
		protocol entity.


NAME		snmp-get-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get Requests Transmitted
SNMP NAME	snmpOutGetRequests
SNMP PATH	snmp 25
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Request PDUs which
		have been generated by the SNMP protocol entity.


NAME		snmp-get-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get Responses Received
SNMP NAME	snmpInGetResponses
SNMP PATH	snmp 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Response PDUs which
		have been accepted and processed by the SNMP
		protocol entity.


NAME		snmp-get-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Get Responses Transmitted
SNMP NAME	snmpOutGetResponses
SNMP PATH	snmp 28
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Get-Response PDUs which
		have been generated by the SNMP protocol entity.


NAME		snmp-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received
SNMP NAME	snmpInPkts
SNMP PATH	snmp 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of Messages delivered to the
		SNMP entity from the transport service.


NAME		snmp-packets-received-with-asn1-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received with ASN.1 Errors
SNMP NAME	snmpInASNParseErrs
SNMP PATH	snmp 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of ASN.1 or BER errors
		encountered by the SNMP protocol entity when
		decoding received SNMP Messages.


NAME		snmp-packets-received-with-bad-community-names
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received with Bad Community Names
SNMP NAME	snmpInBadCommunityNames
SNMP PATH	snmp 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Messages delivered to
		the SNMP protocol entity which used a SNMP
		community name not known to said entity.


NAME		snmp-packets-received-with-bad-community-uses
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received with Bad Community Uses
SNMP NAME	snmpInBadCommunityUses
SNMP PATH	snmp 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Messages delivered to
		the SNMP protocol entity which represented an SNMP
		operation which was not allowed by the SNMP
		community named in the Message.


NAME		snmp-packets-received-with-bad-variable-types
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received with Bad Variable Types
SNMP NAME	snmpInBadTypes
SNMP PATH	snmp 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs delivered to the SNMP
		protocol entity which had an unknown PDU type.


NAME		snmp-packets-received-with-bad-versions
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Received with Bad Versions
SNMP NAME	snmpInBadVersions
SNMP PATH	snmp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Messages which were
		delivered to the SNMP protocol entity and were for
		an unsupported SNMP version.


NAME		snmp-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Packets Transmitted
SNMP NAME	snmpOutPkts
SNMP PATH	snmp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Messages which were
		passed from the SNMP protocol entity to the
		transport service.


NAME		snmp-read-only-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable SNMP Read-Only Access Control
SNMP NAME	ncdAccessSnmpReadOnlyAccessControl
SNMP PATH	ncdAccess 15
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether requests for connections to the
		SNMP daemon from outside the unit will
		be checked against the read-only host access control list


NAME		snmp-read-only-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Only Access Control List
SNMP NAME	ncdAccessSnmpReadOnlyAccessControlTable
SNMP PATH	ncdAccess 16
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of IP hosts that allowed
		to use the SNMP read-only community to access
		network management information via SNMP.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessSnmpROAccessControlTableIndex
SNMP PATH	ncdAccessSnmpReadOnlyAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the SNMP RO Access Control Table


NAME		host
SNMP NAME	ncdAccessSnmpROAccessControlTableHost
SNMP PATH	ncdAccessSnmpReadOnlyAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the SNMP daemon.


END TABLE ROW ENTRIES

NAME		snmp-read-only-community
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Only Community
SNMP NAME	ncdAccessSnmpReadOnlyCommunity1
SNMP PATH	ncdAccess 13
TYPE		STRING
DEFAULT		public
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the first of two possible community names that can
		be specified in SNMP requests to obtain read-only access
		to configuration information.


NAME		snmp-read-only-community-alt
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Only Alternative Community
SNMP NAME	ncdAccessSnmpReadOnlyCommunity2
SNMP PATH	ncdAccess 14
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the second of two possible community names that can
		be specified in SNMP requests to obtain read-only access
		to configuration information.


NAME		snmp-read-only-variable-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Read-Only Variable Error Responses Received
SNMP NAME	snmpInReadOnlys
SNMP PATH	snmp 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number valid SNMP PDUs which were
		delivered to the SNMP protocol entity and for
		which the value of the error-status field is
		`readOnly'.  It should be noted that it is a
		protocol error to generate an SNMP PDU which
		contains the value `readOnly' in the error-status
		field, as such this object is provided as a means
		of detecting incorrect implementations of SNMP.


NAME		snmp-read-only-variable-error-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Read-Only Variable Error Responses Transmitted
SNMP NAME	snmpOutReadOnlys
SNMP PATH	snmp 23
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number valid SNMP PDUs which were generated by
		the SNMP protocol entity and for which the value of the
		error-status field is `readOnly'.


NAME		snmp-read-write-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable SNMP Read-Write Access Control
SNMP NAME	ncdAccessSnmpReadWriteAccessControl
SNMP PATH	ncdAccess 19
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether requests for connections to the
		SNMP daemon from outside the unit will
		be checked against the read-write host access control list


NAME		snmp-read-write-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Write Access Control List
SNMP NAME	ncdAccessSnmpReadWriteAccessControlTable
SNMP PATH	ncdAccess 20
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of IP hosts that allowed
		to use the SNMP read-write community to access
		network management information via SNMP.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessSnmpRWAccessControlTableIndex
SNMP PATH	ncdAccessSnmpReadWriteAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the SNMP RW Access Control Table


NAME		host
SNMP NAME	ncdAccessSnmpRWAccessControlTableAddress
SNMP PATH	ncdAccessSnmpReadWriteAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the SNMP daemon.


END TABLE ROW ENTRIES

NAME		snmp-read-write-community
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Write Community
SNMP NAME	ncdAccessSnmpReadWriteCommunity1
SNMP PATH	ncdAccess 17
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the first of two possible community names that can
		be specified in SNMP requests to obtain read-write access
		to configuration information.


NAME		snmp-read-write-community-alt
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Read-Write Alternative Community
SNMP NAME	ncdAccessSnmpReadWriteCommunity2
SNMP PATH	ncdAccess 18
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the second of two possible community names that can
		be specified in SNMP requests to obtain read-write access
		to configuration information.


NAME		snmp-set-requests-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Set Requests Received
SNMP NAME	snmpInSetRequests
SNMP PATH	snmp 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Set-Request PDUs which
		have been accepted and processed by the SNMP
		protocol entity.


NAME		snmp-set-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Set Requests Transmitted
SNMP NAME	snmpOutSetRequests
SNMP PATH	snmp 27
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Set-Request PDUs which
		have been generated by the SNMP protocol entity.


NAME		snmp-too-big-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Too Big Error Responses Received
SNMP NAME	snmpInTooBigs
SNMP PATH	snmp 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		delivered to the SNMP protocol entity and for
		which the value of the error-status field is
		`tooBig'.


NAME		snmp-too-big-error-responses-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Too Big Error Responses Transmitted
SNMP NAME	snmpOutTooBigs
SNMP PATH	snmp 20
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP PDUs which were
		generated by the SNMP protocol entity and for
		which the value of the error-status field is
		`tooBig.'


NAME		snmp-trap-monitors
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>SNMP Trap Monitors
SNMP NAME	ncdAccessSnmpTrapMonitorsTable
SNMP PATH	ncdAccess 22
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the list of IP hosts to which SNMP traps are sent.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessSnmpTMTIndex
SNMP PATH	ncdAccessSnmpTrapMonitorsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Trap Monitors Table


NAME		host
SNMP NAME	ncdAccessSnmpTMTHost
SNMP PATH	ncdAccessSnmpTrapMonitorsTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the network name/address
		of a node granted permission to
		remotely access the SNMP daemon.


NAME		community
SNMP NAME	ncdAccessSnmpTMTCommunity
SNMP PATH	ncdAccessSnmpTrapMonitorsTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the community name to use
		in the trap message sent to the host.


END TABLE ROW ENTRIES

NAME		snmp-traps-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Traps Received
SNMP NAME	snmpInTraps
SNMP PATH	snmp 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Trap PDUs which have
		been accepted and processed by the SNMP protocol
		entity.


NAME		snmp-traps-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Traps Transmitted
SNMP NAME	snmpOutTraps
SNMP PATH	snmp 29
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of SNMP Trap PDUs which have
		been generated by the SNMP protocol entity.


NAME		snmp-variable-gets-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Variable Gets Completed
SNMP NAME	snmpInTotalReqVars
SNMP PATH	snmp 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of MIB objects which have been
		retrieved successfully by the SNMP protocol entity
		as the result of receiving valid SNMP Get-Request
		and Get-Next PDUs.


NAME		snmp-variable-sets-completed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  SNMP=>Variable Sets Completed
SNMP NAME	snmpInTotalSetVars
SNMP PATH	snmp 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of MIB objects which have been
		altered successfully by the SNMP protocol entity
		as the result of receiving valid SNMP Set-Request
		PDUs.



GROUP tcp

NAME		tcp-ack-only-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Ack-Only Packets Transmitted
SNMP NAME	ncdTcpOutBareAcks
SNMP PATH	ncdTcp 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TCP packets received which acknowledged
		1 or more octets of unacknowledged data.


NAME		tcp-ack-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Ack Packets Received
SNMP NAME	ncdTcpInAcks
SNMP PATH	ncdTcp 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TCP packets transmitted which contained
		no data, and only the ACK flag turned on.


NAME		tcp-active-connect-attempts
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Active Connect Attempts
SNMP NAME	tcpActiveOpens
SNMP PATH	tcp 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times TCP connections have made a
		direct transition to the SYN-SENT state from the
		CLOSED state.


NAME		tcp-connect-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Connect Timeout
SNMP NAME	ncdTcpConnectTimeout
SNMP PATH	ncdTcp 6
TYPE		INTEGER
MIN		1
DEFAULT		75
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) that must elapse
		between a TCP connection attempt and a lack of a response
		for a failure situation to be declared.


NAME		tcp-connection-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Connection Table
SNMP NAME	tcpConnTable
SNMP PATH	tcp 13
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The table of TCP connections.


BEGIN TABLE ROW ENTRIES

NAME		local-ip-address
SNMP NAME	tcpConnLocalAddress
SNMP PATH	tcpConnTable 2
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The local IP address for this TCP connection.  In
		the case of a connection in the listen state which
		is willing to accept connections for any IP
		interface associated with the node, the value
		0.0.0.0 is used.


NAME		local-port
SNMP NAME	tcpConnLocalPort
SNMP PATH	tcpConnTable 3
TYPE		INTEGER
MIN		0
MAX		65535
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The local port number for this TCP connection.


NAME		remote-ip-address
SNMP NAME	tcpConnRemAddress
SNMP PATH	tcpConnTable 4
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The remote IP address for this TCP connection.


NAME		remote-port
SNMP NAME	tcpConnRemPort
SNMP PATH	tcpConnTable 5
TYPE		INTEGER
MIN		0
MAX		65535
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The remote port number for this TCP connection.


NAME		state
SNMP NAME	tcpConnState
SNMP PATH	tcpConnTable 1
TYPE		CHOICE
CHOICES		{ closed listen syn-sent syn-received established fin-wait-1 fin-wait-2 close-wait last-ack closing time-wait }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The state of this TCP connection.


END TABLE ROW ENTRIES

NAME		tcp-connections-reset
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Connections Reset
SNMP NAME	tcpEstabResets
SNMP PATH	tcp 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times TCP connections have made a
		direct transition to the CLOSED state from either
		the ESTABLISHED state or the CLOSE-WAIT state.


NAME		tcp-connections-timed-out-on-keepalives
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Connections Timed Out on Keepalives
SNMP NAME	ncdTcpKeepAliveDrops
SNMP PATH	ncdTcp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections progressing directly to the
		CLOSED state due to too many keep alives being sent.


NAME		tcp-connections-timed-out-on-retransmissions
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Connections Timed Out on Retransmissions
SNMP NAME	ncdTcpRetransDrops
SNMP PATH	ncdTcp 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of connections progressing directly to the
		CLOSED state due to too many retransmissions being sent.


NAME		tcp-default-linger-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Default Linger Time
SNMP NAME	ncdTcpDfltLingerTime
SNMP PATH	ncdTcp 11
TYPE		INTEGER
MIN		1
DEFAULT		120
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default time (in seconds) TCP continues to attempt
		reliable transmission of outstanding data on
		the connection's transmit queue after local software
		closes a connection. This timer is optional and can be
		configure on a per connection basis by the software by
		higher level software.


NAME		tcp-established-connections
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Established Connections
SNMP NAME	tcpCurrEstab
SNMP PATH	tcp 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TCP connections for which the
		current state is either ESTABLISHED or CLOSE-WAIT.


NAME		tcp-failed-connect-attempts
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Failed Connect Attempts
SNMP NAME	tcpAttemptFails
SNMP PATH	tcp 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times TCP connections have made a
		direct transition to the CLOSED state from either
		the SYN-SENT state or the SYN-RCVD state, plus the
		number of times TCP connections have made a direct
		transition to the LISTEN state from the SYN-RCVD
		state.


NAME		tcp-keepalive-idle-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Keepalive Idle Time
SNMP NAME	ncdTcpKeepIdle
SNMP PATH	ncdTcp 8
TYPE		INTEGER
MIN		1
DEFAULT		75
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) that must elapse
		on an established TCP connection with no activity
		before a TCP keepalive packet is generated.


NAME		tcp-keepalive-interval
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Keepalive Interval
SNMP NAME	ncdTcpKeepAliveIntvl
SNMP PATH	ncdTcp 9
TYPE		INTEGER
MIN		1
DEFAULT		75
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) between successive
		transmissions of TCP keepalive packets when no
		response to the keepalive packets has been received.


NAME		tcp-keepalive-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Keepalive Packets Transmitted
SNMP NAME	ncdTcpOutKeepAlives
SNMP PATH	ncdTcp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TCP Keep Alive packets transmitted.


NAME		tcp-max-keepalive-idle-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Max Keepalive Idle Time
SNMP NAME	ncdTcpMaxKeepAliveIdeTime
SNMP PATH	ncdTcp 10
TYPE		INTEGER
MIN		1
DEFAULT		600
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of time (in seconds) that
		TCP keepalives are transmitted with no response
		before a failure situation is declared.


NAME		tcp-max-retransmissions
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Max Retransmissions
SNMP NAME	ncdTcpMaxRxt
SNMP PATH	ncdTcp 7
TYPE		INTEGER
MIN		1
DEFAULT		12
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of retransmission that must
		occur on a TCP connection before a failure situation is
		declared.


NAME		tcp-maximum-number-of-connections
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Maximum Number of Connections
SNMP NAME	tcpMaxConn
SNMP PATH	tcp 4
TYPE		INTEGER
MIN		-1
MAX		2147483647
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The limit on the total number of TCP connections
		the entity can support.  In entities where the
		maximum number of connections is dynamic, this
		object should contain the value -1.


NAME		tcp-maximum-retransmission-time
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Maximum Retransmission Time
SNMP NAME	tcpRtoMax
SNMP PATH	tcp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The maximum value (in seconds) permitted for
		the retransmission timeout.


NAME		tcp-minimum-retransmission-time
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Minimum Retransmission Time
SNMP NAME	tcpRtoMin
SNMP PATH	tcp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The minimum value (in seconds) permitted for
		the retransmission timeout.


NAME		tcp-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Packets Received
SNMP NAME	tcpInSegs
SNMP PATH	tcp 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of segments received, including
		those received in error.  This count includes
		segments received on currently established connections.


NAME		tcp-packets-retransmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Packets Retransmitted
SNMP NAME	tcpRetransSegs
SNMP PATH	tcp 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of segments retransmitted - that
		is, the number of TCP segments transmitted
		containing one or more previously transmitted
		octets.


NAME		tcp-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Packets Transmitted
SNMP NAME	tcpOutSegs
SNMP PATH	tcp 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of segments sent, including
		those on current connections but excluding those
		containing only retransmitted octets.


NAME		tcp-packets-with-errors-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Packets with Errors Received
SNMP NAME	tcpInErrs
SNMP PATH	tcp 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of segments received in error
		(e.g., bad TCP checksums).


NAME		tcp-passive-connects-attempts
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Passive Connects Attempts
SNMP NAME	tcpPassiveOpens
SNMP PATH	tcp 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times TCP connections have made a
		direct transition to the SYN-RCVD state from the
		LISTEN state.


NAME		tcp-receive-buffer-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Receive Buffer Size
SNMP NAME	ncdTcpRecvBufferSize
SNMP PATH	ncdTcp 12
TYPE		INTEGER
MIN		1024
DEFAULT		4096
MAX		9216
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of received data in bytes that a TCP
		connection will buffer in the unit. This corresponds to
		the TCP receive window advertised by the unit to the peer.


NAME		tcp-reset-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Reset Packets Transmitted
SNMP NAME	tcpOutRsts
SNMP PATH	tcp 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TCP segments sent containing the RST flag.


NAME		tcp-retransmission-algorithm-type
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP=>Retransmission Algorithm Type
SNMP NAME	tcpRtoAlgorithm
SNMP PATH	tcp 1
TYPE		CHOICE
CHOICES		{ other constant rsre van-jacobson }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The algorithm used to determine the timeout value
		used for retransmitting unacknowledged octets.


NAME		tcp-send-buffer-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP=>Send Buffer Size
SNMP NAME	ncdTcpSendBufferSize
SNMP PATH	ncdTcp 13
TYPE		INTEGER
MIN		1024
DEFAULT		2048
MAX		65535
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of data in bytes
		awaiting transmission that a TCP connection will buffer
		in the unit. This corresponds to the maximum amount of
		the peer's TCP send window that will be used by the unit.



GROUP tcpip

NAME		tcpip-arp-cache
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  ARP=>ARP Cache
SNMP NAME	ipNetToMediaTable
SNMP PATH	ip 22
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the ARP table which is used to map from IP addresses
		to media dependent physical addresses.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ipNetToMediaIfIndex
SNMP PATH	ipNetToMediaTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Interface index for each entry equivalence


NAME		ethernet-address
SNMP NAME	ipNetToMediaPhysAddress
SNMP PATH	ipNetToMediaTable 2
TYPE		STRING
DEFAULT		00:00:00:00:00:00
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the physical address (Ethernet).


NAME		ip-address
SNMP NAME	ipNetToMediaNetAddress
SNMP PATH	ipNetToMediaTable 3
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP address.


NAME		type
SNMP NAME	ipNetToMediaType
SNMP PATH	ipNetToMediaTable 4
TYPE		CHOICE
CHOICES		{ incomplete dynamic static }
DEFAULT		incomplete
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the state of the entry. A static
		entry is one that is not subject to the usual
		automatic deletion process.


NAME		time-since-last-use
SNMP NAME	ncdIpTimeSinceLastUse
SNMP PATH	ipNetToMediaTable 13
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the last time (in minutes) the entry
		was used by the unit.


END TABLE ROW ENTRIES

NAME		tcpip-arp-complete-entry-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  ARP=>Complete Entry Timeout
SNMP NAME	ncdArpCompleteEntryTimeout
SNMP PATH	ncdArp 2
TYPE		INTEGER
MIN		1
DEFAULT		20
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how long (in minutes) a completed ARP table entry should
		be allowed to exist without being used before it is
		automatically deleted.


NAME		tcpip-arp-incomplete-entry-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  ARP=>Incomplete Entry Timeout
SNMP NAME	ncdArpIncompleteEntryTimeout
SNMP PATH	ncdArp 1
TYPE		INTEGER
MIN		1
DEFAULT		1
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how long (in minutes) an incomplete ARP table
		entry should be allowed to exist without being used before it is
		automatically deleted. Incomplete entries exist when
		an IP address cannot be resolved to a Ethernet address.


NAME		tcpip-dns-default-domain
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>DNS Default Domain
SNMP NAME	ncdNameResolverDnsDefaultDomain
SNMP PATH	ncdNameResolver 19
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default domain to use with DNS
		name service requests.


NAME		tcpip-dns-domain-search
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>DNS Domain Search
SNMP NAME	ncdNameResolverDnsDoNameSearch
SNMP PATH	ncdNameResolver 20
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that when attempting to resolve a name
		with DNS try successively wider scopes of the name
		space. i.e. if the default domain is eng.ncd.com,
		and the host name is hansen, then we first try
		hansen.eng.ncd.com., and then hansen.ncd.com.


NAME		tcpip-name-bad-name-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Bad Name Errors
SNMP NAME	ncdNameResolverBadNameErrs
SNMP PATH	ncdNameResolver 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of 'Bad Name' errors returned by the
		TCP/IP name servers for name requests. This indicates
		a badly formed name.


NAME		tcpip-name-cache-hits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Name Cache Hits
SNMP NAME	ncdNameResolverCacheHits
SNMP PATH	ncdNameResolver 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the answer
		was found in the local TCP/IP name cache.


NAME		tcpip-name-cache-max-lifetime
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Cache Max Lifetime
SNMP NAME	ncdNameResolverNameCacheMaxTimeout
SNMP PATH	ncdNameResolver 13
TYPE		INTEGER
MIN		0
DEFAULT		1800
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of time (in seconds) that a
		TCP/IP name service entry should be used before it
		is automatically deleted.


NAME		tcpip-name-cache-max-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Cache Max Size
SNMP NAME	ncdNameResolverNameCacheMaxSize
SNMP PATH	ncdNameResolver 12
TYPE		INTEGER
MIN		0
DEFAULT		32
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum number of entries in the TCP/IP
		name cache.


NAME		tcpip-name-cache-overflows
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Name Cache Overflows
SNMP NAME	ncdNameResolverCacheOverflows
SNMP PATH	ncdNameResolver 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times a valid entry in the local TCP/IP name cache
		had to be deleted to make room for a new entry.


NAME		tcpip-name-local-cache
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Local Name Cache
SNMP NAME	ncdNameResolverNameCacheTable
SNMP PATH	ncdNameResolver 14
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the TCP/IP name service cache.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdNameResolverTableIndex
SNMP PATH	ncdNameResolverNameCacheTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index into the IP Local Name Cache Table


NAME		name
SNMP NAME	ncdNameResolverTableName
SNMP PATH	ncdNameResolverNameCacheTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the symbolic name of the host.


NAME		address
SNMP NAME	ncdNameResolverTableAddress
SNMP PATH	ncdNameResolverNameCacheTable 3
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP address(es) of the host.


NAME		lifetime
SNMP NAME	ncdNameResolverTableExpTime
SNMP PATH	ncdNameResolverNameCacheTable 4
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the time (relative to the unit boot time
		in seconds) at which the entry will become invalid.


END TABLE ROW ENTRIES

NAME		tcpip-name-memory-allocation-failures
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Memory Allocation Failures
SNMP NAME	ncdNameResolverNoMemErrs
SNMP PATH	ncdNameResolver 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the TCP/IP name resolver
		was unable to allocated required memory.


NAME		tcpip-name-no-server-responses
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>No Server Responses
SNMP NAME	ncdNameResolverNoRspErrs
SNMP PATH	ncdNameResolver 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times no response was received from a
		TCP/IP name server.


NAME		tcpip-name-no-such-name-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>No Such Name Errors
SNMP NAME	ncdNameResolverNoNameErrs
SNMP PATH	ncdNameResolver 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of 'No Such Name' errors returned by the
		TCP/IP name servers for name requests.


NAME		tcpip-name-numerical-addresses
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Numerical Addresses
SNMP NAME	ncdNameResolverNumericalAddrs
SNMP PATH	ncdNameResolver 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the TCP/IP name was
		in numerical format, e.g. 192.43.154.7.


NAME		tcpip-name-requests
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Name Requests
SNMP NAME	ncdNameResolverRequests
SNMP PATH	ncdNameResolver 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the TCP/IP name resolver
		was invoked.


NAME		tcpip-name-server-hits
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Name Server Hits
SNMP NAME	ncdNameResolverServerHits
SNMP PATH	ncdNameResolver 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of invocations where the answer
		was found by consulting the TCP/IP name servers.


NAME		tcpip-name-server-protocol
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Server Protocol
SNMP NAME	ncdNameResolverProtocol
SNMP PATH	ncdNameResolver 15
TYPE		CHOICE
CHOICES		{ dns ien-116 }
DEFAULT		ien-116
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the TCP/IP name service protocol to use
		when contacting the name servers.


NAME		tcpip-name-server-response-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>Name Server Response Errors
SNMP NAME	ncdNameResolverRspErrs
SNMP PATH	ncdNameResolver 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of badly formed responses returned by the
		TCP/IP name servers for name requests.


NAME		tcpip-name-server-retransmission-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Server Retransmission Timeout
SNMP NAME	ncdNameResolverRtxTimeout
SNMP PATH	ncdNameResolver 16
TYPE		INTEGER
MIN		1
DEFAULT		2
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) between
		retransmissions of a TCP/IP name service
		request.


NAME		tcpip-name-server-transaction-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Server Transaction Timeout
SNMP NAME	ncdNameResolverTransactTimeout
SNMP PATH	ncdNameResolver 1
TYPE		INTEGER
MIN		1
DEFAULT		10
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to attempt
		a TCP/IP name service request before a failure
		situation is declared.


NAME		tcpip-name-servers
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  TCP/IP Name Service=>Name Servers
SNMP NAME	ncdNameResolverNameServersTable
SNMP PATH	ncdNameResolver 18
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the list of TCP/IP name servers.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdInetNameServersTableIndex
SNMP PATH	ncdNameResolverNameServersTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the index to the IP Name Servers Table


NAME		server
SNMP NAME	ncdInetNameServersTableAddress
SNMP PATH	ncdNameResolverNameServersTable 2
TYPE		STRING
DEFAULT		0.0.0.0
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the IP address of the name server.


END TABLE ROW ENTRIES

NAME		tcpip-name-system-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TCP/IP Name Service=>System Errors
SNMP NAME	ncdNameResolverSysErrs
SNMP PATH	ncdNameResolver 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the TCP/IP name resolver
		encountered an general system error.



GROUP term

NAME		term-default-connect-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  VT320 Terminal Emulation=>Terminal Default Connect Timeout
SNMP NAME	ncdTermDfltConnectTimeout
SNMP PATH	ncdTerm 4
TYPE		INTEGER
MIN		0
DEFAULT		20
MAX		600
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default amount of time (in seconds) that
		the terminal emulator should attempt to establish a
		connection before declaring an error situation.


NAME		term-default-hosts
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  VT320 Terminal Emulation=>Default Hosts
SNMP NAME	ncdTermDfltConnectionTable
SNMP PATH	ncdTerm 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default list of hosts to present
		to the user in the terminal chooser.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdTermDCTIndex
SNMP PATH	ncdTermDfltConnectionTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Default Hosts table for NCDterm


NAME		protocol
SNMP NAME	ncdTermDCTProtocol
SNMP PATH	ncdTermDfltConnectionTable 2
TYPE		CHOICE
CHOICES		{ telnet lat cterm serial }
DEFAULT		telnet
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the protocol to use.


NAME		host
SNMP NAME	ncdTermDCTHost
SNMP PATH	ncdTermDfltConnectionTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name of the terminal host.


NAME		description
SNMP NAME	ncdTermDCTDescription
SNMP PATH	ncdTermDfltConnectionTable 4
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a description of the terminal host.


END TABLE ROW ENTRIES

NAME		term-restrict-host-choices
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  VT320 Terminal Emulation=>Restrict Host Choices
SNMP NAME	ncdTermRestrictConnectionChoices
SNMP PATH	ncdTerm 2
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the user should only be allowed
		to choose a terminal host specified in the default
		terminal hosts list.


NAME		term-window-delay-time
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  VT320 Terminal Emulation=>Window Delay Time
SNMP NAME	ncdTermAutoMapDelay
SNMP PATH	ncdTerm 3
TYPE		INTEGER
MIN		0
DEFAULT		3
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to wait before
		displaying the terminal window when starting from
		a command line.



GROUP tftp

NAME		tftp-ack-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Ack Packets Received
SNMP NAME	ncdTftpClientInAcks
SNMP PATH	ncdTftp 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TFTP Ack packets received by the TFTP client.


NAME		tftp-ack-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Ack Packets Transmitted
SNMP NAME	ncdTftpClientOutAcks
SNMP PATH	ncdTftp 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TFTP Ack packets sent by the TFTP client.


NAME		tftp-bad-access-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Bad Access Error Responses Received
SNMP NAME	ncdTftpClientInAccessErrors
SNMP PATH	ncdTftp 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an TFTP Error packet was received
		by the TFTP client with the error code set to
		'Access violation.'


NAME		tftp-data-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Data Packets Received
SNMP NAME	ncdTftpClientInDataPkts
SNMP PATH	ncdTftp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TFTP Data packets received by the TFTP client.


NAME		tftp-data-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Data Packets Transmitted
SNMP NAME	ncdTftpClientOutDataPkts
SNMP PATH	ncdTftp 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of TFTP Data packets sent by the TFTP client.


NAME		tftp-disk-full-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Disk Full Error Responses Received
SNMP NAME	ncdTftpClientInDiskFullErrors
SNMP PATH	ncdTftp 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an TFTP Error packet was received
		by the TFTP client with the error code set to 'Disk full'.


NAME		tftp-file-read-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>File Read Requests Transmitted
SNMP NAME	ncdTftpClientReadReqs
SNMP PATH	ncdTftp 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of file read requests made by the TFTP client.


NAME		tftp-file-write-requests-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>File Write Requests Transmitted
SNMP NAME	ncdTftpClientWriteReqs
SNMP PATH	ncdTftp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of file write requests made by the TFTP client.


NAME		tftp-no-available-buffer-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>No Available Buffer Errors
SNMP NAME	ncdTftpClientNoBufs
SNMP PATH	ncdTftp 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the TFTP client failed to allocate
		a buffer.


NAME		tftp-no-file-error-responses-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>No File Error Responses Received
SNMP NAME	ncdTftpClientInNoFileErrors
SNMP PATH	ncdTftp 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times an TFTP Error packet was received
		by the TFTP client with the error code set to
		'File not found'.


NAME		tftp-packets-retransmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  TFTP=>Packets Retransmitted
SNMP NAME	ncdTftpClientRetrans
SNMP PATH	ncdTftp 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times a TFTP packet was retransmitted by
		the TFTP client.



GROUP tokring

NAME		tokring-interface-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Token Ring=>Interface Table
SNMP NAME	dot5Table
SNMP PATH	dot5 1
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A list of Token Ring status and parameter
		values for an 802.5 interface.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	dot5IfIndex
SNMP PATH	dot5Table 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The value of this object identifies the
		802.5 interface for which this entry
		contains management information.


NAME		commands
SNMP NAME	dot5Commands
SNMP PATH	dot5Table 2
TYPE		CHOICE
CHOICES		{ none open reset close }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This object may be written with SNMP
		to open, close and reset the interface.


NAME		ring-status
SNMP NAME	dot5RingStatus
SNMP PATH	dot5Table 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The current interface status which can
		be used to diagnose fluctuating problems
		that can occur on token rings, after a
		station has successfully been added to
		the ring.
		    Before an open is completed, this
		object has the value for the 'no status'
		condition.  The dot5RingState and
		dot5RingOpenStatus objects provide for
		debugging problems when the station
		can not even enter the ring.
		    The object's value is a sum of
		values, one for each currently applicable
		condition.  The following values are
		defined for various conditions:
		 
		        0 = No Problems detected
		       32 = Ring Recovery
		       64 = Single Station
		      256 = Remove Received
		      512 = reserved
		     1024 = Auto-Removal Error
		     2048 = Lobe Wire Fault
		     4096 = Transmit Beacon
		     8192 = Soft Error
		    16384 = Hard Error
		    32768 = Signal Loss
		   131072 = no status, open not completed.


NAME		ring-state
SNMP NAME	dot5RingState
SNMP PATH	dot5Table 4
TYPE		CHOICE
CHOICES		{ opened closed opening closing open-failure ring-failure }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The current interface state with respect
		to entering or leaving the ring.


NAME		last-open-status
SNMP NAME	dot5RingOpenStatus
SNMP PATH	dot5Table 5
TYPE		CHOICE
CHOICES		{ none unknown cable-fault signal-loss timeout ring-failure beaconing duplicate-addr request-failed remove-received successful }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This object indicates the success, or the
		reason for failure, of the station's most
		recent attempt to enter the ring.


NAME		ring-speed
SNMP NAME	dot5RingSpeed
SNMP PATH	dot5Table 6
TYPE		CHOICE
CHOICES		{ unknown 1000000 4000000 16000000 }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The speed or bandwidth of the ring
		specified in (bits/second).


NAME		upstream-neighbor
SNMP NAME	dot5UpStream
SNMP PATH	dot5Table 7
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The MAC-address of the nearest active
		up stream neighbor station in the ring.


NAME		active-monitor-participate
SNMP NAME	dot5ActMonParticipate
SNMP PATH	dot5Table 8
TYPE		CHOICE
CHOICES		{ true false }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Whether or not this station will participate
		in the active monitor selection process


NAME		functional-addresses
SNMP NAME	dot5Functional
SNMP PATH	dot5Table 9
TYPE		CHOICE
CHOICES		{ none }
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The bit mask of all Token Ring functional
		addresses for which this interface will
		accept frames.


END TABLE ROW ENTRIES

NAME		tokring-statistics-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Token Ring=>Statistics Table
SNMP NAME	dot5StatsTable
SNMP PATH	dot5 2
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A table containing Token Ring statistics,
		one entry per 802.5 interface.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	dot5StatsIfIndex
SNMP PATH	dot5StatsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The value of this object identifies the
		802.5 interface for which this entry
		contains management information.


NAME		line-errors
SNMP NAME	dot5StatsLineErrors
SNMP PATH	dot5StatsTable 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a frame
		or token is copied or repeated by a
		station, the E bit is zero in the frame
		or token and one of the following
		conditions exists: 1) there is a
		non-data bit (J or K bit) between the SD
		and the ED of the frame or token, or
		2) there is an FCS error in the frame.


NAME		burst-errors
SNMP NAME	dot5StatsBurstErrors
SNMP PATH	dot5StatsTable 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		detects the absence of transitions for five
		half-bit timers (burst-five error).


NAME		ac-errors
SNMP NAME	dot5StatsACErrors
SNMP PATH	dot5StatsTable 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		receives an AMP or SMP frame in which A is
		equal to C is equal to 0, and then receives
		another SMP frame with A is equal to C is
		equal to 0 without first receiving an AMP
		frame. It denotes a station that cannot set
		the AC bits properly.


NAME		aborted-transmissions
SNMP NAME	dot5StatsAbortTransErrors
SNMP PATH	dot5StatsTable 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		transmits an abort delimiter while
		transmitting.


NAME		internal-errors
SNMP NAME	dot5StatsInternalErrors
SNMP PATH	dot5StatsTable 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		recognizes an internal error.


NAME		lost-frames
SNMP NAME	dot5StatsLostFrameErrors
SNMP PATH	dot5StatsTable 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		is transmitting and its TRR timer expires.
		This condition denotes a condition where a
		transmitting station in strip mode does not
		receive the trailer of the frame before the
		TRR timer goes off.


NAME		receive-congestions
SNMP NAME	dot5StatsReceiveCongestions
SNMP PATH	dot5StatsTable 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		recognizes a frame addressed to its
		specific address, but has no available
		buffer space indicating that the station
		is congested.


NAME		frame-copied-errors
SNMP NAME	dot5StatsFrameCopiedErrors
SNMP PATH	dot5StatsTable 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		recognizes a frame addressed to its
		specific address and detects that the FS
		field A bits are set to 1 indicating a
		possible line hit or duplicate address.


NAME		token-errors
SNMP NAME	dot5StatsTokenErrors
SNMP PATH	dot5StatsTable 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		This counter is incremented when a station
		acting as the active monitor recognizes an
		error condition that needs a token
		transmitted.


NAME		soft-errors
SNMP NAME	dot5StatsSoftErrors
SNMP PATH	dot5StatsTable 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of Soft Errors the interface
		has detected. It directly corresponds to
		the number of Report Error MAC frames
		that this interface has transmitted.
		Soft Errors are those which are
		recoverable by the MAC layer protocols.


NAME		hard-errors
SNMP NAME	dot5StatsHardErrors
SNMP PATH	dot5StatsTable 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times this interface has
		detected an immediately recoverable
		fatal error.  It denotes the number of
		times this interface is either
		transmitting or receiving beacon MAC
		frames.


NAME		signal-loss
SNMP NAME	dot5StatsSignalLossErrors
SNMP PATH	dot5StatsTable 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times this interface has
		detected the loss of signal condition from
		the ring.


NAME		transmit-beacons
SNMP NAME	dot5StatsTransmitBeacons
SNMP PATH	dot5StatsTable 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times this interface has
		transmitted a beacon frame.


NAME		ring-recoveries
SNMP NAME	dot5StatsRecoveries
SNMP PATH	dot5StatsTable 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of Claim Token MAC frames
		received or transmitted after the interface
		has received a Ring Purge MAC frame.  This
		counter signifies the number of times the
		ring has been purged and is being recovered
		back into a normal operating state.


NAME		cable-faults
SNMP NAME	dot5StatsLobeWires
SNMP PATH	dot5StatsTable 16
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the interface has
		detected an open or short circuit in the
		lobe data path.  The adapter will be closed
		and dot5RingState will signify this
		condition.


NAME		removes-received
SNMP NAME	dot5StatsRemoves
SNMP PATH	dot5StatsTable 17
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the interface has
		received a Remove Ring Station MAC frame
		request.  When this frame is received
		the interface will enter the close state
		and dot5RingState will signify this
		condition.


NAME		single-stations
SNMP NAME	dot5StatsSingles
SNMP PATH	dot5StatsTable 18
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the interface has
		sensed that it is the only station on the
		ring.  This will happen if the interface
		is the first one up on a ring, or if
		there is a hardware problem.


NAME		frequency-errors
SNMP NAME	dot5StatsFreqErrors
SNMP PATH	dot5StatsTable 19
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of times the interface has
		detected that the frequency of the
		incoming signal differs from the expected
		frequency by more than that specified by
		the IEEE 802.5 standard.


END TABLE ROW ENTRIES


GROUP udp

NAME		udp-listener-table
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  UDP=>Listener Table
SNMP NAME	udpTable
SNMP PATH	udp 5
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A table containing UDP listener information.


BEGIN TABLE ROW ENTRIES

NAME		local-ip-address
SNMP NAME	udpLocalAddress
SNMP PATH	udpTable 1
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The local IP address for this UDP listener.  In
		the case of a UDP listener which is willing to
		accept datagrams for any IP interface associated
		with the node, the value 0.0.0.0 is used.


NAME		local-port
SNMP NAME	udpLocalPort
SNMP PATH	udpTable 2
TYPE		INTEGER
MIN		0
MAX		65535
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The local port number for this UDP listener.


END TABLE ROW ENTRIES

NAME		udp-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  UDP=>Packets Received
SNMP NAME	udpInDatagrams
SNMP PATH	udp 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of UDP datagrams delivered to UDP applications.


NAME		udp-packets-received-with-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  UDP=>Packets Received with Errors
SNMP NAME	udpInErrors
SNMP PATH	udp 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of received UDP datagrams that could
		not be delivered for reasons other than the lack
		of an application at the destination port.


NAME		udp-packets-received-with-unknown-port
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  UDP=>Packets Received with Unknown Port
SNMP NAME	udpNoPorts
SNMP PATH	udp 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of received UDP datagrams for
		which there was no application at the destination port.


NAME		udp-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  UDP=>Packets Transmitted
SNMP NAME	udpOutDatagrams
SNMP PATH	udp 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total number of UDP datagrams sent from this entity.



GROUP unit

NAME		unit-administrative-status
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Administrative Status
SNMP NAME	ncdSysAdminStatus
SNMP PATH	ncdSystem 7
TYPE		CHOICE
CHOICES		{ running session-reset last-client-close-reset unit-reset }
DEFAULT		running
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The administrative status of the unit.  Options are:
		   Running                 : Unit is running; no resets pending
		   Session Reset           : Session reset pending
		   Last Client Close Reset : Reset on last client close pending
		   Unit Reset              : Unit reset pending


NAME		unit-blocks-of-available-memory
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Blocks of Available Memory
SNMP NAME	ncdSysMemFrags
SNMP PATH	ncdSystem 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of discontiguous blocks of unallocated memory.


NAME		unit-boot-monitor-version
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Boot Monitor Version
SNMP NAME	ncdSysBootPromVersion
SNMP PATH	ncdSystem 5
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A textual description of the boot PROM's installed
		in the unit.


NAME		unit-code-memory-installed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Code Memory Installed
SNMP NAME	ncdSysMemCode
SNMP PATH	ncdSystem 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total amount of code RAM in bytes installed in the system.


NAME		unit-contact
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Administrative Contact
SNMP NAME	sysContact
SNMP PATH	system 4
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the administrative contact for the unit.
		This is provided as a convience for
		system administration personnel.


NAME		unit-global-password
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Unit Global Password
SNMP NAME	ncdAccessGlobalPasswd
SNMP PATH	ncdAccess 38
TYPE		STRING
DEFAULT		nil
PERMISSION	WRITE-ONLY
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		Specifies the password required to obtain read-write access
		to the Config, Pref, SNMP, and File Daemons.


NAME		unit-idle-time
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Idle Time
SNMP NAME	ncdSysIdleTime
SNMP PATH	ncdSystem 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The estimated amount of time (in seconds) since boot
		that the system was not executing any useful task.


NAME		unit-keyboard-controller-version
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Keyboard Controller Version
SNMP NAME	ncdSysKeyboardControllerVersion
SNMP PATH	ncdSystem 6
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A textual description of the keyboard controller
		installed in the unit.


NAME		unit-license-key
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>License Key
SNMP NAME	ncdSysLicenseKey
SNMP PATH	ncdSystem 11
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		YES
DESCRIPTION
		The license key that defines the enabled
		optional licensed software features.


NAME		unit-licensed-features
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Licensed Features
SNMP NAME	ncdSysLicensedFeatures
SNMP PATH	ncdSystem 12
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The list of software features that are licensed
		currently enabled for this unit.


NAME		unit-location
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Physical Location
SNMP NAME	sysLocation
SNMP PATH	system 6
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the physical location of the unit.
		This is provided as a convience for
		system administration personnel.


NAME		unit-low-memory-level
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Show Low Memory Warning Box at  (bytes)
SNMP NAME	ncdSysLowMemWarningThreshold
SNMP PATH	ncdSystem 10
TYPE		INTEGER
MIN		0
DEFAULT		50000
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Resets the threshold (in bytes) for displaying the
		Low on Memory warning box. If free memory drops below
		this value, the warning box will appear with an
		appropriate message.


NAME		unit-memory-available
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Memory Available
SNMP NAME	ncdSysMemAvail
SNMP PATH	ncdSystem 2
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The amount of RAM memory in bytes which is currently unallocated.


NAME		unit-memory-installed
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Memory Installed
SNMP NAME	ncdSysMemTotal
SNMP PATH	ncdSystem 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The total amount of RAM in bytes installed in the system.
		This does not include special purpose RAM such as video memory.


NAME		unit-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Unit Name
SNMP NAME	sysName
SNMP PATH	system 5
TYPE		STRING
DEFAULT		unknown
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the symbolic name of the NCD unit.


NAME		unit-optional-features
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Optional Features
SNMP NAME	ncdSysOptionalFeatures
SNMP PATH	ncdSystem 13
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The list of optional software features that
		are currently enabled for this unit.


NAME		unit-query-for-name-at-boot
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Unit and Licenses=>Query for Unit Name at Boot
SNMP NAME	ncdSysQueryNameAtBoot
SNMP PATH	ncdSystem 9
TYPE		CHOICE
CHOICES		{ none tcpip ncdnet }
DEFAULT		none
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies that the unit should send a reverse name
		request at boot to the name servers in an
		attempt to determine the unit's symbolic name.
		
		Choices:
		  None - Do not try reverse query.
		
		  TCPIP - Try reverse query to TCP/IP name servers,
		  if none are defined try the TCPIP boot server if
		  that is defined. Note TCPIP name server protocol
		  must be DNS for query to succeed. IEN-116 does not
		  support reverse queries.
		
		  NCDnet - Try reverse query to MOP boot server if
		  that is defined.


NAME		unit-snmp-system-object-id
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>SNMP System Object Id
SNMP NAME	sysObjectID
SNMP PATH	system 2
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The authoritative identification of the SNMP
		network management subsystem contained in the entity.


NAME		unit-tcpip-service-level
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>TCP/IP Service Level
SNMP NAME	sysServices
SNMP PATH	system 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A value which indicates the set of network services that
		this entity primarily offers. For NCD units, the value is
		always 72.
		
		The value is a sum.  This sum initially takes the
		value zero, Then, for each layer, L, in the range
		1 through 7, that this node performs transactions
		for, 2 raised to (L - 1) is added to the sum.  For
		example, a node which performs primarily routing
		functions would have a value of 4 (2^(3-1)).  In
		contrast, a node which is a host offering
		application services would have a value of 72
		(2^(4-1) + 2^(7-1)).  Note that in the context of
		the Internet suite of protocols, values should be
		calculated accordingly:
		
		  layer  functionality
			   1  physical (e.g., repeaters)
			   2  datalink/subnetwork (e.g., bridges)
			   3  internet (e.g., IP gateways)
			   4  end-to-end  (e.g., IP hosts)
			   7  applications (e.g., mail relays)
		
		For systems including OSI protocols, layers 5 and
		6 may also be counted.


NAME		unit-time-since-boot
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Time Since Boot
SNMP NAME	sysUpTime
SNMP PATH	system 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The time since the system was last booted (in seconds).


NAME		unit-version
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  Unit=>Version
SNMP NAME	sysDescr
SNMP PATH	system 1
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		A textual description of the entity.  This value
		includes the full name and version identification
		of the unit's hardware, and software.



GROUP xremote

NAME		xremote-additional-escape-chars
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  XRemote=>Additional Escape Chars
SNMP NAME	ncdXremoteEscTable
SNMP PATH	ncdXremote 18
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Although the XRemote transport protocol has a pre-defined list of
		characters that will be escaped, additional escape characters may be
		defined.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXremoteEscIndex
SNMP PATH	ncdXremoteEscTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the list of additional escape characters when using the
		XRemote transport protocol.


NAME		escape-character
SNMP NAME	ncdXremoteEscChar
SNMP PATH	ncdXremoteEscTable 2
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		A character which should not be sent in the clear across the serial
		line because it will be recognized as
a control character by intervening
		software/hardware.  If this character is embedded in the data stream,
		it will be translated into an escape sequence.


END TABLE ROW ENTRIES

NAME		xremote-allow-xremotetcp-connection
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  XRemote=>Allow XRemoteTCP Connection
SNMP NAME	ncdXremoteNetEnabled
SNMP PATH	ncdXremote 19
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		If true, an XRemote/TCP connection is permitted,
		subject to any host-based access control.


NAME		xremote-authorize-xremote-clients
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  XRemote=>Authorize XRemote Clients
SNMP NAME	ncdXremoteAuthEnabled
SNMP PATH	ncdXremote 17
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		If true, XRemote clients will be authenticated
		like any other X client.  If false, no
		authentication is performed and any XRemote
		client will be allowed access to the X terminal


NAME		xremote-data-compression-mode
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  XRemote=>Data Compression Mode
SNMP NAME	ncdXremoteCompressType
SNMP PATH	ncdXremote 16
TYPE		CHOICE
CHOICES		{ default lzw-14 lzw-12 none }
DEFAULT		default
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies how data in XRemote packets should be
		compressed.


NAME		xremote-next-receive-sequence-number
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Next Receive Sequence Number
SNMP NAME	ncdXremoteNxtReceiveSequenceNumber
SNMP PATH	ncdXremote 15
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The expected sequence number of the next received
		packet.


NAME		xremote-next-transmit-sequence-number
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Next Transmit Sequence Number
SNMP NAME	ncdXremoteTransSequenceNumber
SNMP PATH	ncdXremote 12
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The sequence number of the next packet to be
		transmitted.


NAME		xremote-oldest-unacknowledged-packet
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Oldest Unacknowledged Packet
SNMP NAME	ncdXremoteUnackPkt
SNMP PATH	ncdXremote 13
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The sequence number of the oldest transmitted packet
		for which an acknowledgment has not been received.


NAME		xremote-packet-round-trip-time
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packet Round Trip Time
SNMP NAME	ncdXremoteRoundTripTime
SNMP PATH	ncdXremote 9
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The current approximation of the amount of time (in
		milliseconds) from when a packet is sent until the
		corresponding acknowledgment is received.  The round
		trip time is used to compute the time-out length.


NAME		xremote-packet-transmission-errors
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packet Transmission Errors
SNMP NAME	ncdXremotePktTransErrors
SNMP PATH	ncdXremote 4
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of errors encountered while trying to
		transmit a packet.


NAME		xremote-packets-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packets Received
SNMP NAME	ncdXremotePktsReceived
SNMP PATH	ncdXremote 6
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of XRemote packets received.


NAME		xremote-packets-received-out-of-sequence
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packets Received Out of Sequence
SNMP NAME	ncdXremotePktsOutOfSequence
SNMP PATH	ncdXremote 8
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of XRemote packets received with a bad
		sequence number.


NAME		xremote-packets-retransmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packets Retransmitted
SNMP NAME	ncdXremotePktsRetrans
SNMP PATH	ncdXremote 5
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of XRemote packets that have been
		retransmitted.


NAME		xremote-packets-transmitted
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packets Transmitted
SNMP NAME	ncdXremotePktsTransmitted
SNMP PATH	ncdXremote 3
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of XRemote packets that have been
		transmitted, including retransmitted packets.


NAME		xremote-packets-with-errors-received
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Packets with Errors Received
SNMP NAME	ncdXremotePktsWithErrorsReceived
SNMP PATH	ncdXremote 7
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of XRemote packets received in error.


NAME		xremote-receive-window-size
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Receive Window Size
SNMP NAME	ncdXremoteReceiveWinSize
SNMP PATH	ncdXremote 14
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of packets that may be legally received
		from the remote host without an acknowledgment
		being sent.


NAME		xremote-state
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>State
SNMP NAME	ncdXremoteState
SNMP PATH	ncdXremote 2
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The state of the XRemote connection.


NAME		xremote-tcp-port
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  XRemote=>TCP Port
SNMP NAME	ncdXremoteListenPort
SNMP PATH	ncdXremote 20
TYPE		INTEGER
MIN		1024
DEFAULT		5900
MAX		65535
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the TCP port number on which the NCD unit
		listens for XRemote connections.


NAME		xremote-time-out-length
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Time-out Length
SNMP NAME	ncdXremoteTimeOut
SNMP PATH	ncdXremote 10
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The current time-out length (in milliseconds).
		Packets which are not acknowledged within the
		time-out period are retransmitted.


NAME		xremote-transmit-window-size
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>Transmit Window Size
SNMP NAME	ncdXremoteTransWinSize
SNMP PATH	ncdXremote 11
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		The number of packets that may be transmitted
		before an acknowledgment from the remote host is
		required.


NAME		xremote-xremote-version
HIDEBOX		Console=>Statistics=>Show Statistics=>
		  XRemote=>XRemote version
SNMP NAME	ncdXremoteVersion
SNMP PATH	ncdXremote 1
TYPE		INTEGER
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Revision level of the XRemote protocol being used.



GROUP xserver

NAME		xserver-access-control-enabled
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Enable X Access Control
SNMP NAME	ncdAccessAccessEnabled
SNMP PATH	ncdAccess 3
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies whether xhost-style access control
		is on or off for client connections.


NAME		xserver-access-control-enabled-default
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>Default for Enable X Access Control
SNMP NAME	ncdAccessDfltAccessEnabled
SNMP PATH	ncdAccess 2
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		Specifies whether xhost-style access control
		is on or off by default for client connections.


NAME		xserver-access-control-list
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Access Control=>X Access Control List
SNMP NAME	ncdAccessAccessControlTable
SNMP PATH	ncdAccess 4
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the host access control list for the X server.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdAccessACTIndex
SNMP PATH	ncdAccessAccessControlTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the X Access Control List


NAME		host
SNMP NAME	ncdAccessACTAddress
SNMP PATH	ncdAccessAccessControlTable 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the name of the host that is
		granted access to make connections
		to the server.


NAME		family
SNMP NAME	ncdAccessACTFamily
SNMP PATH	ncdAccessAccessControlTable 3
TYPE		CHOICE
CHOICES		{ tcpip ncdnet vms-decwindows }
DEFAULT		tcpip
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The access control family to which
		this entry applies.


END TABLE ROW ENTRIES

NAME		xserver-arc-cache-max-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Arc Cache Maximum Size
SNMP NAME	ncdXserverArcCacheSize
SNMP PATH	ncdXserver 20
TYPE		INTEGER
MIN		0
DEFAULT		524288
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of memory (in bytes)
		that can be used for arc caching. If the arc cache
		memory is needed to satisfy an X client request, the
		arc cache may be flushed.


NAME		xserver-black-pixel
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Black Pixel
SNMP NAME	ncdXserverXBlackPixel
SNMP PATH	ncdXserver 24
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		255
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		specifies the pixel to be reported as BlackPixel


NAME		xserver-default-colormap
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Default Colormap
SNMP NAME	ncdXserverColormapTable
SNMP PATH	ncdXserver 23
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		specifies the initial contents of the default
		colormap


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverCTIndex
SNMP PATH	ncdXserverColormapTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Default Colormap Table


NAME		pixel
SNMP NAME	ncdXserverCTPixel
SNMP PATH	ncdXserverColormapTable 2
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		255
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		TBD


NAME		rgb
SNMP NAME	ncdXserverCTRgb
SNMP PATH	ncdXserverColormapTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		TBD


NAME		read-only
SNMP NAME	ncdXserverCTReadOnly
SNMP PATH	ncdXserverColormapTable 4
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		TBD


END TABLE ROW ENTRIES

NAME		xserver-default-font
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Default Font
SNMP NAME	ncdXserverDefaultFont
SNMP PATH	ncdXserver 7
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		Specifies the X server's default font.


NAME		xserver-default-font-path
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Default Font Path
SNMP NAME	ncdXserverDefaultFontPathTable
SNMP PATH	ncdXserver 6
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default set of directories where the unit
		should look for fonts. The current X server font path is
		reset to this value on session reset.
		
		Special values are:
		  'built-ins' which refers to fonts built
		  into the NCD server.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverFontPathTableIndex
SNMP PATH	ncdXserverDefaultFontPathTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the default font path entry table


NAME		font-path-entry
SNMP NAME	ncdXserverFontPathTableEntry
SNMP PATH	ncdXserverDefaultFontPathTable 2
TYPE		STRING
DEFAULT		built-ins
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		Specifies the default font path directories set
		at server reset


END TABLE ROW ENTRIES

NAME		xserver-default-visual
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Default Visual
SNMP NAME	ncdXserverXDefaultVisual
SNMP PATH	ncdXserver 22
TYPE		CHOICE
CHOICES		{ static-gray gray-scale static-color pseudo-color true-color direct-color }
DEFAULT		static-gray
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		specifies the X server's default visual


NAME		xserver-disabled-extensions
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Disabled X Extensions
SNMP NAME	ncdXserverXDisabledExt
SNMP PATH	ncdXserver 17
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies the extensions that should not be made available


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverDisExtTableIndex
SNMP PATH	ncdXserverXDisabledExt 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the disabled X extensions table


NAME		extension-name
SNMP NAME	ncdXserverDisExtTableName
SNMP PATH	ncdXserverXDisabledExt 2
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a disabled extension


END TABLE ROW ENTRIES

NAME		xserver-enable-local-dead-key-processing
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Local Dead Key Support
SNMP NAME	ncdXserverDeadKeySupport
SNMP PATH	ncdXserver 4
TYPE		BOOL
DEFAULT		true
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Allows some keyboards to use local
		dead key processing


NAME		xserver-font-alias-file-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Font Alias File Name
SNMP NAME	ncdXserverFontAliasFileName
SNMP PATH	ncdXserver 11
TYPE		STRING
DEFAULT		fonts.alias
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file name to use for the font aliases.


NAME		xserver-font-cache-max-size
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Font Cache Maximum Size
SNMP NAME	ncdXserverFontCacheSize
SNMP PATH	ncdXserver 8
TYPE		INTEGER
MIN		0
DEFAULT		100000
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum amount of memory (in bytes)
		that can be used for font caching. If the font cache
		memory is needed to satisfy an X client request, the
		font cache may be flushed.


NAME		xserver-font-directory-file-name
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Font Directory File Name
SNMP NAME	ncdXserverFontDirFileName
SNMP PATH	ncdXserver 10
TYPE		STRING
DEFAULT		fonts.dir
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file name to use for the font directory.


NAME		xserver-font-path-alias-table
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Font Name Table
SNMP NAME	ncdXserverFontPathAliasTable
SNMP PATH	ncdXserver 12
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a symbolic mapping between user-specified
		strings and font path names.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverAliasTableIndex
SNMP PATH	ncdXserverFontPathAliasTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the default font path alias table


NAME		font-path-alias
SNMP NAME	ncdXserverAliasTableAlias
SNMP PATH	ncdXserverFontPathAliasTable 2
TYPE		STRING
DEFAULT		100dpi
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies a font path aliases for the given value


NAME		font-path-value
SNMP NAME	ncdXserverAliasTableValue
SNMP PATH	ncdXserverFontPathAliasTable 3
TYPE		STRING
DEFAULT		/usr/lib/X11/ncd/fonts/pcf/100dpi/
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the value for the given font alias
		 correspondence


END TABLE ROW ENTRIES

NAME		xserver-fontserver-open-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Open Timeout
SNMP NAME	ncdXserverFontserverOpenTimeout
SNMP PATH	ncdXserver 15
TYPE		INTEGER
MIN		0
DEFAULT		30
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to attempt to establish
		a connection to a font server before declaring an error
		situation.


NAME		xserver-fontserver-read-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Read Timeout
SNMP NAME	ncdXserverFontserverReadTimeout
SNMP PATH	ncdXserver 14
TYPE		INTEGER
MIN		0
DEFAULT		20
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the amount of time (in seconds) to attempt
		to read information from a font server before declaring
		an error situation.


NAME		xserver-fontserver-reopen-timeout
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Reopen Timeout
SNMP NAME	ncdXserverFontserverReopenTimeout
SNMP PATH	ncdXserver 16
TYPE		INTEGER
MIN		0
DEFAULT		10
MAX		100
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the timeout (in seconds) before failing
		to reopen the font server connection.


NAME		xserver-fontserver-retry-attempts
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Retry Attempts
SNMP NAME	ncdXserverFontserverRetryAttempts
SNMP PATH	ncdXserver 13
TYPE		INTEGER
MIN		0
DEFAULT		5
MAX		25
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of times to retry a font server
		request before declaring an error situation.


NAME		xserver-initial-x-resources
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Initial X Resources
SNMP NAME	ncdXserverInitialXResources
SNMP PATH	ncdXserver 19
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the initial resources of the RESOURCE_MANAGER
		root window property. Resources listed in this parameter
		are stored in the X server, where they are accessible by
		X clients.


NAME		xserver-input-extension-device
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Input Extension Device
SNMP NAME	ncdXserverInputExtensionDevice
SNMP PATH	ncdXserver 26
TYPE		CHOICE
CHOICES		{ tablet 3d-mouse touchscreen }
DEFAULT		tablet
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specify which input extension device is
		attached to serial port.


NAME		xserver-keyboard-narrow-keysym-tables
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Narrow Keysym Tables
SNMP NAME	ncdXserverNarrowKeyTable
SNMP PATH	ncdXserver 3
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		NO
DESCRIPTION
		Specifies whether to use R3 2-entry keysym tables
		instead of R4-style 4-entry keysym tables


NAME		xserver-keyboard-type
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Keyboard Type
SNMP NAME	ncdXserverCurrentKeyboard
SNMP PATH	ncdXserver 1
TYPE		CHOICE
CHOICES		{  }
DEFAULT		
PERMISSION	READ-WRITE
EFFECT		AT_BOOT
NVRAM		YES
DESCRIPTION
		Specifies the type of keyboard in use.
		
		NOTE: Choices depend on attached keyboard.


NAME		xserver-keyboard-type-choices
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Keyboard Type Choices
SNMP NAME	ncdXserverKeyboardTypeChoices
SNMP PATH	ncdXserver 2
TYPE		TABLE
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies the list of currently allowed choices
		for the type of keyboard in use.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverKeyboardChoiceIndex
SNMP PATH	ncdXserverKeyboardTypeChoices 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the keyboard choice table


NAME		choice
SNMP NAME	ncdXserverCurrentKeyboardChoice
SNMP PATH	ncdXserverKeyboardTypeChoices 2
TYPE		STRING
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Specifies an available choice for the type
		of the current keyboard in use.


END TABLE ROW ENTRIES

NAME		xserver-keysym-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Keysym File
SNMP NAME	ncdXserverKeysymDBPath
SNMP PATH	ncdXserver 27
TYPE		STRING
DEFAULT		/usr/lib/X11/ncd/XKeysymDB
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file name of the keysym database
		used by local clients.


NAME		xserver-mouse-buttons
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Mouse Buttons
SNMP NAME	ncdXserverMouseButtons
SNMP PATH	ncdXserver 5
TYPE		CHOICE
CHOICES		{ auto-detect 2 }
DEFAULT		auto-detect
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the number of buttons on the mouse
		attached to the unit. The choice 'Auto' allows
		the unit to attempt to automatically determine
		the number of buttons. Note that the choice '2'
		is only needed with a Microsoft mouse.
		With all other mice the number of buttons is
		automatically detected.


NAME		xserver-retain-font-path
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Fonts=>Retain Font Path Across Sessions
SNMP NAME	ncdXserverRetainFonts
SNMP PATH	ncdXserver 9
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the X server should retain the font path
		the last client disconnects from the server, and it
		undergoes a session reset.


NAME		xserver-retain-x-settings
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>Retain X Settings Across Sessions
SNMP NAME	ncdXserverXServerRetainSettings
SNMP PATH	ncdXserver 18
TYPE		BOOL
DEFAULT		false
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies that the X server should retain the settings
		of the resource database, keyboard, mouse, and screen
		saver settings when the last client disconnects from
		the server, and it undergoes a session reset.


NAME		xserver-rgb-file
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>RGB File
SNMP NAME	ncdXserverRgbPath
SNMP PATH	ncdXserver 21
TYPE		STRING
DEFAULT		/usr/lib/X11/ncd/rgb.txt
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the file name of the color database.


NAME		xserver-touchscreen-calibration-limits
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  Input Devices=>Touchscreen Calibration Limits
SNMP NAME	ncdXServerTouchscreenCalibrationLimitsTable
SNMP PATH	ncdXserver 27
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Touchscreen calibration limits -- Lower Left( x,y), Upper Right (x,y)


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncdXserverTouchscreenCalibrationLimitsIndex
SNMP PATH	ncdXServerTouchscreenCalibrationLimitsTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Touchscreen Calibration Limits List


NAME		x-min
SNMP NAME	ncdXserverTouchscreenCalibrationLimitsXMin
SNMP PATH	ncdXServerTouchscreenCalibrationLimitsTable 2
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the minimum touchscreen x coordinate which
		is in the active area of the screen


NAME		y-min
SNMP NAME	ncdXserverTouchscreenCalibrationLimitsYMin
SNMP PATH	ncdXServerTouchscreenCalibrationLimitsTable 3
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the minimum touchscreen y coordinate which
		is in the active area of the screen


NAME		x-max
SNMP NAME	ncdXserverTouchscreenCalibrationLimitsXMax
SNMP PATH	ncdXServerTouchscreenCalibrationLimitsTable 4
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum touchscreen x coordinate which
		is in the active area of the screen


NAME		y-max
SNMP NAME	ncdXserverTouchscreenCalibrationLimitsYMax
SNMP PATH	ncdXServerTouchscreenCalibrationLimitsTable 5
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		4294967295
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the maximum touchscreen y coordinate which
		is in the active area of the screen


END TABLE ROW ENTRIES

NAME		xserver-white-pixel
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  X and Graphics=>White Pixel
SNMP NAME	ncdXserverXWhitePixel
SNMP PATH	ncdXserver 25
TYPE		INTEGER
MIN		0
DEFAULT		0
MAX		255
PERMISSION	READ-WRITE
EFFECT		AT_SESSION_STARTUP
NVRAM		NO
DESCRIPTION
		specifies the pixel to be reported as WhitePixel



GROUP ncd3270

NAME		ncd3270-default-hosts
HIDEBOX		Console=>Setup=>Change Setup Parameters=>
		  3270 Terminal Emulation=>Default Hosts
SNMP NAME	ncd3270DfltConnectionTable
SNMP PATH	ncd3270 1
TYPE		TABLE
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		Specifies the default list of hosts to present
		to the user in the terminal chooser.


BEGIN TABLE ROW ENTRIES

NAME		index
SNMP NAME	ncd3270DCTIndex
SNMP PATH	ncd3270DfltConnectionTable 1
TYPE		INTEGER
VIEW		SNMP ONLY
MIN		0
MAX		4294967295
PERMISSION	READ-ONLY
NVRAM		NO
DESCRIPTION
		Index into the Default Hosts table for NCD3270


NAME		protocol
SNMP NAME	ncd3270DCTProtocol
SNMP PATH	ncd3270DfltConnectionTable 2
TYPE		CHOICE
CHOICES		{ telnet }
DEFAULT		telnet
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The protocol to use.


NAME		host
SNMP NAME	ncdTermDCTHost
SNMP PATH	ncd3270DfltConnectionTable 3
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The name of the terminal host.


NAME		port
SNMP NAME	ncdTermDCTPort
SNMP PATH	ncd3270DfltConnectionTable 4
TYPE		STRING
DEFAULT		23
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The port number to use.


NAME		model
SNMP NAME	ncd3270DCTModel
SNMP PATH	ncd3270DfltConnectionTable 5
TYPE		CHOICE
CHOICES		{ model-2 model-3 model-4 model-5 }
DEFAULT		model-2
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		The model to use.


NAME		description
SNMP NAME	ncdTermDCTDescription
SNMP PATH	ncd3270DfltConnectionTable 6
TYPE		STRING
DEFAULT		nil
PERMISSION	READ-WRITE
EFFECT		IMMEDIATE
NVRAM		NO
DESCRIPTION
		A description of the host.


END TABLE ROW ENTRIES