## Slide 1: Interaction of gamma rays with matter
total absorption coefficient: μ/ρ [cm2/g]
Aluminum
Lead
i=1 photoelectric effect
i=2 Compton scattering
i=3 pair production

## Slide 2: Mass dependence of X-ray absorption
For X-ray radiation the photoelectric effect is the most important interaction.
Lead absorbs more than Beryllium!
82Pb serves as shielding for X-ray and γ-ray radiation; lead vests are used by medical staff people who are exposed to X-ray radiation. Co-sources are transported in thick lead container.
On the contrary:
4Be is often used as windows in X-ray tubes to allow for almost undisturbed transmission of X-ray radiation.

## Slide 3: Mass dependence μ/ρ of X-ray absorption
wave length dependence for Pt as absorber
element number dependence for λ=0.1 nm or 12.4 keV

## Slide 4: X-ray image shows the effect of different absorptions
Bones absorb more radiation as tissues because of their higher 20Ca content

## Slide 5: Interaction of gamma rays with matter

## Slide 6: Interaction of gamma rays with matter
Photo effect:
Absorption of a photon by a bound electron and conversion of the γ-energy in potential and kinetical energy of the ejected electron.
(Nucleus preserves the momentum conservation.)

## Slide 7: Interaction of gamma rays with matter
Compton scattering:
Elastic scattering of a γ-ray on a free electron. A fraction of the γ-ray energy is transferred to the Compton electron. The wave length of the scattered γ-ray is increased: λ‘ > λ.
Maximum energy of the
scattered electron:
Energy of the scattered
γ-photon:
Special case for E>>mec2:
γ-ray energy after 1800 scatter
is approximately
Gap between the incoming γ-ray and the maximum electron energy.

## Slide 8: Interaction of gamma rays with matter
σCompton
Compton scattering:
Elastic scattering of a γ-ray on a free electron. A fraction of the γ-ray energy is transferred to the Compton electron. The wave length of the scattered γ-ray is increased: λ‘ > λ.

## Slide 9: Interaction of gamma rays with matter
Compton scattering:
Elastic scattering of a γ-ray on a free electron.
The angle dependence is expressed by the
Klein-Nishina-Formula:
As shown in the plot forward scattering (θ small) is dominant for Eγ>100 keV.
Angular distribution:
Intensity as a function of θ:
MeV
r0=2.818 fm

## Slide 10: Interaction of gamma rays with matter
Pair production:
If γ-ray energy is >> 2m0c2 (electron rest mass 511 keV), a positron-electron pair can be formed in the strong Coulomb field of a nucleus. This pair carries the γ-ray energy minus 2m0c2.
Pair production for Eγ>2mec2=1.022MeV
γ-ray > 1 MeV
magnetic field
γ’s
e-
picture of a bubble chamber

## Slide 11: Gamma-ray interaction cross section
All three interaction (photo effect, Compton scattering and pair production) lead to an attenuation of the γ-ray or X-ray radiation when passing through matter. The particular contribution depends on the γ-ray energy:
The absorption attenuates the intensity, but the energy and the frequency of the γ-ray and X-ray radiation is preserved!
Photo effect: ~Z4-5, Eγ-3.5
Compton: ~Z, Eγ-1
Pair: ~Z2, increases with Eγ

## Slide 12: Gamma-ray spectrum of a radioactive decay
γ1
γ2
CE γ2
SE γ2
DE γ2
511 keV
BSc
Pb X-ray
γ1+γ2
Pb-Box