## Slide 1: Outline: Transmutation for Nuclear Waste Yacine Kadi
Lecturer: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de
web-page: https://web-docs.gsi.de/~wolle/ and click on
The problem of nuclear waste
Nuclear reactor
Transmutation and incineration
Accelerator Driven System ADS

## Slide 2: The basic process is nuclear transmutation
1919 Rutherford 210Po accelerator!
1940 E.O. Lawrence/USA and W.N. Semenov/USSR proposed to use a particle accelerator
as a neutron source
1941 G. Seaborg produced the first μg of 239Pu with the Berkeley 60 inch cyclotron
1950 E.O. Lawrence proposed the Materials Testing Accelerator (MTA) at the Lawrence
Livermore Radiation Lab, to produce 239Pu from Oak Ridge depleted Uranium
1952 W.B. Lewis in Canada proposed to use an accelerator to produce 233U from Thorium
for CANDU reactors (electro-breeder concept)
MTA and Lewis‘ projects dropped or slowed down when
a) rich Uranium deposits were discovered in USA, and
b) it was realized that it required several hundred mA of
beam intensity, hundred of MW to produce the beam

## Slide 3: What is the nuclear waste transmutation
To transmute means to convert one element to another and by extension one isotope to another
The main physical process to perform useful transmutation is nuclear fission. One example of transmutation by fission can be:
Sometimes one or several captures and decays must take place before fission can perform the useful transmutation:
n
n+241Pu
242Am
242Cm

## Slide 4: Characteristic properties of nuclear fission

## Slide 5: Primordial heavy nuclei
232Th: Z=90, N=142
234U: Z=92, N=142 (0.0055%)
235U: Z=92, N=143 (0.72%)
238U: Z=92, N=146 (99.2745%)
excitation by thermal neutrons
Only nuclei with odd neutron number fission after capture of thermal neutrons.
Nuclei with even neutron number are fertile.
(By capture of thermal neutrons, a nucleus with odd neutron number is formed.)
The only natural nuclear fuel for conventional fission reactors is 235U.

## Slide 6: Absorption- and fission cross sections for neutrons
We start with thermalized neutrons,
η is the average number of fission neutrons per thermalized neutron.
For 235U: σf = 584 b and σa = 97 b, <ν>=2.4
For 238U: σf = 0 b and σa = 2.1 b
Effective value of η = 1.3 for natural Uranium is too small for chain reaction.
→ 235U has to be enriched to 3% (η=1.8)
0.0253 eV
thermalized

## Slide 7: Nuclear reactor
Controlled chain reaction
"Fuel" 235U enriched from 0,72% to 3,5%.
Fission → 2.2 to 3 neutrons,
exactly one of those induces another fission (criticality = 1)
Control of reactor possible due to delayed neutrons.
Variation of criticality by rods, absorbing neutrons.

## Slide 8: Problem of nuclear waste
Which kind of waste?
Fission products
Plutonium —
Dangerous waste or fuel?
Minor actinides
The time scale
Possible solutions
Deposition — safe?, accepted?
Transmutation and incineration by nuclear reactions —
"Cleaning up" in reasonable time?

## Slide 9: Nuclear reactions in the reactor
Fission:
neutron-breeding:
129I (15.7·106 y)
107Pd (6.5·106 y)
135Cs (2·106 y)
93Zr (1.5·106 y) …
Pu, Am, Cm, Np isotopes

## Slide 10: List of the reaction products
235U: Fuel (total reserve for ≈ 200 years)
Fission products:
Isotope | lifetime | 900 MW, 1 year
79Se | 70000 years | 0.1 kg
93Zr | 1.5 million years | 15.5 kg
99Tc | 210000 years | 17.7 kg
107Pd | 6.5 million years | 4.4 kg
126Sn | 10000 years | 0.44 kg
129I | 15.7 million years | 3.9 kg
135Cs | 2 million years | 7.7 kg
239Pu: Fuel or dangerous waste?
Isotope | lifetime | 900 MW, 1 year
239Pu | 24119 years | 123.1 kg
Other actinides produced by breeding: many not fissile by neutrons
Balance: After a few years, the fuel is consumed.
Problem: Increased neutron capture → poisoning

## Slide 11: Variation in radiotoxicity over time

## Slide 12: The spallation process
Several nuclear reactions are capable of producing neutrons

## Slide 13: Transmutation of radioactive waste
By spallation neutrons
high energy consumption
By an hybrid reactor (accelerator driven system ADS)?
A subcritical reactor with additional neutrons produced by 1 GeV protons.

## Slide 14: Transmutation with an accelerator driven system (ADS)
Accelerator
Spallation Target
Sub-critical Core
accelerator | 
particles | protons
energy | 600 MeV
current | 2.4-4 mA
mode | CW
MTBF | > 250 h
reactor | 
power | ~85 MWth
keff | 0.95
spectrum | fast (flexible)
fuel | 30-35% Pu MOX
coolant | LBE (PbBi)
target | 
main reaction | spallation
output | 2·1017 n/s
material | LBE (PbBi coolant)
power | 2.4 MW

## Slide 15: Critical versus Sub-critical Systems
effective neutron multiplication factor
self-sustained process: k=1
(if k<1 the reactor stops)
(if k>1 the reactor is super-critical
externally driven process: k<1 (k=0.98)
G0=2.7 for Pb
EA ≡ energy amplifier

## Slide 16: Energy gain in ADS systems

## Slide 17: Neutron production
Neutrons are produced through the spallation process on heavy nuclei
at 1 GeV, each proton produce 32 neutrons by spallation
Spallation: A nuclear process in which a high energy proton excites a neutron rich nucleus which decays sending out neutrons (and other particles)
The average energy deposited on the target, about 50 MeV/A, is lower than for deuteron induced nuclear processes.
Neutrons with a broad energy spectrum peaked at 1 MeV

## Slide 18: Guidelines for ADS parameters choice

## Slide 19: Physics of subcritical systems

## Slide 20: Guidelines for ADS parameters choice

## Slide 21: Myrrha project

## Slide 22: Myrrha project

## Slide 23: The Hybrid System (ADS)
Principle:
Slightly under-critical
Controllable by spallation neutrons,
produced by 1 GeV protons
Advantages:
Can be operated with 232Th → 233U
232Th reserves sufficient for 21000 years
Supports some ´poisoning´
Can transmute or incinerate nuclear waste
Is insensitive to some variation of the criticality during long operation
Long operation of fuel rods
Problems:
Nuclear reactions up to 1 GeV must be known
Yield of spallation neutrons
Production of radioactive nuclei by spallation
Material damages due to irradiation

## Slide 24: The Hybrid System (ADS)
Thorium is a major asset to minimize waste production
It takes 7 neutron captures to go from 232Th to 239Pu
Pu equilibrium concentration ~ 10-4 as opposed to 15% in U-Pu system

## Slide 25: Research Program at GSI for Transmutation and Incineration of radioactive nuclear waste
Precision Measurements of isotopic yields
197Au (800 A MeV) + 1H
208Pb (1 A GeV) + 1H
208Pb (1 A GeV) + 2H
208Pb (500 A MeV) + 1H
238U (1 A GeV) + 1H
238U (1 A GeV) + 2H
238U (1 A GeV) + 208Pb
Development of nuclear-reaction models

## Slide 26: Proton- versus heavy-ion induced reactions
Proton- and heavy-ion induced reactions give very similar isotope distribution:
28 GeV p + 238U
8 GeV 48Ca+Be
Na
Target fragmentation: GeV p + Atarget → A
Projectile fragmentation: GeV/u Aproj + p → A
are equivalent

## Slide 27: Identification Pattern
208Pb + 1H, 1GeV/A
T. Enqvist et al., Nucl. Phys. A686 (2001), 481

## Slide 28: Production cross sections
F. Rejmund et al. NPA 683 (2001) 540
J. Benlliure et al. NPA 683 (2001) 513
T. Enqvist et al. NPA 686 (2001) 481
T. Enqvist et al. NPA 703 (2002) 435
M. Bernas et al. to be published
PhD: B. Mustapha, E. Casarejos, J. Taieb,
M.V. Ricciardi, J. Pereira